## Slide 1: PV198 – One-chip Controllers LCD Display

## Slide 2: Content
LCD Display usage
LCD 1602A
Driver
Application

## Slide 3: LCD Display usage
Printers
Routers
Industrial equipment
…

## Slide 4: LCD 1602A – Overview
LCD 1602A display driver
  HD44780U Display Controller – Datasheet
  4 bits connection
  Connection via GPIO pins (7 outputs)

## Slide 5: LCD 1602A – Message

## Slide 6: LCD 1602A – Scheme

## Slide 7: LCD 1602A – Scheme
MK66FN2M0 MCU
FRDM-K66F board
GND
5V
DAC0_OUT
LCD_RS
LCD_RW
LCD_E
LCD_DB4
LCD_DB5
LCD_DB6
LCD_DB7
LCD 1602A
HD44780U Display Controller
1
2
3
4
5
6
7
8
9
10
11
12
13
14
VSS
VCC
VEE
RS
R/W
E
DB0
DB1
DB2
DB3
DB4
DB5
DB6
DB7
J3_12 – GND
J3_10 – P5V_USB
J4_11 – DAC0_OUT
J1_14 – PTC2
J1_12 – PTC5
J1_10 – PTC12
J1_8 – PTC8
J1_6 – PTC16
J1_4 – PTC4
J1_2 – PTC3
We will use DAC output instead of potentiometer

## Slide 8: LCD 1602A – Driver
Support of the 4-bit communication initialization
SysTick timer usage for delays
Basic command and data transfer functions
Does not read busy flag – uses delays instead

## Slide 9: LCD 1602A – Driver Interface
The LCD driver requires to define the following identifiers in the Pins tool for GPIO output pins:
  LCD_RS
  LCD_RW
  LCD_E
  LCD_DB4
  LCD_DB5
  LCD_DB6
  LCD_DB7

## Slide 10: LCD 1602A – Driver Interface
The following LCD driver functions are provided:
  void LCD_4BitsInit(uint32_t systick_clk_freq, bool cursor_on, bool cursor_blinking)
  void LCD_Clear()
  void LCD_Home()
  void LCD_SetPosition(uint8_t x, uint8_t y)
  void LCD_PutChar(uint8_t character)
  void LCD_Print(char s[])
  void LCD_SendCommand(uint8_t command)
  void LCD_SendData(uint8_t data, MessageType_t messageType)
SysTick timer is used for implementation of delay
Our task is to implement this function

## Slide 11: Application
LCD driver initialization
RTC peripheral initialization
Real date and time display demo

## Slide 12: Application
Initialization sequence of the LCD driver
  BOARD_InitPins();
  LCD_4BitsInit(BOARD_BOOTCLOCKRUN_CORE_CLOCK, false, false);
Runtime usage of the driver (example):
  LCD_SetPosition(0, 0);
  LCD_Print(“a string”);
Initialization of GPIO pins (wired interface) with the generated code from the Pins tools
Initialization of the LCD driver (using core clock frequency and without cursor)
Displaying “a string” on the LCD screen at position 0,0 (the first column and first line)

## Slide 13: Application
Implement function according to message format picture:
  void LCD_SendData(uint8_t data, MessageType_t messageType)
Bonus:
  Display floating text on the display

## Slide 14: Homework
Use LCD display with any project created before (accelerometer, temperature sensor, …)