## Slide 1: PV198 – One-chip Controllers I2C

## Slide 2: NXPCUP
International competition with autonomous cars.
FI Team:
  Write email to 492926 to register (until 28.10.)
  You will get a task to solve
  Recruitment until 12.12. – we will pick the top students

## Slide 3: Content
What is I2C
What is it used for
How does it work
FRDM-K66F I2C
Accelerometer & Magnetometer
Application

## Slide 4: What is I2C
I2C – Inter-Integrated Circuit
Invented in 1982 by Philips Semiconductor (now NXP Semiconductors)

## Slide 5: What is it used for
Intra-board communication
Peripherals
Sensors

## Slide 6: How does it work
2 wires (Clock – SCL, Data – SDA) – pulled high
Multi-master & multi-slave
100 kbit/s – 5 Mbit/s
7-bit addressing / 10-bit addressing
Synchronous
Half-duplex

## Slide 7: How does it work – Scheme
https://learn.sparkfun.com/tutorials/i2c/all

## Slide 8: How does it work – Message
K66 Sub-Family Reference Manual, Figure 58-2.

## Slide 9: FRDM-K66F I2C
4 I2C modules
Address match wakeup in low power modes
SMBus support
Methods to use:
  BOARD_I2C_Receive
  BOARD_I2C_Send

## Slide 10: Accelerometer & Magnetometer
FXOS8700CQ – link
3-axis, linear accelerometer + 3-axis, magnetometer combined into a single package

## Slide 11: Accelerometer & Magnetometer
Connected to I2C bus and 2 GPIO signals
Freedom FRDM-K66F Development Platform User’s Guide, Table 6.

## Slide 12: Application – Template
startInitialization (check sensor ID, wake-up)
setupOrientationDetection (enable detection, interrupts, etc.) – Homework
finishInitialization (setup frequency, activate sensor)

## Slide 13: Application
Create an application that reads accelerometer output data registers
  Study the datasheet!
Print register values into console
Trap: Check configuration of pins and peripherals
Bonus:
Calculate tilt angle from received values

## Slide 14: Homework
Create an application that detects orientation of the board (the same way as mobile phones do)
Use the feature of the sensor – do not calculate it in the MCU from XYZ register values
Use interrupt from sensor
Print current orientation into console when orientation of the board changes

## Slide 15: Homework
Write your code into method setupOrientationDetection()
Link to Application note: AN4068