## Slide 1: Module 10: LAN Security Concepts
Instructor Materials
Switching, Routing and Wireless Essentials v7.0 (SRWE)
Notes: Cisco Networking Academy Program
Switching, Routing and Wireless Essentials v7.0 (SRWE)
Module 10: LAN Security Concepts

## Slide 2: Module 10: Activities
What activities are associated with this module?
Page # | Activity Type | Activity Name | Optional?
10.1.6 | Check Your Understanding | Endpoint Security | Recommended
10.2.7 | Check Your Understanding | Access Control | Recommended
10.3.4 | Check Your Understanding | Layer 2 Security Threats | Recommended
10.4.4 | Check Your Understanding | MAC Address Table Attacks | Recommended
10.5.1 | Video | VLAN and DHCP Attacks | Recommended
10.5.6 | Video | ARP Attacks, STP Attacks, and CDP Reconnaissance | Recommended
10.5.11 | Check Your Understanding | LAN Attacks | Recommended
Notes: 2

## Slide 3: Module Objectives
Module Title: LAN Security Concepts
Module Objective: Explain how vulnerabilities compromise LAN security
Topic Title | Topic Objective
Endpoint Security | Explain how to use endpoint security to mitigate attacks
Access Control | Explain how AAA and 802.1x are used to authenticate LAN endpoints and devices
Layer 2 Security Threats | Identify Layer 2 vulnerabilities
MAC Address Table Attack | Explain how a MAC address table attack compromised LAN security
LAN Attacks | Explain how LAN attacks compromise LAN security
Notes: 3
10- Introduction
10.0.2 – What will I learn in this module

## Slide 4: 10.1 Endpoint Security
Notes: 10 – LAN Security Concepts
10.1 – Endpoint Security

## Slide 5: Network Attacks Today
The news media commonly covers attacks on enterprise networks. Simply search the internet for “latest network attacks” to find up-to-date information on current attacks. Most likely, these attacks will involve one or more of the following:
  Distributed Denial of Service (DDoS) – This is a coordinated attack from many devices, called zombies, with the intention of degrading or halting public access to an organization’s website and resources.
  Data Breach – This is an attack in which an organization’s data servers or hosts are compromised to steal confidential information.
  Malware – This is an attack in which an organization’s hosts are infected with malicious software that cause a variety of problems. For example, ransomware such as WannaCry encrypts the data on a host and locks access to it until a ransom is paid.
Notes: 10 – LAN Security Concepts
10.1 – Endpoint Security
10.1.1 – Network Attacks Today

## Slide 6: Network Security Devices
Various network security devices are required to protect the network perimeter from outside access. These devices could include the following:
Virtual Private Network (VPN) enabled router - provides a secure connection to remote users across a public network and into the enterprise network. VPN services can be integrated into the firewall.
Next-Generation Firewall (NGFW) - provides stateful packet inspection, application visibility and control, a next-generation intrusion prevention system (NGIPS), advanced malware protection (AMP), and URL filtering.
Network Access Control (NAC) - includes authentication, authorization, and accounting (AAA) services. In larger enterprises, these services might be incorporated into an appliance that can manage access policies across a wide variety of users and device types. The Cisco Identity Services Engine (ISE) is an example of a NAC device.
Notes: 10 – LAN Security Concepts
10.1 – Endpoint Security
10.1.2 – Network Security Devices

## Slide 7: Dodatečné funkce mění firewall v UTM resp. NGFW
tunelování
translace adres
autentizace uživatelů
detekce průniků
blokace, restrikce a antivirový nástroj
podpora demilitarizovaného portu
vzdálené řízení nastavování
alarmy
kešování informací atd.
Notes:     Tunelování, tj. vytváření sítí VPN (Virtual Private Network).
    Translace adres - NAT (Network Address Translation), kdy všem adresám
    vnitřní LAN je přiřazena jedna nebo sada IP adres.
    Autentizace uživatelů přihlašovaných z vnější sítě.
    Detekce průniků, např. DoS (Denial of Service) Attack - útok, který si klade
    za cíl ne ukradnout nějakou informaci, ale vyřadit některý z prvků sítě z
    činnosti (realizací je např. Ping of Death, SYN Flood, LAND Attack, IP
    Spoofing, atd.). Testován byl např. široce používaný nástroj ”WinNuke”,
    který je určen k vyřazení vzdáleného PC. Známý DoS útok má název ”Smurf
    Attack” z listopadu roku 1997: útočník rozešle velké množství pingů
    s podvrženou adresou odesilatele, za kterou si vybere adresu počítače, na
    který chce útočit. Tyto počítače odpoví pakety ”ping reply” a vyhlédnutý
    počítač je těmito pakety zahlcen.
    Blokování prvků Javy a ActiveX. Zvláště prvky ActiveX mohou
    sloužit jako prostředky útoku.
    Podpora demilitarizovaného portu a jeho ochrana před útoky typu DoS.
    Vzdálené řízení, kdy řídicí příkazy jsou přenášeny v zašifrované podobě.
    Vzdálené nastavování konfigurace směrovačů.
    Vydávání varovných zpráv (alarmů).
    Detekce příznaků virů a odesílání podezřelých paketů ke zpracování
    antivirovým software na jiném počítači.
    Nástroje pro restrikci nežádoucích informací (odvádějící od pracovního
    výkonu atd.).
    Kešování užitečné informace.

## Slide 8: UTM (unified threat management) a NGFW (nextgen FW)
UTM byly původně firewally kategorie SMB rozšířené o funkce IDS/IPS, antimalwaru, antispamu a filtrování obsahu v jediném snadno spravovatelném zařízení. Nověji přidaly funkce, jako je VPN, vyvažování zátěže a prevence ztráty dat (DLP), a jsou stále častěji dodávány jako služba prostřednictvím cloudu.
NGFW kombinují tradiční filtrování portů a protokolů s funkcemi IDS/IPS a schopností detekovat provoz na aplikační vrstvě; postupem času přidali další funkce, jako je hloubková kontrola paketů a detekce malwaru.
Ochrana proti malwaru a virům, webový proxy a další, které existují v bráně firewall UTM, nejsou původní součástí architektury NGFW, protože tyto linie byly původně outsourcovány a odstraněny, což zajistilo bohaté stupně škálovatelnosti pro velká prostředí.

## Slide 9: Výrobci NGEW a UTM

## Slide 10: Obrana průmyslových zařízení pomocí zónové obrany
Speciální firewally (conduits) mají pomocí seznamů povolených příkazů zabránit přelévání problémů z jedné zóny do druhé. Řada od sebe oddělených zón umožňuje realizovat tzv. obranu v hloubce.
Typickým conduitem je např. Tofino Security Appliance (TSA).

## Slide 11: Příklad rozdělení řízení elektrárny do jednotlivých úrovní

## Slide 12: Endpoint Protection
Endpoints are hosts which commonly consist of laptops, desktops, servers, and IP phones, as well as employee-owned devices. Endpoints are particularly susceptible to malware-related attacks that originate through email or web browsing.
Endpoints have typically used traditional host-based security features, such as antivirus/antimalware, host-based firewalls, and host-based intrusion prevention systems (HIPSs).
Endpoints today are best protected by a combination of NAC, AMP software, an email security appliance (ESA), and a web security appliance (WSA).
Notes: 10 – LAN Security Concepts
10.1 – Endpoint Security
10.1.3 – Endpoint Protection

## Slide 13: CISCO Cognitive Threat Analytics (CTA), pak Cognitive Intelligence nakonec naintegrováno do Cisco Secure Endpoint (AMP for Endpoints)

## Slide 14: Hodnocení Cisco AMP https://www.trustradius.com/endpoint-security
Nejlépe hodnocené produkty nejsou od Cisco: Sophos Intercept X, FortiClient, Bitdefender GravityZone a Symantec Endpoint Security.

## Slide 15: Hodnocení u Gartnera https://www.gartner.com/reviews/market/endpoint-detection-and-response-solutions/vendor/cisco/product/cisco-amp-for-endpoints

## Slide 16: Nejlépe hodnocené starší produkty dle Gartnera

## Slide 17: Aktuální produkty EndPoint Security softwaru

## Slide 18: Cynet

## Slide 19: Přístup Cynetu
XDR Extension Detention and Response
Managed DR
klamání

## Slide 20: Ukázka playbooku (Plays v YAML formátu)
4 | hosts | {{ hosts }} | This key is an Ansible magic variable. It is needed to identify the target device on which this Play will run. The value of this is a Jinja template, which Change Automation will substitute at runtime based on the devices selected by the user via the UI or API.
5 | router_ip | {{ inventory_hostname }} | This key is a Cisco-defined variable needed for the Verb. The value is a Jinja template referencing an Ansible special variable.
6 | role | router_check_install_consistency | This is another Cisco check Verb. See the Verb Reference for details.
7 | role | router_op_dlm_node_lock | This is a Cisco action Verb. See the Verb Reference for details.

## Slide 21: Cisco Email Security Appliance
The Cisco ESA device is designed to monitor Simple Mail Transfer Protocol (SMTP). The Cisco ESA is constantly updated by real-time feeds from the Cisco Talos, which detects and correlates threats and solutions by using a worldwide database monitoring system. This threat intelligence data is pulled by the Cisco ESA every three to five minutes.
These are some of the functions of the Cisco ESA:
  Block known threats
  Remediate against stealth malware that evaded initial detection
  Discard emails with bad links
  Block access to newly infected sites.
  Encrypt content in outgoing email to prevent data loss.
Notes: 10 – LAN Security Concepts
10.1 – Endpoint Security
10.1.4 – Cisco Email Security Appliance

## Slide 22: Cisco Web Security Appliance
The Cisco Web Security Appliance (WSA) is a mitigation technology for web-based threats. It helps organizations address the challenges of securing and controlling web traffic.
The Cisco WSA combines advanced malware protection, application visibility and control, acceptable use policy controls, and reporting.
Cisco WSA provides complete control over how users access the internet. Certain features and applications, such as chat, messaging, video and audio, can be allowed, restricted with time and bandwidth limits, or blocked, according to the organization’s requirements.
The WSA can perform blacklisting of URLs, URL-filtering, malware scanning, URL categorization, Web application filtering, and encryption and decryption of web traffic.
Notes: 10 – LAN Security Concepts
10.1 – Endpoint Security
10.1.5 – Cisco Web Security Appliance
10.1.6 – Check Your Understanding – Endpoint Security

## Slide 23: Vlastnosti Endpoint Security Softwaru
Tradiční skenování koncových bodů a antivirové/antimalwarové funkce
Plánované nebo nepřetržité sledování souborů a připojených zařízení
Zamknutí či omezení přístupu ke koncovým bodům správcem
Omezení přístupu k různým webům a aplikacím
Integrovaný firewall
Konfigurace a kontroly souladu se zásadami
Automatizované aktualizace

## Slide 24: Tools for Incident Prevention and Detection
SIEM – Security Information and Event Management
  Software that collects and analyzes security alerts, logs and other real time and historical data from security devices on the network
DLP – Data Loss Prevention
  Stops sensitive data from being stolen or escaped from the network
  Designs to monitor and protect data in three different states
Cisco Identity Services Engine (Cisco ISE) and TrustSec
  Uses role-based access control policies
Notes: 4.3 – Cisco’s Approach to Cybersecurity
4.3.3 – Tools for Incident Prevention and Detection
4.3.3.1 - Tools for Incident Prevention and Detection

## Slide 25: Architektura Cisco TrustSec
kontrola přístupu založená na rolích
všechny ověřovací mechanizmy se sbíhají do jediného centrálního systému: zjednodušuje správu bezpečnostních politik
pomáhá udržovat integritu a diskrétnost dat po celou dobu jejich průchodu sítí: minimalizuje riziko úniku informací

## Slide 26: Cisco ISE 3395 Identity Services Engine

## Slide 27: Prohlížeč událostí na Windows

## Slide 28: V prohlížeči událostí hledáme pomocí filtru

## Slide 29: Syslog server
  Slouží pro sběr logů ze síťových a koncových zařízení.
  Typicky naslouchá na UDP portu 514.
  Hackeři mohou blokovat přenos dat, manipulovat s daty protokolu nebo manipulovat se softwarem, který vytváří a přenáší zprávy protokolu.
  1980 –> Syslog, 1998 –> Syslog-ng (podpora TLS a šifrování) , 2004 –> rsyslog (protokol RELP – Reliable Event Logging Protocol)
Notes: 11.1 Technologies and Protocols
11.1.1 – Monitoring Common Protocols
11.1.1.1 – Syslog and NTP

## Slide 30: Do sítě doplníme syslog server
R3(config)# logging 10.2.2.6
R3(config)# logging trap informational
R3(config)# logging source-interface loopback 0
R3(config)# logging on

## Slide 31: Úrovně chybových zpráv systému logování syslog
Nejvyšší úroveň
Nejnižší úroveň
Defaultní úroveň je 7 (debugging) – zprávy jsou posílány na konzolový port směrovače (line con0).

## Slide 32: Dostaneme záplavu výstupů (zde Kiwi)

## Slide 33: NetFlow
Umožňuje účtování síťového provozu, plánování sítě, zabezpečení, možnosti sledování odmítnutí služby a monitorování sítě.
Poskytuje informace o uživatelích a aplikacích sítě, dobách využití špiček a směrování provozu.
Shromažďuje metadata nebo data o toku, nikoli samotná data toku.
Notes: 11.2 Log Files
11.2.3 – Network Logs
11.2.3.2 - NetFlow

## Slide 34: Sledování toků ve Stealwatch

## Slide 35: ELK umí log management, ale ne korelační funkce atd.
Elastic Search – distribuovaný vyhledávací engine
Logstash – nástroj pro směrování zpráv
Kibana – HTML rozhraní pro zobrazování dat z Elastic Search

## Slide 36: SIEM: Zápisu logů je převeden do zápisu událostí
Precizace probíhají pomocí substitucí: Router.A=Network, Host.A=Mail, Host.B/Host.C=Portal. a přidáním bezpečnostní hodnoty události (Event Priority).
Agregace může být v SIEM volitelně provedena nejen nad událostmi, ale i nad „vytěženou informací“, jako např. na source_hostname, source_ip, target_hostname, target_ip, atp.
Korelace je pokročilejší agregace, neboť pracuje z různými formáty událostí mající stejnou kategorii děje = taxonomy.

## Slide 37: Příklad: Dragon (OEM IBM) - dashboard

## Slide 38: Virus Total

## Slide 39: Virus Total výsledek

## Slide 40: 10.2 Access Control
Notes: 10 – LAN Security Concepts
10.2 – Access Control

## Slide 41: Authentication with a Local Password
Many types of authentication can be performed on networking devices, and each method offers varying levels of security.
The simplest method of remote access authentication is to configure a login and password combination on console, vty lines, and aux ports.
SSH is a more secure form of remote access:
  It requires a username and a password.
  The username and password can be authenticated locally.
The local database method has some limitations:
  User accounts must be configured locally on each device which is not scalable.
  The method provides no fallback authentication method.
Notes: 10 – LAN Security Concepts
10.2 – Access Control
10.2.1 – Authentication with a Local Password

## Slide 42: AAA Components
AAA stands for Authentication, Authorization, and Accounting, and provides the primary framework to set up access control on a network device.
AAA is a way to control who is permitted to access a network (authenticate), what they can do while they are there (authorize), and to audit what actions they performed while accessing the network (accounting).
Notes: 10 – LAN Security Concepts
10.2 – Access Control
10.2.2 – AAA Components

## Slide 43: Authentication
Local and server-based are two common methods of implementing AAA authentication.
Local AAA Authentication:
Method stores usernames and passwords locally in a network device (e.g., Cisco router).
Users authenticate against the local database.
Local AAA is ideal for small networks.
Server-Based AAA Authentication:
With the server-based method, the router accesses a central AAA server.
The AAA server contains the usernames and password for all users.
The router uses either the Remote Authentication Dial-In User Service (RADIUS) or Terminal Access Controller Access Control System (TACACS+) protocols to communicate with the AAA server.
When there are multiple routers and switches, server-based AAA is more appropriate.
Notes: 10 – LAN Security Concepts
10.2 – Access Control
10.2.3 - Authentication

## Slide 44: Authorization
AAA authorization is automatic and does not require users to perform additional steps after authentication.
Authorization governs what users can and cannot do on the network after they are authenticated.
Authorization uses a set of attributes that describes the user’s access to the network. These attributes are used by the AAA server to determine privileges and restrictions for that user.
Notes: 10 – LAN Security Concepts
10.2 – Access Control
10.2.4 - Authorization

## Slide 45: Accounting
AAA accounting collects and reports usage data. This data can be used for such purposes as auditing or billing. The collected data might include the start and stop connection times, executed commands, number of packets, and number of bytes.
A primary use of accounting is to combine it with AAA authentication.
  The AAA server keeps a detailed log of exactly what the authenticated user does on the device, as shown in the figure. This includes all EXEC and configuration commands issued by the user.
  The log contains numerous data fields, including the username, the date and time, and the actual command that was entered by the user. This information is useful when troubleshooting devices. It also provides evidence for when individuals perform malicious acts.
Notes: 10 – LAN Security Concepts
10.2 – Access Control
10.2.5 - Accounting

## Slide 46: 802.1X
The IEEE 802.1X standard is a port-based access control and authentication protocol. This protocol restricts unauthorized workstations from connecting to a LAN through publicly accessible switch ports. The authentication server authenticates each workstation that is connected to a switch port before making available any services offered by the switch or the LAN.
With 802.1X port-based authentication, the devices in the network have specific roles:
  Client (Supplicant) - This is a device running 802.1X-compliant client software, which is available for wired or wireless devices.
  Switch (Authenticator) –The switch acts as an intermediary between the client and the authentication server. It requests identifying information from the client, verifies that information with the authentication server, and relays a response to the client. Another device that could act as authenticator is a wireless access point.
  Authentication server –The server validates the identity of the client and notifies the switch or wireless access point that the client is or is not authorized to access the LAN and switch services.
Notes: 10 – LAN Security Concepts
10.2 – Access Control
10.2.6 – 802.1X
10.2.7 – Check Your Understanding – Access Control

## Slide 47: Konkrétní útok pomocí yersinie
http://www.jay-miah.co.uk/vlan-hopping-concept-attack-example-and-prevention/

## Slide 48: 10.3 Layer 2 Security Threats
Notes: 10 – LAN Security Concepts
10.3 – Layer 2 Security Threats

## Slide 49: Layer 2 Vulnerabilities
Recall that the OSI reference model is divided into seven layers which work independently of each other. The figure shows the function of each layer and the core elements that can be exploited.
Network administrators routinely implement security solutions to protect the elements in Layer 3 up through Layer 7. They use VPNs, firewalls, and IPS devices to protect these elements. However, if Layer 2 is compromised, then all the layers above it are also affected. For example, if a threat actor with access to the internal network captured Layer 2 frames, then all the security implemented on the layers above would be useless. The threat actor could cause a lot of damage on the Layer 2 LAN networking infrastructure.
Notes: 10 – LAN Security Concepts
10.3 – Layer 2 Security Threats
10.3.1 - Layer 2 Vulnerabilities

## Slide 50: Switch Attack Categories
Security is only as strong as the weakest link in the system, and Layer 2 is considered to be that weak link. This is because LANs were traditionally under the administrative control of a single organization. We inherently trusted all persons and devices connected to our LAN. Today, with BYOD and more sophisticated attacks, our LANs have become more vulnerable to penetration.
Category | Examples
MAC Table Attacks | Includes MAC address flooding attacks.
VLAN Attacks | Includes VLAN hopping and VLAN double-tagging attacks. It also includes attacks between devices on a common VLAN.
DHCP Attacks | Includes DHCP starvation and DHCP spoofing attacks.
ARP Attacks | Includes ARP spoofing and ARP poisoning attacks.
Address Spoofing Attacks | Includes MAC address and IP address spoofing attacks.
STP Attacks | Includes Spanning Tree Protocol manipulation attacks.
Notes: 10 – LAN Security Concepts
10.3 – Layer 2 Security Threats
10.3.2 - Switch Attack Categories

## Slide 51: arpspoof v Kali
1. Kontrola defaultní brány: ip route
2. Oskenování sítě: netdiscover -r 192.168.1.0/24 -r … range
3. Útok: arpspoof -i eth0 -t 192.168.1.10 -r 192.168.1.1

## Slide 52: arp skener ve scapy
from scapy.all import *def arp_scan(ip): request = Ether(dst="ff:ff:ff:ff:ff:ff") / ARP(pdst=ip) ans, unans = srp(request, timeout=2, retry=1) result = [] for sent, received in ans: result.append({'IP': received.psrc, 'MAC': received.hwsrc}) return result

## Slide 53: Switch Attack Mitigation Techniques
Solution | Description
Port Security | Prevents many types of attacks including MAC address flooding attacks and DHCP starvation attacks.
DHCP Snooping | Prevents DHCP starvation and DHCP spoofing attacks.
Dynamic ARP Inspection (DAI) | Prevents ARP spoofing and ARP poisoning attacks.
IP Source Guard (IPSG) | Prevents MAC and IP address spoofing attacks.
These Layer 2 solutions will not be effective if the management protocols are not secured. The following strategies are recommended:
Always use secure variants of management protocols such as SSH, Secure Copy Protocol (SCP), Secure FTP (SFTP), and Secure Socket Layer/Transport Layer Security (SSL/TLS).
Consider using out-of-band management network to manage devices.
Use a dedicated management VLAN where nothing but management traffic resides.
Use ACLs to filter unwanted access.
Notes: 10 – LAN Security Concepts
10.3 – Layer 2 Security Threats
10.3.3 - Switch Attack Mitigation Techniques
10.3.4 – Check Your Understanding– Layer 2 Security Threats

## Slide 54: 10.4 MAC Address Table Attack
Notes: 10 – LAN Security Concepts
10.4 – MAC Address Table Attack

## Slide 55: Switch Operation Review
Recall that to make forwarding decisions, a Layer 2 LAN switch builds a table based on the source MAC addresses in received frames. This is called a MAC address table. MAC address tables are stored in memory and are used to more efficiently switch frames.
Notes: 10 – LAN Security Concepts
10.4 – MAC Address Table Attack
10.4.1 – Switch Operation Review

## Slide 56: MAC Address Table Flooding
All MAC tables have a fixed size and consequently, a switch can run out of resources in which to store MAC addresses. MAC address flooding attacks take advantage of this limitation by bombarding the switch with fake source MAC addresses until the switch MAC address table is full.
When this occurs, the switch treats the frame as an unknown unicast and begins to flood all incoming traffic out all ports on the same VLAN without referencing the MAC table. This condition now allows a threat actor to capture all of the frames sent from one host to another on the local LAN or local VLAN.
Note: Traffic is flooded only within the local LAN or VLAN. The threat actor can only capture traffic within the local LAN or VLAN to which the threat actor is connected.
Notes: 10 – LAN Security Concepts
10.4 – MAC Address Table Attack
10.4.2 – MAC Address Table Flooding

## Slide 57: MAC Address Table Attack Mitigation
What makes tools such as macof so dangerous is that an attacker can create a MAC table overflow attack very quickly. For instance, a Catalyst 6500 switch can store 132,000 MAC addresses in its MAC address table. A tool such as macof can flood a switch with up to 8,000 bogus frames per second; creating a MAC address table overflow attack in a matter of a few seconds.
Another reason why these attack tools are dangerous is because they not only affect the local switch, they can also affect other connected Layer 2 switches. When the MAC address table of a switch is full, it starts flooding out all ports including those connected to other Layer 2 switches.
To mitigate MAC address table overflow attacks, network administrators must implement port security. Port security will only allow a specified number of source MAC addresses to be learned on the port. Port security is further discussed in another module.
Notes: 10 – LAN Security Concepts
10.4 – MAC Address Table Attack
10.4.3 – MAC Address Table Attack Mitigation
10.4.4 – Check Your Understanding – MAC Address Table Attacks

## Slide 58: 10.5 LAN Attacks
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks

## Slide 59: Video – VLAN and DHCP Attacks
This video will cover the following:
VLAN Hopping Attack
VLAN Double-Tagging Attack
DHCP Starvation Attack
DHCP Spoofing Attack
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.1 – Video – VLAN and DHCP Attacks

## Slide 60: VLAN Hopping Attacks
A VLAN hopping attack enables traffic from one VLAN to be seen by another VLAN without the aid of a router. In a basic VLAN hopping attack, the threat actor configures a host to act like a switch to take advantage of the automatic trunking port feature enabled by default on most switch ports.
The threat actor configures the host to spoof 802.1Q signaling and Cisco-proprietary Dynamic Trunking Protocol (DTP) signaling to trunk with the connecting switch. If successful, the switch establishes a trunk link with the host, as shown in the figure. Now the threat actor can access all the VLANs on the switch. The threat actor can send and receive traffic on any VLAN, effectively hopping between VLANs.
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.2 – VLAN Hopping Attacks

## Slide 61: VLAN Double-Tagging Attacks
A threat actor is specific situations could embed a hidden 802.1Q tag inside the frame that already has an 802.1Q tag. This tag allows the frame to go to a VLAN that the original 802.1Q tag did not specify.
Step 1: The threat actor sends a double-tagged 802.1Q frame to the switch. The outer header has the VLAN tag of the threat actor, which is the same as the native VLAN of the trunk port.
Step 2: The frame arrives on the first switch, which looks at the first 4-byte 802.1Q tag. The switch sees that the frame is destined for the native VLAN. The switch forwards the packet out all native VLAN ports after stripping the VLAN tag. The frame is not retagged because it is part of the native VLAN. At this point, the inner VLAN tag is still intact and has not been inspected by the first switch.
Step 3: The frame arrives at the second switch which has no knowledge that it was supposed to be for the native VLAN. Native VLAN traffic is not tagged by the sending switch as specified in the 802.1Q specification. The second switch looks only at the inner 802.1Q tag that the threat actor inserted and sees that the frame is destined the target VLAN. The second switch sends the frame on to the target or floods it, depending on whether there is an existing MAC address table entry for the target.
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.3 – VLAN Double-Tagging Attacks

## Slide 62: VLAN Double-Tagging Attacks (Cont.)
A VLAN double-tagging attack is unidirectional and works only when the attacker is connected to a port residing in the same VLAN as the native VLAN of the trunk port. The idea is that double tagging allows the attacker to send data to hosts or servers on a VLAN that otherwise would be blocked by some type of access control configuration. Presumably the return traffic will also be permitted, thus giving the attacker the ability to communicate with devices on the normally blocked VLAN.
VLAN Attack Mitigation - VLAN hopping and VLAN double-tagging attacks can be prevented by implementing the following trunk security guidelines, as discussed in a previous module:
  Disable trunking on all access ports.
  Disable auto trunking on trunk links so that trunks must be manually enabled.
  Be sure that the native VLAN is only used for trunk links.
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.3 – VLAN Double-Tagging Attacks (Cont.)

## Slide 63: DHCP Messages
DHCP servers dynamically provide IP configuration information including IP address, subnet mask, default gateway, DNS servers, and more to clients. A review of the sequence of the DHCP message exchange between client and server is show in the figure.
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.4 – DHCP Messages

## Slide 64: DHCP Attacks
Two types of DHCP attacks are DHCP starvation and DHCP spoofing. Both attacks are mitigated by implementing DHCP snooping.
DHCP Starvation Attack – The goal of this attack is to create a DoS for connecting clients. DHCP starvation attacks require an attack tool such as Gobbler. Gobbler has the ability to look at the entire scope of leasable IP addresses and tries to lease them all. Specifically, it creates DHCP discovery messages with bogus MAC addresses.
DHCP Spoofing Attack – This occurs when a rogue DHCP server is connected to the network and provides false IP configuration parameters to legitimate clients. A rogue server can provide a variety of misleading information, including the following:
    Wrong default gateway - The rogue server provides an invalid gateway or the IP address of its host to create a man-in-the-middle attack. This may go entirely undetected as the intruder intercepts the data flow through the network.
    Wrong DNS server - The rogue server provides an incorrect DNS server address pointing the user to a nefarious website.
    Wrong IP address - The rogue server provides an invalid IP address effectively creating a DoS attack on the DHCP client.
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.5 – DHCP Attacks

## Slide 65: Video – ARP Attacks, STP Attacks, and CDP Reconnaissance
This video will cover the following:
ARP Spoofing Attack
ARP Poisoning Attack
STP Attack
CDP Reconnaissance
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.6 - Video – ARP Attacks, STP Attacks, and CDP Reconnaissance

## Slide 66: ARP Attacks
Hosts broadcast ARP Requests to determine the MAC address of a host with a destination IP address. All hosts on the subnet receive and process the ARP Request. The host with the matching IP address in the ARP Request sends an ARP Reply.
A client can send an unsolicited ARP Reply called a “gratuitous ARP”. Other hosts on the subnet store the MAC address and IP address contained in the gratuitous ARP in their ARP tables.
An attacker can send a gratuitous ARP message containing a spoofed MAC address to a switch, and the switch would update its MAC table accordingly. In a typical attack, a threat actor sends unsolicited ARP Replies to other hosts on the subnet with the MAC Address of the threat actor and the IP address of the default gateway, effectively setting up a man-in-the-middle attack.
There are many tools available on the internet to create ARP man-in-the-middle attacks.
IPv6 uses ICMPv6 Neighbor Discovery Protocol for Layer 2 address resolution. IPv6 includes strategies to mitigate Neighbor Advertisement spoofing, similar to the way IPv6 prevents a spoofed ARP Reply.
ARP spoofing and ARP poisoning are mitigated by implementing Dynamic ARP Inspection (DAI).
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.7- ARP Attacks

## Slide 67: Address Spoofing Attacks
IP address spoofing is when a threat actor hijacks a valid IP address of another device on the subnet or uses a random IP address. IP address spoofing is difficult to mitigate, especially when it is used inside a subnet in which the IP belongs.
MAC address spoofing attacks occur when the threat actors alter the MAC address of their host to match another known MAC address of a target host. The switch overwrites the current MAC table entry and assigns the MAC address to the new port. It then inadvertently forwards frames destined for the target host to the attacking host.
When the target host sends traffic, the switch will correct the error, realigning the MAC address to the original port. To stop the switch from returning the port assignment to its correct state, the threat actor can create a program or script that will constantly send frames to the switch so that the switch maintains the incorrect or spoofed information.
There is no security mechanism at Layer 2 that allows a switch to verify the source of MAC addresses, which is what makes it so vulnerable to spoofing.
IP and MAC address spoofing can be mitigated by implementing IP Source Guard (IPSG).
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.8 – Address Spoofing Attacks

## Slide 68: STP Attack
Network attackers can manipulate the Spanning Tree Protocol (STP) to conduct an attack by spoofing the root bridge and changing the topology of a network. Attackers can then capture all traffic for the immediate switched domain.
To conduct an STP manipulation attack, the attacking host broadcasts STP bridge protocol data units (BPDUs) containing configuration and topology changes that will force spanning-tree recalculations. The BPDUs sent by the attacking host announce a lower bridge priority in an attempt to be elected as the root bridge.
This STP attack is mitigated by implementing BPDU Guard on all access ports. BPDU Guard is discussed in more detail later in the course.
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.9 – STP Attack

## Slide 69: CDP Reconnaissance
The Cisco Discovery Protocol (CDP) is a proprietary Layer 2 link discovery protocol. It is enabled on all Cisco devices by default. Network administrators also use CDP to help configure and troubleshoot network devices. CDP information is sent out CDP-enabled ports in periodic, unencrypted, unauthenticated broadcasts. CDP information includes the IP address of the device, IOS software version, platform, capabilities, and the native VLAN. The device receiving the CDP message updates its CDP database.
To mitigate the exploitation of CDP, limit the use of CDP on devices or ports. For example, disable CDP on edge ports that connect to untrusted devices.
  To disable CDP globally on a device, use the no cdp run global configuration mode command. To enable CDP globally, use the cdp run global configuration command.
  To disable CDP on a port, use the no cdp enable interface configuration command. To enable CDP on a port, use the cdp enable interface configuration command.
Note: Link Layer Discovery Protocol (LLDP) is also vulnerable to reconnaissance attacks. Configure no lldp run to disable LLDP globally. To disable LLDP on the interface, configure no lldp transmit and no lldp receive.
Notes: 10 – LAN Security Concepts
10.5 – LAN Attacks
10.5.10 – CDP Reconnaissance
10.5.11 – Check Your Understanding – LAN Attacks

## Slide 70: 10.6 Module Practice and Quiz
Notes: 10 – LAN Security Concepts
10.6 – Module Practice and Quiz

## Slide 71: Module 10: Best Practices
Topic 10.1
    What is another threat that you can think of?
    What methods do you employ to protect yourself against SPAM and phishing?
Topic 10.2
    Can you think of an instance where using a local database would be preferable to using a centralized database?
    Why is layer 2 security so important?
Topic 10.3
    What configuration or process do you consider to be the cornerstone of layer 2 security?
    In what instances would a dedicated management VLAN be too cumbersome to implement?
Topic 10.4
    Do you know of any other tools that could generate a MAC address flooding attack?
    What is the danger in the flooding of unknown unicast frames?
Topic 10.5
    What configuration(s) could you implement to prevent unauthorized trunks, and thus VLAN Hopping attacks?
    Where in the network should a layer 2 discovery protocol be enabled?
Notes: 71

## Slide 72: Module 10: Best Practices (Cont.)
Téma 10.1
Jaké metody používáte k ochraně proti SPAMU a phishingu?
Téma 10.2
Napadá vás instance, kde by bylo lepší použít lpkální databázi než centralizovanou databázi?
Proč je zabezpečení vrstvy 2 tak důležité?
Téma 10.3
Jakou konfiguraci nebo proces považujete za základní kámen zabezpečení vrstvy 2?
V jakých případech by byla vyhrazená (dedikovaná) správa VLAN příliš těžkopádná na implementaci?
Téma 10.4
Znáte nějaké další nástroje, které by mohly generovat útok na MAC adresy?
Jaké je nebezpečí při zaplavení neznámých unicast snímků?
Téma 10.5
Jaké konfigurace byste mohli implementovat, abyste zabránili neoprávněným trunkům, a tedy útokům VLAN Hopping attacks?
Kde v síti by měl být povolen protokol zjišťování vrstvy 2?
Notes: 72

## Slide 73
Cynet XDR provides multiple, integrated prevention
technologies to block standard and advanced attacks across
your environment. The detection power achieved by natively
combining signals and data from multiple sources simply
cannot be matched by siloed, point protection solutions.

## Slide 74: Module Practice and Quiz What Did I Learn In This Module?
Endpoints are particularly susceptible to malware-related attacks that originate through email or web browsing, such as DDOS, date breaches, and malware. These endpoints have typically used traditional host-based security features, such as antivirus/antimalware, host-based firewalls, and host-based intrusion prevention systems (HIPSs). Endpoints are best protected by a combination of NAC, host-based AMP software, an email security appliance (ESA), and a web security appliance (WSA).
AAA controls who is permitted to access a network (authenticate), what they can do while they are there (authorize), and to audit what actions they performed while accessing the network (accounting).
The IEEE 802.1X standard is a port-based access control and authentication protocol that restricts unauthorized workstations from connecting to a LAN through publicly accessible switch ports.
If Layer 2 is compromised, then all layers above it are also affected. The first step in mitigating attacks on the Layer 2 infrastructure is to understand the underlying operation of Layer 2 and the Layer 2 solutions: Port Security, DHCP Snooping, DAI, and IPSG. These won’t work unless management protocols are secured.
Notes: 10 – LAN Security Concepts
10.6 – Module Practice and Quiz
10.6.1 – What did I learn in this module?

## Slide 75: Module Practice and Quiz What Did I Learn In This Module? (Cont.)
MAC address flooding attacks bombard the switch with fake source MAC addresses until the switch MAC address table is full.
A VLAN hopping attack enables traffic from one VLAN to be seen by another VLAN without the aid of a router.
A VLAN double-tagging attack is unidirectional and works only when the threat actor is connected to a port residing in the same VLAN as the native VLAN of the trunk port.
VLAN hopping and VLAN double-tagging attacks can be prevented by implementing the following trunk security guidelines:
  Disable trunking on all access ports.
  Disable auto trunking on trunk links so that trunks must be manually enabled.
  Be sure that the native VLAN is only used for trunk links.
Two types of DHCP attacks are DHCP starvation and DHCP spoofing. Both attacks are mitigated by implementing DHCP snooping.
Notes: 10 – LAN Security Concepts
10.6 – Module Practice and Quiz
10.6.1 – What did I learn in this module? (Cont.)

## Slide 76: Module Practice and Quiz What Did I Learn In This Module? (Cont.)
ARP Attack: A threat actor sends a gratuitous ARP message containing a spoofed MAC address to a switch, and the switch updates its MAC table accordingly. Now the threat actor sends unsolicited ARP Replies to other hosts on the subnet with the MAC Address of the threat actor and the IP address of the default gateway. ARP spoofing and ARP poisoning are mitigated by implementing DAI.
Address Spoofing Attack: IP address spoofing is when a threat actor hijacks a valid IP address of another device on the subnet or uses a random IP address. MAC address spoofing attacks occur when the threat actors alter the MAC address of their host to match another known MAC address of a target host. IP and MAC address spoofing can be mitigated by implementing IPSG.
STP Attack: Threat actors manipulate STP to conduct an attack by spoofing the root bridge and changing the topology of a network. Threat actors make their hosts appear as root bridges; therefore, capturing all traffic for the immediate switched domain. This STP attack is mitigated by implementing BPDU Guard on all access ports.
CDP Reconnaissance: CDP information is sent out CDP-enabled ports in periodic, unencrypted broadcasts. CDP information includes the IP address of the device, IOS software version, platform, capabilities, and the native VLAN. The device receiving the CDP message updates its CDP database. the information provided by CDP can also be used by a threat actor to discover network infrastructure vulnerabilities. To mitigate the exploitation of CDP, limit the use of CDP on devices or ports.
Notes: 10 – LAN Security Concepts
10.6 – Module Practice and Quiz
10.6.1 – What did I learn in this module? (Cont.)
10.6.2 – Module Quiz – LAN Security Concepts

## Slide 77: Module 10: LAN Security Concepts New Terms and Commands
Data Breach
Malware
Next-Generation Firewall (NGFW)
Next-Generation IPS (NGIPS)
Advanced Malware Protection (AMP)
Authentication, Authorization, Accounting (AAA)
Identity Services Engine (ISE)
Host-Based Intrusion Prevention System (HIPS)
Email Security Appliance (ESA)
Web Security Appliance (WSA)
login {local}
Remote Authentication Dial-In User Service (RADIUS)
Terminal Access Controller Access Control System (TACACS+)
IEEE 802.1X
Client (Supplicant)
Authenticator
Port Security
DHCP Snooping
Dynamic ARP Inspection (DAI)
IP Source Guard (IPSG)
VLAN Hopping
VLAN Double-Tagging
DHCP Starvation
DHCP Spoofing
Gratuitous ARP
ARP Spoofing
ARP Poisoning
Cisco Discovery Protocol (CDP)
no cdp run
no cdp enable
no lldp run
no lldp transmit | receive