## Slide 1: 02 Measuring Energy
Václav Šebek

## Slide 2: Measuring Energy
Literature:
  Bhattacharyya, S.C., 2011. Energy Economics: Concepts, Issues, Markets and Governance. Springer London, London.
  Chapters 2 and 13

## Slide 3: From data to information
Measuring energy

## Slide 4: What is energy? recap
A property of objects meaning capability of doing work or being transferred elsewhere
Most common heat, electricity, motive
Units:
  Energy: 1 [Watt hour] = 3.600 [Joule]
  Power: 1 [Watt] = 1 [Joule per second]
Power gives you what are you able to do
Energy says what you have done already

## Slide 5: What is energy? recap
Footnote
  Ton of Oil Equivalent [toe] ≈ 42 GJ
  Ton of Coal Equivalent [tce] ≈ 29 GJ
    Czech lignite at 10 to 20 [GJ.t-1]
  British Thermal Unit [BTU] ≈ 1.05 kJ
  Quad ≈ 1,055 PJ
    US Dep. of Energy meaning quadrillion of BTU
    Czech republic TPES 2014 ≈ 1.7 PJ ≈ 1.6 Quads

## Slide 6: What is energy? recap
Heat, light, motive force, chemical transformation etc.
2 thermodynamic laws
  Mass and energy cannot vanish but transform
  No 100% conversion – losses inevitable
Primary x Secondary energy
  Primary – directly from nature (oil, coal, wind, sun, nuclear…)
  Secondary – derived from Primaries (electricity, gasoline…)

## Slide 7: What is energy? recap
Other divisions (boundaries change)
  Renewable x Non-Renewable
  Commercial x Non-Commercial
  Modern x Traditional
  Conventional x Non-Conventional

## Slide 8: Energy System
Supply – Conversion – Consumption
Extraction  PES  Transport  Final Energy  End use app  Useful energy
Losses
Energy corporations all through the system  wide variety of companies

## Slide 10: Energy Information
Broadly required data:
  Energy use by various economic activities
  E production, transformation and delivery to various users
  „Field“ technical and operating statistics
  Financial and cost information
  Macro-economic, social, political information

## Slide 11: Energy Information
Transform into information about energy…
  Pricing
  Investment
  Research & Development
  System Management
  Contingency Plan
  Long-term Planning

## Slide 12: Energy Accounting Framework
Comprehensive account of energy flows including losses and any consumption
See table
  Production – transformation – consumption
Accounting units
  Commodity (physical, tones, barrels…)
  Overall Energy Balance (common unit, eg BTU, GJ, TOE…) – easier comparison

## Slide 13: Energy Accounting Framework
Supply-side
Production (+)
Trade (import/export) (+/-)
Bunkers (transport costs, e.g. Tankers) (-)
Stock change (+/-)
Primary energy requirement (PER)
Conversion
Statistical difference (+/-)
Transformation input (-)
Energy sectors‘ own use (-)
Transmission and Distribution losses (-)
Net supply available
Net domestic consumption
Final energy consumption
Agriculture
Industry
Transport
Residential
Commercial
Non-energy uses
Total energy needed to satisfy country’s demand and transformation requirements
Primary need (shown in TPES)
Efficiency indicator
Sectorial situation may be analyzed

## Slide 14: Energy Accounting Units - Example
Consumer | TJ | kt | GJ/t | Share |  |  | 
 |  |  |  | TJ | kt | ktce | ktoe
PP Chvaletice | 16 631 | 978 | 17,00 | 32% | 33% | 567 | 397
Refinery Litvínov | 7 072 | 530 | 13,35 | 14% | 18% | 241 | 169
HP Otrokovice | 4 523 | 274 | 16,51 | 9% | 9% | 154 | 108
Paperworks Mondi Štětí | 4 358 | 180 | 16,70 | 8% | 6% | 149 | 104
HP Strakonice, a.s. | 1 754 | 112 | 15,66 | 3% | 4% | 60 | 42
HP Třinec | 1 698 | 106 | 16,00 | 3% | 4% | 58 | 41
HP Poříčí | 789 | 47 | 16,79 | 2% | 2% | 27 | 19
PP Hodonín | 446 | 27 | 16,63 | 1% | 1% | 15 | 11
Export | 6 640 | 332 | 20,00 | 13% | 11% | 227 | 159
Retail | 8 360 | 418 | 20,00 | 16% | 14% | 285 | 200
Total/mean | 52 271 | 3 004 | 17,40 | 100% | 100% | 1 784 | 1 248
Tab – A lignite surface mine yearly consumption decomposition
All units above are scientific – commercial units (eg TCE) might be not

## Slide 15: Lignite Surface Mine

## Slide 16: Useful Ratios
Energy supply mix
  Share of various sources on primary supply
Self-reliance
  What portion of energy is of domestic origin
Share of renewables
Power generation mix
Efficiency
  Electricity production
  Refining
  Overall
Per capita consumption (primary and final)
Energy intensity

## Slide 17: Some energy data issues
Availability
  lags, various sources, imprecision, confidentiality
Quality
  Different standards and methodologies, deliberate changes, trade and balance discrepancies
Cross border comparison
  Traditional fuels, terminologies, sectors definition, accounting
Common measurment
Conversion factors

## Slide 18: At what price?
Measuring energy

## Slide 19: Price - recap
Price x value
Price
  Objective measurable figure
  Result of supply/demand
  Denotes relative scarcity of a good
Value
  Subjective, individual, not measurable
  Depends on time, place and people
Value of price is priceless

## Slide 20: Energy Pricing
Self-sufficient country
  Price set domestically between export and import parity price
Q
P
S
D
Q
P
S
D
p* = pm
Max domestic production below world price
p*
Realized consumption
Import
+
= domestic consumption
Importing country
  Import (world) price
pm
q*
q’
q*
px

## Slide 21: Energy Pricing
Q
P
S
D
Max domestic consumption
Export
+
= Total domestic production
Net exporter
  Domestic demand satisfied below world price
  Equilibrium price should be that of world price
  In reality domestic prices of oil exporters significantly lower due subsidies
p* = px

## Slide 22: Peak and Off-Peak Pricing
[MW]
Daytime
Chart: Daily consumption of Electricity
| 7 | 8 | 10 | 11 | 12 | 13 | 14 | 16 | 17 | 18 | 19 | 20 | 22 | 23 | 24 | 1 | 2 | 4 | 5 | 6 | 7 | 8 | 10 | 11 | 12 | 13 | 14 | 16 | 17 | 18 | 19 | 20 | 22 | 23 | 24 | 1 | 2 | 4 | 5 | 6 | 7 | 8 | 10 | 11 | 12 | 13 | 14 | 16 | 17 | 18 | 19 | 20 | 22 | 23 | 24 | 1
Denní zatížení sítě | 7.9635 | 8.3817 | 8.7135 | 8.9266 | 9 | 8.9266 | 8.7135 | 8.3817 | 7.9635 | 7.5 | 7.0365 | 6.6183 | 6.2865 | 6.0734 | 6 | 6.0734 | 6.2865 | 6.6183 | 7.0365 | 7.5 | 7.9635 | 8.3817 | 8.7135 | 8.9266 | 9 | 8.9266 | 8.7135 | 8.3817 | 7.9635 | 7.5 | 7.0365 | 6.6183 | 6.2865 | 6.0734 | 6 | 6.0734 | 6.2865 | 6.6183 | 7.0365 | 7.5 | 7.9635 | 8.3817 | 8.7135 | 8.9266 | 9 | 8.9266 | 8.7135 | 8.3817 | 7.9635 | 7.5 | 7.0365 | 6.6183 | 6.2865 | 6.0734 | 6 | 6.0734

## Slide 23: Peak and Off-Peak Pricing
Chart: Decomposition of electricity consumption by origin
| 7 | 8 | 10 | 11 | 12 | 13 | 14 | 16 | 17 | 18 | 19 | 20 | 22 | 23 | 24 | 1 | 2 | 4 | 5 | 6 | 7 | 8 | 10 | 11 | 12 | 13 | 14 | 16 | 17 | 18 | 19 | 20 | 22 | 23 | 24 | 1 | 2 | 4 | 5 | 6 | 7 | 8 | 10 | 11 | 12 | 13 | 14 | 16 | 17 | 18 | 19 | 20 | 22 | 23 | 24 | 1
Jádro | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.6 | 3.4 | 3.2 | 3 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6
OZE | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.4 | 0.9 | 1.5 | 2.1 | 1.9 | 1.7 | 1.3 | 0.6 | 0.5 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.5 | 1 | 1.4 | 2.9 | 3.3 | 1 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.5 | 0.9 | 1.2 | 1.3 | 1.1 | 0.8 | 0.6
Uhlí | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 2.8635 | 1.8 | 1.5365 | 1.3183 | 1.3865 | 1.8734 | 1.9 | 2.0734 | 2.2865 | 2.6183 | 3.0365 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 2.5 | 2.0266 | 3.5 | 3.5 | 3.5 | 3.5 | 3.1365 | 2.7183 | 2.3865 | 2.1734 | 2.3 | 2.5734 | 2.9865 | 3.7183 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 3.5365 | 2.8183 | 2.3865 | 2.3734 | 2.6 | 2.8734
Špička | 0.56353 | 0.98168 | 1.3135 | 1.5266 | 1.6 | 1.5266 | 1.2135 | 0.38168 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.46353 | 0.78168 | 0.61353 | 0.42658 | 0 | 0 | 0.61353 | 0.98168 | 0.56353 | 0.1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.13647 | 0.6 | 1.0635 | 1.4817 | 1.8135 | 2.0266 | 2.1 | 2.0266 | 1.8135 | 1.4817 | 1.0635 | 0.4 | 0 | 0 | 0 | 0 | 0 | 0
[MW]
Daytime
Nuclear (yellow) – Renewables (green) – Coal (brown) – Peak gas (blue)

## Slide 24: Peak and Off-Peak Pricing
Chart: Electricity Exchange Pricing
| 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400 | 1500 | 1600 | 1700 | 1800 | 1900 | 2000 | 2100 | 2200 | 2300 | 2400 | 2500 | 2600 | 2700 | 2800 | 2900 | 3000 | 3100 | 3200 | 3300 | 3400 | 3500 | 3600 | 3700 | 3800 | 3900 | 4000 | 4100 | 4200 | 4300 | 4400 | 4500 | 4600 | 4700 | 4800 | 4900 | 5000 | 5100 | 5200 | 5300 | 5400 | 5500 | 5600 | 5700 | 5800 | 5900 | 6000 | 6100 | 6200 | 6300 | 6400 | 6500 | 6600 | 6700 | 6800 | 6900 | 7000 | 7100 | 7200 | 7300 | 7400 | 7500 | 7600 | 7700 | 7800 | 7900 | 8000 | 8100 | 8200 | 8300 | 8400 | 8500 | 8600 | 8700 | 8800 | 8900 | 9000 | 9100 | 9200 | 9300 | 9400 | 9500 | 9600 | 9700 | 9800 | 9900 | 10000 | 10100 | 10200 | 10300 | 10400 | 10500 | 10600 | 10700
Nuclear | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
Lignite | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.32 | 0.32 | 0.32 | 0.32 | 0.32 | 0.32 | 0.35 | 0.35 | 0.35 | 0.35 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.39 | 0.39 | 0.39 | 0.39 | 0.39 | 0.4 | 0.4 | 0.4 | 0.4
Hard Coal | 0.5 | 0.5 | 0.5 | 0.5 | 0.51 | 0.51 | 0.51 | 0.51 | 0.51 | 0.54 | 0.54 | 0.54 | 0.54 | 0.54 | 0.54 | 0.54
Gas | 0.7 | 0.7 | 0.7 | 0.74 | 0.74 | 0.74 | 0.74 | 0.74 | 0.8 | 0.8 | 0.8 | 0.87 | 0.87
Peak | 1 | 1 | 1 | 1.2 | 1.2
[Kč/KWh]
D
Price

## Slide 25: Renewables and Electricity Pricing
Chart: Electricity Exchange Pricing
| 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400 | 1500 | 1600 | 1700 | 1800 | 1900 | 2000 | 2100 | 2200 | 2300 | 2400 | 2500 | 2600 | 2700 | 2800 | 2900 | 3000 | 3100 | 3200 | 3300 | 3400 | 3500 | 3600 | 3700 | 3800 | 3900 | 4000 | 4100 | 4200 | 4300 | 4400 | 4500 | 4600 | 4700 | 4800 | 4900 | 5000 | 5100 | 5200 | 5300 | 5400 | 5500 | 5600 | 5700 | 5800 | 5900 | 6000 | 6100 | 6200 | 6300 | 6400 | 6500 | 6600 | 6700 | 6800 | 6900 | 7000 | 7100 | 7200 | 7300 | 7400 | 7500 | 7600 | 7700 | 7800 | 7900 | 8000 | 8100 | 8200 | 8300 | 8400 | 8500 | 8600 | 8700 | 8800 | 8900 | 9000 | 9100 | 9200 | 9300 | 9400 | 9500 | 9600 | 9700 | 9800 | 9900 | 10000 | 10100 | 10200 | 10300 | 10400 | 10500 | 10600 | 10700
Nuclear | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
Lignite | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.32 | 0.32 | 0.32 | 0.32 | 0.32 | 0.32 | 0.35 | 0.35 | 0.35 | 0.35 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.39 | 0.39 | 0.39 | 0.39 | 0.39 | 0.4 | 0.4 | 0.4 | 0.4
Hard Coal | 0.5 | 0.5 | 0.5 | 0.5 | 0.51 | 0.51 | 0.51 | 0.51 | 0.51 | 0.54 | 0.54 | 0.54 | 0.54 | 0.54 | 0.54 | 0.54
Gas | 0.7 | 0.7 | 0.7 | 0.74 | 0.74 | 0.74 | 0.74 | 0.74 | 0.8 | 0.8 | 0.8 | 0.87 | 0.87
Peak | 1 | 1 | 1 | 1.2 | 1.2
[Kč/KWh]
Demand
Price

## Slide 26: Renewables and Electricity Pricing
Chart: Renewables incoming
| 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400 | 1500 | 1600 | 1700 | 1800 | 1900 | 2000 | 2100 | 2200 | 2300 | 2400 | 2500 | 2600 | 2700 | 2800 | 2900 | 3000 | 3100 | 3200 | 3300 | 3400 | 3500 | 3600 | 3700 | 3800 | 3900 | 4000 | 4100 | 4200 | 4300 | 4400 | 4500 | 4600 | 4700 | 4800 | 4900 | 5000 | 5100 | 5200 | 5300 | 5400 | 5500 | 5600 | 5700 | 5800 | 5900 | 6000 | 6100 | 6200 | 6300 | 6400 | 6500 | 6600 | 6700 | 6800 | 6900 | 7000 | 7100 | 7200 | 7300 | 7400 | 7500 | 7600 | 7700 | 7800 | 7900 | 8000 | 8100 | 8200 | 8300 | 8400 | 8500 | 8600 | 8700 | 8800 | 8900 | 9000 | 9100 | 9200 | 9300 | 9400 | 9500 | 9600 | 9700 | 9800 | 9900 | 10000 | 10100 | 10200 | 10300 | 10400 | 10500 | 10600 | 10700
Renewables
Nuclear | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
Lignite | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.32 | 0.32 | 0.32 | 0.32 | 0.32 | 0.32 | 0.35 | 0.35 | 0.35 | 0.35 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.39 | 0.39 | 0.39 | 0.39 | 0.39 | 0.4 | 0.4 | 0.4 | 0.4
Hard Coal | 0.5 | 0.5 | 0.5 | 0.5 | 0.51 | 0.51 | 0.51 | 0.51 | 0.51 | 0.54 | 0.54 | 0.54 | 0.54 | 0.54 | 0.54 | 0.54
Gas | 0.7 | 0.7 | 0.7 | 0.74 | 0.74 | 0.74 | 0.74 | 0.74 | 0.8
Peak
[Kč/KWh]
Demand
Price

## Slide 27: Renewables and Electricity Pricing
Chart: Renewables out…
| 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400 | 1500 | 1600 | 1700 | 1800 | 1900 | 2000 | 2100 | 2200 | 2300 | 2400 | 2500 | 2600 | 2700 | 2800 | 2900 | 3000 | 3100 | 3200 | 3300 | 3400 | 3500 | 3600 | 3700 | 3800 | 3900 | 4000 | 4100 | 4200 | 4300 | 4400 | 4500 | 4600 | 4700 | 4800 | 4900 | 5000 | 5100 | 5200 | 5300 | 5400 | 5500 | 5600 | 5700 | 5800 | 5900 | 6000 | 6100 | 6200 | 6300 | 6400 | 6500 | 6600 | 6700 | 6800 | 6900 | 7000 | 7100 | 7200 | 7300 | 7400 | 7500 | 7600 | 7700 | 7800 | 7900 | 8000 | 8100 | 8200 | 8300 | 8400 | 8500 | 8600 | 8700 | 8800 | 8900 | 9000 | 9100 | 9200 | 9300 | 9400 | 9500 | 9600 | 9700 | 9800 | 9900 | 10000 | 10100 | 10200 | 10300 | 10400 | 10500 | 10600 | 10700
Renewables
Nuclear | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
Lignite | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.32 | 0.32 | 0.32 | 0.32 | 0.32 | 0.32 | 0.35 | 0.35 | 0.35 | 0.35 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.375 | 0.39 | 0.39 | 0.39 | 0.39 | 0.39 | 0.4 | 0.4 | 0.4 | 0.4
Hard Coal | 0.5 | 0.5 | 0.5 | 0.5 | 0.51 | 0.51
Gas | 0.7 | 0.7 | 0.7 | 0.74 | 0.74 | 0.74 | 0.74 | 0.74 | 0.8 | 0.8 | 0.8 | 0.87 | 0.87
Peak | 1 | 1 | 1 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2
[Kč/KWh]
Demand
Price

## Slide 28
50
0
100
10/2010
10/2012
10/2011
10/2013
10/2014
€/MWh
170 € daily mean, 250 € daily max 10.2.2012
0 € daily mean, -450 € daily min 25.12.2012
Zdroj: https://www.epexspot.com/
Daily electricity price at European Power Exchange Leipzig

## Slide 29: Merit order application - Oil
See: http://www.economist.com/blogs/graphicdetail/2016/01/daily-chart-6

## Slide 30: Price is vital piece of information

## Slide 31: How to regulate?
Measuring energy

## Slide 32: Allowances v Taxes
Government aims to decrease CO2 emissions
Two ways of achieving that:
  Tax – payment for each ton of CO2 emitted
  Tradable allowances – permission to emit particular volume of CO2
Different parameters
  Tax – maximum price for decarbonisation is set
  Allowances – maximum volume is set

## Slide 33: Example 1
Two types of PP in a Country – A and B
Both emit 40t CO2 per year = total 80t/y
Different emission reduction costs per 10t
  A = $2,000; B = $4,000
Government’ objective is 60t CO2 per year
  Regulation
  Tax
  Allowances

## Slide 34: Example 1
Regulation
  Each PP must decrease emissions by 10t/y
  Costs = 2,000 + 4,000 = $6,000
Allowances
  60t allowances issued, both A and B get 30t
  B buys 10t allowances from A and emits 40t
  A emit 20t … total emissions 60t
  Costs = 2 * 2,000 = $4,000
  Price of allowance between $2k and $4k
Taxation
  T < $2k … no emission reduction & C+T = $0 + $0…16k
  $2k < T < $4k … 40t of A reduced & C+T = $8k + $8k…16k
  $4k < T … all emissions reduced & C+T = $16k + $0

## Slide 35: Example 2
Company | Emissions [t] | Costs reducing 1 t
A | 70 | 20
B | 80 | 25
C | 50 | 10
Total | 200 | 
Government objective: 120 t
Method: Allowances
Who will sell at what price?
What will be final cost of reducing emissions?

## Slide 36: Example 2
Chart: 
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120
Supply | 10 | 10 | 10 | 10 | 20 | 20 | 20 | 20 | 25 | 25 | 25 | 25
Demand | 25 | 25 | 25 | 25 | 20 | 20 | 20 | 10
Company | Emissions [t] | Costs reducing 1 t
A | 70 | $20
B | 80 | $25
C | 50 | $10
Total | 200 (120 allowances issued) | 
S
D
C sells 40t allowances to B at price of $20
Total costs = $1,100
  A reduces 30t at $20
  B doesn’t reduce
  C reduces 50 at $10
Costs w/o trade
  $1,700