## Slide 1
Energy Resources:
Past, Present, and Future

## Slide 2
Energy is the ability to do work
1st Law of Thermodynamics:
energy cannot be created or destroyed
2nd Law of Thermodynamics:
energy goes from a high quality to a lower quality during each energy transformation; while energy is conserved, it’s ability to do work decreases
Forms of energy: potential, kinetic, thermal, chemical, electrical, etc.

## Slide 3
Energy is key to Sustaining system structure and complexity
Natural and human systems build and maintain order and organization by taking in high quality energy, using it, and passing degraded energy outside of the system boundary.
Our society is dependent on the energy flows that support it AND having a sink for the waste.
System
(human or
natural)
High quality
Energy Input
Low quality
Energy output (waste heat)

## Slide 4
Simplified Ecosystem

## Slide 5
Renewable versus nonrenewable resources
Renewable energy resources – are continuously replenished at a rate useful for human consumption
Nonrenewable energy resources – are limited in supply or are replenished at a rate that is negligible compared to rate of human consumption.

## Slide 6
Conventional Energy Sources
1. Fossil fuels---coal, petroleum, natural gas---have stored solar energy, that we draw on today for the activities of the modern life.
Alternative Energy Sources
2. Nuclear power began in US in 1957 in Shippingport, PA. Use varies greatly from country to country
3. Renewable energy---hydroelectric power; biomass such as wood, waste, and biofuels; geothermal; solar; and wind---is replenishable

## Slide 10
Energy Consumption by Primary Energy Source

## Slide 11
Energy Consumption by Source, 1635-2006

## Slide 12
Energy end uses:
Heat
Transport
Electricity
Energy Sectors:
Residential/Commercial
Industrial
Transportation
What
Where

## Slide 13
Historical Energy Use
Earlier civilizations used renewable energy sources exclusively
Biomass for heat and cooking

## Slide 14
Historical Energy Use
Earlier civilizations used renewable energy sources exclusively
Wind for windmills (pumping) and sailing

## Slide 15
Historical Energy Use
Earlier civilizations used renewable energy sources exclusively
Water for watermills (milling)

## Slide 16
Historical Energy Use
Earlier civilizations used renewable energy sources exclusively
Animal and human energy for labor

## Slide 17
Historical Energy Use
Earlier civilizations used renewable energy sources exclusively
Biomass for heat and cooking
Wind for windmills (pumping) and sailing
Water for watermills (milling)
Solar for thermal regulation
Animal and human energy for labor
These sources are renewable with little long term impact on the environment, but have a generally low energy density.
Energy density is the amount of energy stored in a given space per unit volume

## Slide 18
Transition to fossil fuels
Coal – used as early as 13th century, extensive use by mid-19th century
Oil – used mid-late 19th century
Natural Gas – used late 19th century, big boom after WWII

## Slide 19
Fossil Fuels are derived from partially decomposed organic materials transformed in Earth’s crust by pressure, heat and bacterial processes. It takes millions of years for these organisms to chemically change into fossil fuels.

## Slide 20
Coal formation

## Slide 22
Coal Consumption by Sector

## Slide 23
Electricity Generation
whether from fossil fuels, nuclear, renewable fuels, or other sources - is usually* based on the fact that:
"When copper wire is moving through a magnetic field, an electric current is generated in that wire."
www.hawaii.gov/dbedt/ert/electgen.html
* exceptions are electrochemistry (batteries) and photovoltaic effect

## Slide 24
In the picture, the shaft and armature (with copper wire) spin around. The magnets are on the outside (they don't move). Electricity, at the "+" and "-" terminals, is shown in the picture as a lighting bolt.
The wire is in the presence of the magnetic field,
but is NOT touching the magnet

## Slide 25
So where do all the different energy sources come in? It's all a question of how to get (and keep) the system moving (i.e. how to keep the copper wire spinning around).
In a steam power plant, fuels (such as petroleum, coal, or biomass) are burned to heat water which turns into steam, which goes through a turbine, which spins...turning the copper wire (armature) inside the generator and generating an electric current.

## Slide 26
Electric generators are essentially very large quantities of copper wire spinning around inside very large magnets at very high speeds.
A commercial utility electric generator -- for example, a 180-megawatt generator is 20 ft in diameter, 50 ft long, and weighs >50 tons. The copper coils (called the "armature") spin at 3600 rpm. Although the principle is simple (copper wire and magnets), it's not necessarily easy!

## Slide 27
In a nuclear power plant, nuclear reactions create heat to heat water, which turns into steam, which goes through a turbine, which spins...turning the copper armature inside the generator and generating an electric current.
In a wind turbine, the wind pushes against the turbine blades, causing the rotor to spin...turning the copper armature inside the generator and generating an electric current.
In a hydroelectric turbine, flowing (or falling) water pushes against the turbine blades, causing the rotor to spin...turning the copper armature inside the generator and generating an electric current.
The different energy sources just provide energy to do the same basic thing...turning the copper armature inside the generator and generating an electric current.

## Slide 28
Hamsters
Humans

## Slide 29
A "generator" and "motor" are essentially the same thing: what you call it depends on whether electricity is going into the unit or coming out of it.
A generator produces electricity. In a generator, something causes the shaft and armature to spin. Lots of things can be used to make a shaft spin. It doesn't matter what's used to spin the shaft - the electricity that's produced is the same.
A motor uses electricity. The electric current causes the armature and shaft to spin.

## Slide 31
Original Col. Drake Well, August 27, 1859
Titusville, Pa

## Slide 32
Petroleum Consumption by Sector

## Slide 36
World oil flow
U.S. uses 19 Million barrels of petroleum per DAY. Most for transportation.

## Slide 38
M.K. Hubbert’s view of the oil age over the long-term

## Slide 39
Natural gas is currently seen as a transition or “bridge” fuel: from coal to renewables
Pros:
Lower carbon emissions than coal
Prices are low (now)
Supply is high (now)
Cons:
Methane emissions are more potent GHG than CO2 Non-renewable resource

## Slide 40
Environmental Impacts of
Fossil Fuel Use
Oil spills
Photochemical smog
Acid mine drainage
Climate Change

## Slide 41
Environmental impacts of fossil fuel use
Recovery – land disruption, loss of habitat, surface water pollution, air pollutants, land subsidence
Off-shore oil drilling –oil seepages, aesthetic degradation
Refining – spills leaks, soil and groundwater pollution
Delivery – Spills
Use CO2 – emission, air pollution (smog), acid rain
BOTH SUPPLY AND USE ISSUES
WITH FOSSIL FUEL RESOURCES

## Slide 42
Renewable Energy
Hydroelectric
Biomass
Wind
Geothermal
Solar
Tidal

## Slide 44
Most renewables start with solar energy
Have specific end uses
Have lower energy density
Lower environmental impact

## Slide 45
Renewable Energy Consumption by Sector

## Slide 46
Hydroelectric power (250BKw ~10% total in U.S.)
By Tomia - Own work, CC BY 2.5, https://commons.wikimedia.org/w/index.php?curid=3302749

## Slide 47
Wind Energy

## Slide 49
Solar Energy
Passive solar uses building designs (i.e., walls, windows, floors, roofs, materials, and landscaping) to manage energy budget.
Daylighting optimizes the use of natural light.
Notes: Daylighting can also reduce the need for air-conditioning in rooms heated by light bulbs

## Slide 50
Passive solar design uses overhangs or vegetation

## Slide 51
Active solar uses mechanical equipment for heating, collecting, and electricity generation.
Photovoltaics
Collectors
Solar hot water, NOT PV

## Slide 52
Providing hot water for homes

## Slide 54
Photovoltaic cell or solar cell
Solar panels on the rooftops of Barton and Douglass Houses.

## Slide 55
West Bengal, India. Rooftop PV modules on a village health center provide power for refrigerators containing medicines and vaccines, for lights, and for other important needs. U.S.DOE
Remote applications of PV where electric grid does not exist

## Slide 56
In 1997 "Sojourner" explored Mars using high-efficiency photovoltaic (PV) cells which generated 16 watts of power.

## Slide 57
Biomass
Electricity/heat
Wood/wood chips
Waste
Transport
Ethanol
corn
cellulose
Biodiesel

## Slide 59
Complications of ethanol
Fossil inputs to agriculture
Fertilizer and pesticide inputs
Low energy return on energy invested
Drives up price for food

## Slide 60
2014 cost per kilowatt by energy source

## Slide 61
Energy use in daily life
(Ecological Footprint – measuring your impact)
Household consumption
Transportation
Diet

## Slide 62
Household consumption
most energy use is from the BIG/LONG-TERM appliances
(one time opportunity):
Furnace
Air Conditioning
Refrigerator
Hot water heater
Lighting – use CFLs
Electronics

## Slide 63
Transportation
Increase fuel efficiency
Alternative/hybrid technology
Reduce number of trips
Reduce distance of trips
Use mass transit
LAND USE PLANNING

## Slide 64
Diet
Locally grown food
Less processed food
Organic food (less fossil energy inputs)
Eat lower on the food chain (less meat)
Less food waste

## Slide 65
TABLE 1. Global installed capacity in 2003 (MW)
Energy Future
Transition to Renewables
(cleaner and sustainable)
Increased Efficiency and Conservation in all sectors
Reduce need for transportation through wise development decisions

## Slide 66: Food, energy, water nexus
It takes energy and water to grow food
It takes water to produce energy
It takes energy to move and clean water
It takes food for the people provide food, water, and energy

## Slide 67
watershed
Watershed is all area that drains to a common point

## Slide 70: Food production and trade (YSSP Project by Nemi Vora, Univ. of Pittsburgh)
Trade can in(de)crease environmental impact of food production depending on trading partners
Physical food trade vs. virtual (embodied) resource trade
Notes: Food trade ensures food security, and gives us food diversity. SO, to account for these embodied impact, we talk about virtual trade. So, when you are importing food, you are also importing impacts associated with it.

## Slide 71: Building layered trade networks
C
A
B
C
A
B
C
A
B
 | A | B | C
A | 0 | 10 | 0
B | 0 | 0 | 5
C | 10 | 5 | 0
Example food trade matrix, flow in mass units from row to column
Food
flows
Irrigation water
Irrigation embodied energy
Irrigation embodied greenhouse gas (GHG)
emissions
C
A
B
Origin
Destination
Water | A | B | C
A | 0 | 8 | 0
B | 0 | 0 | 4
C | 7 | 4 | 0
Energy | A | B | C
A | 0 | 8 | 0
B | 0 | 0 | 2
C | 2 | 2 | 0
GHG Emissions | A | B | C
A | 0 | 15 | 0
B | 0 | 0 | 3
C | 14 | 7 | 0
Notes: Example data formulated as matrix, trade from row to column, directed graphs, layers
Cereal grains in USA:
95% of production is corn, Wheat sorghum, barley and oats, For oats, larger production.

## Slide 72: Actual trade vs. maximal indeterminacy
A.) Actual trade B.) Maximal Indeterminacy (zero dependency) - flow structure evenly redistributed given network flow constraints. Each visualization represents only flows that are at least 1% of the maximum link weight
A.)
B.)
Notes: Accounting for total transfers (a.k.a system structure) (Evenly re-distributed does not mean all states are trading equal volume, still account for total flow) But weighted by flow of total product to both nodes
Maximal indeterminancy
Importance of within-state flows reduced
  local consumption redistributed and reduced

## Slide 73: Trade dependencies for Texas
Texas largest out-of-state importer
Origin States | Food imports to Texas in (US tons) | Rank by trade flow | PMI | Rank by PMI
Texas | 2.9E+07 | 1 | 3.74 | 1
Kansas | 2.8E+07 | 2 | 2.24 | 2
Oklahoma | 2.3E+06 | 3 | 1.39 | 4
Nebraska | 1.4E+06 | 4 | -2.34 | 12
Louisiana | 9.9E+05 | 5 | 0.60 | 6
Missouri | 5.7E+05 | 6 | -1.63 | 7
Minnesota | 4.4E+05 | 7 | -3.79 | 22
Illinois | 2.9E+05 | 8 | -4.53 | 28
North Dakota | 2.4E+05 | 9 | -3.51 | 21
New Mexico | 1.9E+05 | 10 | 1.45 | 3
California | 1.6E+05 | 11 | -2.68 | 15
Georgia | 1.5E+05 | 12 | -1.83 | 8
Arkansas | 1.4E+05 | 13 | -2.86 | 16
Understanding Texas’s import dependencies
Lower PMI rank: Potential to increase trade
Notes: Flow ranks do not necessarily match with PMI ranks.
Another way of looking at PMI values is you are looking at direct trade transactions, you are not considering total flows/ potential of the trading partners in receiving and sending.
Flow ranks do not necessarily match with PMI ranks.

## Slide 74: Trade dependencies for Texas
Texas largest out-of-state importer
Origin States | Food imports to Texas in (US tons) | Rank by trade flow | PMI | Rank by PMI
Texas | 2.9E+07 | 1 | 3.74 | 1
Kansas | 2.8E+07 | 2 | 2.24 | 2
Oklahoma | 2.3E+06 | 3 | 1.39 | 4
Nebraska | 1.4E+06 | 4 | -2.34 | 12
Louisiana | 9.9E+05 | 5 | 0.60 | 6
Missouri | 5.7E+05 | 6 | -1.63 | 7
Minnesota | 4.4E+05 | 7 | -3.79 | 22
Illinois | 2.9E+05 | 8 | -4.53 | 28
North Dakota | 2.4E+05 | 9 | -3.51 | 21
New Mexico | 1.9E+05 | 10 | 1.45 | 3
California | 1.6E+05 | 11 | -2.68 | 15
Georgia | 1.5E+05 | 12 | -1.83 | 8
Arkansas | 1.4E+05 | 13 | -2.86 | 16
Understanding Texas’s import dependencies
Higher PMI rank: More dependent than expected
Notes: Flow ranks do not necessarily match with PMI ranks.
Another way of looking at PMI values is you are looking at direct trade transactions, you are not considering total flows/ potential of the trading partners in receiving and sending.
Flow ranks do not necessarily match with PMI ranks.

## Slide 75: PMI values for virtual water imports to Texas
Gravity model of trade
Notes: Concistent with trade models, known as gravity models that indicate distance enables trade.

## Slide 76
PMI for virtual water imports to Texas
The white states indicate no imports.
Size of circles represent total water withdrawals for irrigation.

## Slide 77
[1] Groundwater stress index from Gleeson, Tom, et al. "Water balance of global aquifers revealed by groundwater footprint." Nature (2012), GIS layer from world resource institute, Aqueduct
Virtual water import vulnerability of Texas
Ogallala aquifer
Groundwater stress index from ref [1]
Notes: GW stress: GF fotrpint per area
GF footprint: C/R-E: C: area averaged annual abstraction of GW, recharge rate= artificial recharge, groundwater contribution to environmental streamflows,in length per time,
Environmental flow: quantitiy of groundwater flow that needs to be allocated to surface water flow to sustain ecosystem services including vegetation, which is most important during flow conditions. A fraction of recharge allocated to environmental flow.

## Slide 78: PMI value for embodied GHG emissions

## Slide 79: Conclusions:
Energy is the basis for all actions and activities
Most of the energy we currently use is from non-renewable resources (coal, oil, natural gas)
Each energy source has a different target use
Transition to renewables will address environmental problems but will be difficult to scale to our current rate of use
Oil for transportation will be the most difficult to replace
We recognize better now the clear interdependencies between energy, food supply, and water use.

## Slide 80
THANK YOU FOR YOUR ATTENTION