## Slide 1
Practical training
in Histology
Physiotherapy (bc.)

## Slide 2: Organization issues
Beginning - strictly
Change your shoes - you cannot enter the hall with outdoor shoes (slippers)
Locker room – shoes, jackets, coats, bags etc. (use padlock)
Cell phone – switched off or in silent mode
Microscopic hall = laboratory
  – eating, drinking, smoking not allowed
  – students have to follow the instructions
  – academic misconducts or inappropriate behavior result in excluding
  from the lesson or course
Follow safety rules
You have dedicated working place
You are responsible for microscope, slide set, EM atlas

## Slide 3
Practical lesson
Introduction, presentation (demonstrated topic)
Your individual work = study of the slides, schematic but precise drawing of tissue structure, careful description. The result of your work is PROTOCOL in each practice.
Students come prepared for practices - programmes on pin-boards or dpt. webpage
Attendance
100% attendance
Substitution only in exceptional cases, after permissions from both the teacher of your group and the lesson where you plan to substitute
Make a protocol during substitution, let it check and sign by the chief teacher

## Slide 4
Registration of substitution:
Datum Jméno Ročník Skupina Č. praktika Č. místa Vyučující - podpis
Date Name Year Group Nr. of practice Nr. of place Teacher- signature
Each absence must be excused via study department and in IS (medical report from doctor,
Official invitation, etc. Is necessary).

## Slide 5
Protocols
you have to make paper protocols (no tablets, laptops)
A4 size, blank, without lines, according to the template
pencil handdrawings (no pen)
complete set of your protocols is required for getting the credits
the quality of the protocol is approved by your teacher’s signature at the end of practical lesson
Low-quality protocols cannot be approved and you have to substitute the respective practical lesson
Testing your knowledge
Credit test in the last practice of semester (20 questions – max. 20 points, result 12 – 20 points = P (passed), 0 – 11 N (not passed), one resit is possible.
Exam in exam period: 2 questions from histology topics of lectures and practices (marks A – F).
3 terms: 1 regular and 2 resits.

## Slide 6
The english form of protocol:
on www of department

## Slide 7
Credits
- 100% attendance
- complete set of signed protocols from all lessons
- Passed credit test (written in practice before the last)
End of practice:
- The practice is closed by teacher

## Slide 8
http://www.med.muni.cz/histology



protocol

## Slide 9
Recommended literature
+ Lectures
Protocols

## Slide 10: HISTOLOGY
structure and ultrastructure of normal cells and tissues,
cytology and general histology
special histology = microscopic anatomy of individual organs
relevance: oncology, surgery, hematology, pathology, forensic,…

## Slide 11: Histology
Resolution of naked eye – 0,1 mm
Resolution of light microscopy – 10 nm
Resolution of electron microscopy – 0,1 nm

## Slide 12: Tissue processing for the light microscopy (LM) (making of permanent preparations – slides)
SAMPLING (obtaining of material – cells, tissue pieces)
FIXATION of samples (tissue blocks)
RINSING (washing) of samples
EMBEDDING of samples - embedded blocks
CUTTING of blocks - sections
AFFIXING of sections
STAINING of sections
MOUNTING of sections

## Slide 13: SAMPLING
A small piece of organ (tissue) is sampled and quickly put into the fixative medium.
Biopsy during surgical dissection of organs in living organism
= excision
= puncture (liver or kidney parenchyma, bone marrow)
= curettage (uterine endometrium, adenoid vegetation)
Necropsy from dead individual (sections); in experiments laboratory animals are used and tissue have to be sampled as soon as possible after the break of blood circulation
The specimens shouldn't be more than 5 – 10 mm3 thick and fixation should follow immediately.

## Slide 14: FIXATION
Definition: denaturation and stabilization of cell proteins with minimum artifacts)
The reason of fixation: freshly removed tissues are chemically unstable – dry, shrink, undergo hypoxia, autolysis and bacteriological changes
To stop or prevent these changes and preserve the structure tissue samples have to be fixed. During the fixation, all tissue proteins are converted into inactive denaturized (stable) form.
3 main requirements on fixatives:
- good preservation of structure
- quick penetration into tissue block
- no negative effects on tissue staining

## Slide 15
Fixatives: solutions of different chemicals
- organic fixatives – ALDEHYDES – formaldehyde (most frequently used for LM)
– glutaraldehyde (used for EM)
– ALCOHOLS – 96 – 100 % (absolute) ethylalcohol
– ORGANIC ACIDS – glacial acetic acid, picric acid,
trichloracetic acid
- inorganic fixatives – INORGANIC ACIDS – chromic acid, osmium tetraoxide (OsO4)
– SALTS OF HEAVY METALS – mercuric chloride HgCl2
- compound fixatives – mixtures (two or more chemical components to offset
undesirable effects fo indiviual (simple) fixatives.
FLEMMING´s fluid – with OsO4
ZENKER´s and HELLY´s fluid, SUSA fluid – with HgCl2
BOUIN´s fluid – with picric acid
CARNOY´s fluid – with alcohol
Performance: fixatives are carried out at room temperature, the duration varies
between 12 – 24 hours, specimen must be covered by 20 – 50 times fixative volume:
Ratio of tissue block volume to fixative volume 1 cm3 : 20 – 50 cm3

## Slide 16: RINSING and EMBEDDING
All samples should be washed to remove the excess of fixative; the choice of rinsing medium is determined by type of fixative: running tap-water or 70-80% ethanol
Relevance of embedding: tissues and organs are brittle and unequal in density, they must be hardened before cutting

## Slide 17: Embedding media
water soluble – gelatine, celodal, water soluble waxes
anhydrous – paraffin, celoidin

## Slide 18
EMBEDDING into PARAFFIN
dehydration – to remove water from fixed samples by ascending series of ethanol is used (50%, 70%, 90%, 96%. each step - 2 – 6 hours
clearing – the ethanol must be replaced with organic solvatant that dissolves paraffin – benzene or xylene
infiltration – melted paraffin wax (56°C) is used; 3 x 6 hours.
casting (blocking out) – moulds (plastic, paper or metal chambers) are used for embedding.
The moulds are filled with melted paraffin, tissue samples are then placed inside and immediately immersed in cold water to cool paraffin quickly down.
These paraffin blocks are ready for trimming

## Slide 19
Automated device for tissue dehydration
Leica TP 1020

## Slide 20
Paper chambers
- metal

## Slide 21: CUTTING
Microtome – a machine with automatic regulation of section thickness: 5 – 10 μm is optimum.
sliding microtome – block is fixed in holder, knife or razor moves horizontally
rotary microtome – knife is fixed,
block holder moves vertically

## Slide 22
Rotary microtome
Sliding microtome

## Slide 23
Freezing microtome (cryostat)
= rotary microtome housed in freezing box
(– 60º C)
Cutting of frozen tissue without the embedding

## Slide 24
1
2
3
4
5
6
7
sampling
fixation
fixation
cutting
cutting
section affixing
section affixing

## Slide 27: AFFIXING
Mixture of glycerin and egg albumin or gelatin
Section are transferred from microtome razor or knife on the level of warm water (45º C), where they are stretched; then they are put on slides coated with adhesive mixture; excess of water is drained and slides are put in incubator (thermostat, 37º C) over night to affixing of sections.

## Slide 28
Stretching of sections on warm water
Stretching on a warm plate

## Slide 29: STAINING
Different cell or tissue structures are not apparent without staining.
Cellular structures exhibit different affinity to staining dyes
alkaline dyes (basic or nuclear) – react with anionic groups of cell and tissue components
basophilia – basophilic structures in the cell
acid dyes (cytoplasmic) – react with cationic groups
acidophilia – acidophilic structures in the cell
neutrophilia – no reaction

## Slide 30
Staining methods: routine – HE, AZAN
(demonstrate all components of tissue)
special
visualizes only special structures
impregnation
by silver salt for detection
of nerve or reticular fibers
HE – the most frequent used method
Lipid droplets
detected by oil red

## Slide 31: ROUTINE STAINING with HEMATOXYLINE – EOSIN (HE)
Hematoxyline – basic (nuclear) dye
Eosin – acid (cytoplasmic dye
Staining procedure:
paraffin must be removed (dissolved) by xylene
sections are rehydrated in descending series of ethanol (100% 96% 80%)
staining with hematoxyline
differentiation in acid ethanol and water (excess of dye is removed)
staining with eosin
rinsing in water (excess of dye is removed)
dehydration in graded ethanol series (80% 96% 100%)
clearing in xylene

## Slide 32
Xylen I Xylen II 100% 96% H2O hematoxyline acidic
ethanol ethanol ethanol
Xylen IV xylen III 100% 96% H2O eosin H2O
ethanol ethanol
HEMATOXYLINE – EOSIN (HE)
Deparaffination Rehydration Washing Staining Differentiation
Clearing Dehydration Washing Staining Washing

## Slide 33: Staining results:
HE = Hematoxyline – Eosin
nuclei – bright clear blue or dark violet
cytoplasm and collagen fibers – pink
muscle tissue – red
HES = Hematoxyline – Eosin – Safron
connective tissue – yellow
AZAN = AZocarmin – ANiline blue – orange G
nuclei – red
erythrocytes – orange
muscle – red
collagen fibers – blue

## Slide 34
cuvette
flask
slides holder
(basket)
Staining tools:

## Slide 35: Automatic slide stainer
staining set of boxes with media

## Slide 36: MOUNTING
Finally, preparates are closed with coverslip (coverglass) to form a permanent preparate. Small amount of mounting medium must be placed between stained section and the coverslip.
Mounting media: soluble in xylene – canada balsam soluble in water – glycerin-gelatine, arabic gum

## Slide 37
Permanent histological slides for study in the light microscope

## Slide 38: Hematoxyline and eosin (HE)

## Slide 39: Hematoxyline and eosin (HE)
cell cytoplasm
cell nuclei
collagenous
connective tissue

## Slide 40: Hematoxyline and eosin (HE)
basophilic cytoplasm
of glandular cells
(contains ribosomes
with RNA)
acidophilic cytoplasm
of epithelial cells

## Slide 41: Hematoxyline, eosin and saffron (HES)
cartillage
Collagenous fibers
of connective tissue
are yellow after staining
with saffron

## Slide 42: Azocarmine and aniline blue (AZAN)
Kidney – collagen connective tissue

## Slide 43: Impregnation of tissue with silver
Lien - reticular fibers
Cerebellum – nerve fibers

## Slide 44
Visit us at:
http://www.med.muni.cz/histology