Basic of Arteficial Ventilation
L.Dadak

---
Ventilator
O2
CO2
[Speaker Notes: The function of the ventilator is to help get oxygen into the patient and carbon dioxide out]

---
Ventilator
generates a controlled flow of gas into a patient’s airways. Oxygen and air are received from cylinders or wall outlets, the gas is pressure reduced and blended according to the prescribed inspired oxygen tension (FiO2), accumulated in a receptacle within the machine, and delivered to the patient using one of many available modes of ventilation.

---
Positive pressure ventilation
- gas flows along a pressure gradient between the upper airway and the alveoli.
  The magnitude, rate and duration of flow are determined by the operator.
- Flow is either volume targeted and pressure variable, or pressure limited and volume variable.

---
Mode of ventilation
- Control / assist
- Support
- Volume
- Pressure
SIMV = Synchronized Intermittent Mandatory Ventilation

---
Mode of vent.
- VCV = eliminate CO2
  - anesthesia
  - post-arrest
- PCV = lung problem
- PSV = weaning from ventilator

---
Getting oxygen in
Getting oxygen in
- Depends on
  - PAO2
    - FIO2
    - PACO2
    - Alveolar pressure
    - Ventilation
  - Diffusing capacity
  - Perfusion
  - Ventilation-perfusion matching
[Speaker Notes: Getting oxygen in is dependent on a number of factors. Some of these can be manipulated to a large extent by mechanical ventilation]

---
Carbon dioxide out
Carbon dioxide out
- Respiratory rate
- Tidal volume
- Deadspace
[Speaker Notes: Carbon dioxide elimination is dependent on the respiratory rate, tidal volume and ventilation perfusion matching]

---
Main determinants
Main determinants
Oxygen in
 FIO2
 mean alveolar pressure
PEEP
    - Re-open alveoli and  shunt
Carbon dioxide out
 ventilation
  RR
  tidal volume
[Speaker Notes: In summary, the most important means of improving oxygenation are increasing the inspired concentration of oxygen, increasing the mean airway and therefore the mean alveolar pressure and applying PEEP to re-open alveoli. Carbon dioxide removal can be increased by increasing the respiratory rate or tidal volume]

---
Mean airway pressure
Mean airway pressure
Time
Time
Mean airway pressure
Mean airway pressure
Pressure
Pressure
Peak Pressure
[Speaker Notes: Airway pressure can be increased in a number of ways. It is easier to understand why these methods increase mean pressure if one remembers that the mean airway pressure refers to the mean across the entire respiratory cycle, both inspiration and expiration. The most obvious method of increasing the pressure is to increase the tidal volume but this will also increase the peak and plateau airway pressures and therefore increase the chance of ventilator induced lung injury.]

---
Mean airway pressure
Time
Time
Mean airway pressure
Mean airway pressure
Pressure
Pressure
Peak Pressure
[Speaker Notes: Prolonging the inspiratory time increases the mean pressure without increasing the peak pressure]

---
Inspiratory time
Inspiratory time
- Set as:
  - % of respiratory cycle
  - I:E ratio
- Expiratory time not set
  - Remaining time after inspiration before next breath
[Speaker Notes: It can be set as a percentage of the respiratory cycle or as a ratio of inspiration to expiration, the so called I:E ratio. Note that on most ventilators the expiratory time is not set directly but is merely the remaining time after inspiration before the next breath]

---
Inspiratory time
- Increased inspiratory time
  - Improved oxygenation
  - Unnatural pattern of breathing
    - Deeper sedation
  - Increased risk of gas trapping
[Speaker Notes: Although increasing the inspiratory time may improve oxygenation inspiratory times of >30% or I:E ratios of >1:2 are often uncomfortable for the patient resulting in a need for a deeper level of sedation. In addition less time is available for expiration resulting in an increased risk of gas trapping.]

---
Mean airway pressure
PEEP
Time
Time
Mean airway pressure
Mean airway pressure
Pressure
Pressure
[Speaker Notes: Finally increasing the positive end-expiratory pressure or PEEP will increase the mean pressure but may also increase the peak and plateau pressures.]

---
PEEP
PEEP
Improves oxygenation
    -  mean alveolar pressure
    -  shunting
[Speaker Notes: However PEEP has the major advantage that it may decrease shunting by re-opening alveoli.]

---
Other settings
Other settings
Trigger sensitivity
 sensitivity preferable
Flow triggering general more sensitive than pressure triggering
 flow or  pressure   sensitivity
[Speaker Notes: The trigger sensitivity determines how easy it is for the patient to trigger the ventilator to deliver a breath. In general increased sensitivity is preferable in order to improve patient-ventilator synchrony (ie to stop the patient "fighting" the ventilator) but excessively high sensitivity may result in false or auto-triggering (ie ventilator detects what it "thinks" is an attempt by the patient to breath although the patient is apnoeic). Triggering may be flow-triggered or pressure triggered. Flow triggering is generally more sensitive. The smaller the flow or the smaller the negative pressure the more sensitive the trigger]

---
Other settings
Rise time
Rise time
Inspiratory time
Inspiratory time
Time
Time
Pressure
Pressure
[Speaker Notes: The rise time determines speed of rise of flow (volume control mode) or pressure (pressure control and pressure regulated volume control modes). Very short rise times may be more uncomfortable for the patient. Long rise times may result in a lower tidal volume being delivered or higher pressure being required.]

---
Respiratory complications
Respiratory complications
- Nosocomial pneumonia
- Barotrauma
- Gas trapping
[Speaker Notes: Respiratory complications of mechanical ventilation include nosocomial pneumonia, barotrauma and gas trapping]

---
Barotrauma
Barotrauma
- High pressures (barotrauma)
- High volumes (volutrauma)
- Shear injury
[Speaker Notes: Barotrauma is actually a misnomer because ventilator associated lung injury is thought to be due to due to high volumes and shear injury as well high pressures. Shear injury is the result of repetitive collapse and re-expansion of alveoli and due to tension at the interface between open and collapsed alveoli]

---
Gas trapping
Gas trapping
[Speaker Notes: Gas trapping occurs if there is insufficient time for alveoli to empty before the next breath]

---
Gas trapping

---
Gas trapping

---
Gas trapping

---
Gas trapping

---
Gas trapping

---
Gas trapping

---
Gas traping

---
Gas trapping
- Predisposing factors:
  - asthma or COPD
  - long inspiratory time ( expiratory time short)
  - high respiratory rate ( absolute expiratory time short)
- Effects
  - progressive hyperinflation of alveoli
  - progressive rise in end-expiratory pressure (intrinsic PEEP)
[Speaker Notes: It is more likely to occur in patients with asthma or COPD, when inspiratory time is long (and therefore expiratory time short) or when respiratory rate is high and therefore the absolute expiratory time short. Gas trapping results in progressive hyperinflation of alveoli and a progressive rise in end-expiratory pressure (as this increase in PEEP is not due to an increase in set PEEP it is known as intrinsic PEEP)]

---
Intrinsic PEEP (PEEPi)
Intrinsic PEEP (PEEPi)
size 12{"PEEP" size 8{i} =" PEEP" size 8{"tot"}"-PEEP" size 8{e}} {}
PEEPtot
PEEPe
Time
Pressure
[Speaker Notes: Intrinsic PEEP can be measured on most ventilators by using the expiratory pause hold control. As the pressures in the respiratory system equilibrate the expiratory pressure measured by the ventilator rises. This occurs after a few seconds. The pressure displayed is the total PEEP. Intrinsic PEEP is obtained by subtracting the set or extrinsic PEEP from the total PEEP.]

---
Gas trapping
- Adverse effects
  - Barotrauma
  - Cardiovascular compromise
[Speaker Notes: Adverse effects include barotrauma and cardiovascular compromise due to high intrathoracic pressure. In an extreme case this can lead to cardiac arrest with pulseless electrical activity.]

---
Cardiovascular effects
Cardiovascular effects
- Preload
  - positive intrathoracic pressure reduces venous return
  - exacerbated by
    - high inspiratory pressure
    - prolonged inspiratory time
    - PEEP
[Speaker Notes: Preload is reduced. This is predominantly due to reduced venous return. Normally venous return is enhanced by the negative intrathoracic pressure during inspiration. Not only is this abolished by positive pressure ventilation but venous return is actually impeded by the positive intrathoracic pressures. This effect will by exacerbated by any factors that increase the mean intrathoracic pressure such as high inspiratory pressures, prolonged inspiratory times and the application of PEEP.]

---
Cardiovascular effects
decreased afterload due to decreased LV transmural pressure
size 12{"T "= { {P size 8{"tm"}" x R"} over {"2H"} } } {}
[Speaker Notes: LV afterload is directly related to LV transmural pressure]

---
Cardiovascular effects
decreased afterload due to decreased LV transmural pressure
size 12{P size 8{"IC"}" - P" size 8{"pl"}} {}
size 12{"T "= { {P size 8{"tm"}" x R"} over {"2H"} } } {}

---
Cardiovascular effects
Overall effect depends on whether ventricular contractility is normal or abnormal
 contractility
(/)  cardiac output
normal contractility
 cardiac output

---
Hypotension
Hypotension
- Consider
  - Drug induced
  - Gas trapping
  - Tension pneumothorax
[Speaker Notes: If the patient becomes hypotensive shortly after intubation and ventilation the most likely causes are drug induced hypotension due to the vasodilating properties of anaesthetic induction agents, gas trapping due to over-enthusiastic ventilation and tension pneumothorax. Drug induced hypotension usually responds to fluid loading. If gas trapping is suspected disconnect the patient from the ventilator. As the trapped gas is released the hypotension will resolve, usually within 30-60 seconds. A tension pneumothorax is rare but the possibility should be considered as it is easily treated and failure to diagnose it may be fatal. Treatment is by needle thoracostomy.]