## Slide 1
Cardiac action potential and underlying ionic currents
Methods, physiology and selected pathologies
Assoc. Prof. MUDr. Markéta Bébarová, Ph.D.
The presentation was created with the support of the FRMU project „Modernization of teaching of cardiac cellular electrophysiology“, MUNI/FR/1490/2018.

## Slide 2
1:Ganong´s Review of Medical Physiology, 23rd edition
1
Notes: Jak je obecně známo, podkladem fyziologicky probíhající mechanické aktivity srdce je adekvátně utvářená aktivita elektrická. Srdeční svalové buňky jsou jedním z typů vzrušivých tkání. Jsou tedy schopné na stimulaci reagovat vznikem akčního napětí, které se šíří srdeční svalovinou a umožní její následnou kontrakci vedoucí k vypuzení krve ze srdce do krevního oběhu.
Elektrická aktivita srdce vzniká a na pracovní myokard se šíří prostřednictvím srdečního převodního systému. Obrazem elektrické aktivity na úrovni jednotlivé srdeční buňky je akční napětí. Jeho konfigurace se zásadním způsobem liší v buňkách převodního systému a v buňkách pracovní svaloviny srdce a rovněž pak v rámci samotné pracovní svaloviny náležící k různým srdečním oddílům a vrstvám.
Odlišná konfigurace akčního napětí je podmíněna odlišným zastoupením a aktivitou jednotlivých iontových membránových proudů. Pro správné utváření akčního napětí je klíčová dokonalá souhra těchto proudů. Narušení funkce prakticky kteréhokoliv z iontových kanálů a tedy změna kteréhokoliv z iontových proudů pak může vést ke vzniku proarytmogenního stavu.

## Slide 3
1: http://tmedweb.tulane.edu/tmedwiki/doku.php/intro_to_the_heart_cardiac_electrophysiology
1
1
Notes: Fáze AN.
Iontový podklad AN. Význam souhry jednotlivých proudů pro správné utváření AN.
Tyto iontové proudy, tedy proudy nesené ionty, které jsou hydrofilními a tedy lipofobními částicemi, tečou přes buněčnou membránu přes speciální proteiny přemosťující buněčnou membránu, tzv. iontové kanály.

## Slide 4
Ionic Channels
1
1:Despopoulos, Color Atlas of Physiology, 2003
1
Notes: Iontové kanály – typ pasivního transportu, po elektrochemickém gradientu.
Různé typy iontových kanálů. Vrátkování.

## Slide 5
Impact of Knowledge on Electrical Properties
of Cardiac Cells for Clinical Medicine
1
Inherited Arrhythmogenic Syndromes
Acquired Arrhythmogenic Syndromes
On a base of other primary cardiac diseases
Side effects of drugs
Effects of other substances including addictive drugs
Sudden Cardiac Death
Mechanisms of Action of Antiarrhythmic Drugs

## Slide 6
Electrophysiological Methods in Cardiology
On the level of whole organism
  Example: ECG
On the level of the heart
  Example: Intracardiac ECG
On the isolated heart
  Example: Langendorff heart perfusion
On the multicellular cardiac samples
On the isolated cardiomyocytes
    Example: Whole cell patch clamp
  On the single membrane channels
    Example: Single channel patch clamp
Measurements could be performed:
1
Zipes D. and Jalife J. ; Cardiac Electrophysiology: From Cell To Bedside, 2003

## Slide 7
On the level of whole organism
  Example: ECG
On the level of the heart
  Example: Intracardiac ECG
On the isolated heart
  Example: Langendorff heart perfusion
1
Basic principle of methods:
We measure the potential difference between two points
  of a volume conductor
Measured quantity voltage.
Recorded signals represent a sum of contributions of electrical activities
  of individual cells of the organ during propagation of excitation.
Electrophysiological Methods in Cardiology
Measurements could be performed:

## Slide 8
1
On the multicellular cardiac samples
On the isolated cardiomyocytes
    Example: Whole cell patch clamp
  On the single membrane channels
    Example: Single channel patch clamp)
Basic principle of methods:
We measure membrane voltage, which is the difference between
  the extracellular and intracellular medium, or membrane current.
Electrophysiological Methods in Cardiology
Measurements could be performed:

## Slide 9
Basic principle of measurements
on various levels of organism

## Slide 10
Electrocardiography
1
We record voltage and
its changes over the time.
EKG
V [mV]
t [s]
1:http://www.cndajin.com/group/human-figure-outline/#photo_2
1

## Slide 11
1
Adopted from Malmivuo, J., Plonsey, R., 1995. Bioelectromagnetism: principles and applications of bioelectric and biomagnetic fields. Oxford University Press, New York
Mechanism of impulse creation:
Electrocardiography

## Slide 12
1
Adopted from Malmivuo, J., Plonsey, R., 1995. Bioelectromagnetism: principles and applications of bioelectric and biomagnetic fields. Oxford University Press, New York
Mechanism of impulse creation:
Electrocardiography

## Slide 13
Intracardiac electrocardiography
1
1: http://www.medicalexpo.com/prod/osypka/product-111576-879783.html; 2: http://www.drjohnm.dreamhosters.com/wp-content/uploads/2010/12/EPS-Teal_3.jpg
An invasive method, routinely used in clinical practice
Basic principle:
  A multipolar catheter is inserted into the heart. It is positioned in close proximity
  along the conduction system. The signal is registered from the tip of the catheter.
1. Multipolar catheter
2. Intracardial position of the catheter with the example
of recorded signal

## Slide 14
1
We can measure:
Function of sinus node
Conduction thorugh the atrial wall
Conduction in atrioventricular node
Conduction through Hiss bundle
Conduction through Purkinje fibers
Hiss bundle electrogram
A
H
V
SA
AV
EKG
EHS
PQ
QRS
A
H
V
PQ segment
A
V
P
The interpretation of recorded signal
Intracardiac electrocardiography
PA
HV
AH

## Slide 15
1
An experimental methos
The heart is placed in the Langendorff perfusion set:
LW
RV
aorta →
Principle of the retrogarde perfusion
direction of flow of the solution
close aortic valve
empty ventricles
perfusion through the coronary artery
1: https://www.adinstruments.com/research/animal/cardiovascular/isolated-heart-systems/langendorff
1
Measuremt on the isolated heart

## Slide 16
Measurement is performed by:
electrodes embedded in walls of the bath
reference electrode
Epicardial suction electrode
Electrogram
Monophasic action potential
[mV]
Measuremt on the isolated heart

## Slide 17
Glass microelectrode
Ag/AgCl electrode
Reference Ag/AgCl electrode
Glass microelectrode
Set-up
Measurement on multicullular cardiac samples

## Slide 18
A stimulation of the sample is needed for the measurement
It could be performed in two modes:
Im
Um
Ic
Ic
Im
Um
ICa-L
INa
Ito
IK, IK1
Stimulation
Recorded signal
current clamp mode
voltage clamp mode
Measurement on multicullular cardiac samples

## Slide 19
Patch-clamp
Both whole cell patch-clamp and single channel patch-clamp require
  an isolated cardiac cells.
By the successful dissociation, we obtain a sufficient fraction of viable,
  funtionally undamaged cells responding to electrical stimulation by:
  Contraction
  Characteristic electrical activity (action potential and membrane currents)

## Slide 20
Patch-clamp
Enzymatic isolation of cardiac cells:

## Slide 21
Possibilities of using patch-clamp
Isolated cardiac cells
Cell lines transiently expressing
  human ionic channels
Measurements could be performed on:
Induced pluripotent stem
  cell-derived cardiac cells
  (iPSC-CM)

## Slide 22
Patch-clamp
Establish a contact with a cell
Whole cell patch-clamp

## Slide 23
Measurement on a single cell
Two mode of measurement:
Voltage clamp
Current clamp
Patch-clamp
Whole cell patch-clamp

## Slide 24
Glass microelectrode
[pA]
Membrane patch with single channel
Current flowing through single channel in response to imposed voltage pulse
Patch-clamp
Single channel patch-clamp

## Slide 25
5 µM ACh
50 μM ACh
Single channel current at -110 mV induced by acetylcholine at rat neuromuscular junction (nicotinic receptors; Mulrine and Ogden)
Glass microelectrode
Membrane patch with single channel
Patch-clamp
Single channel patch-clamp

## Slide 26
Ionic channel gating under physiological and pathological conditions
  Example: Changes of cardiac ionic currents in failing heart
Drug effects on ionic channels
  Example: Describing the pro-arrhythmogenic properties of certain drugs, i.e.:
          Effect of antiarrhythmic drug ajmaline on action potential and on IK(ATP)
          Effect of antipsychotic drug perphenazine on INa and Ito
          Effect of ethanol on IK1
          Effect of anidepressant nefazodone on IKr
Impact of a mutation on drug effects on a channel
Ionic channel dysfunction caused by a mutation
  Example: Analysis of arrhythmogenic syndromes:
          Long QT syndrome
          Brugada syndrome
We can analyse:
1
Possibilities of using patch-clamp

## Slide 27
          Example: Effect of antiarrhythmic drug ajmaline on action potential
CONTROL
AJMALINE
WASH-OUT

## Slide 28
          Příklad: Vliv antiarytmika ajmalinu na IK(ATP)
Control
After DNP
aplication
240 mV
3 nA
50 ms
IK(ATP)
Měření IK(ATP)
Voltage
clamp
impulse
Recorded current

## Slide 29
          Example: Effect of antiarrhythmic drug ajmaline on IK(ATP)
Recorded current
Changes after
ajmaline
aplication
240 mV
Measurement of IK(ATP)
IK(ATP) in control
IK(ATP) after ajmaline aplication
Voltage
clamp
impulse
Kontrola

## Slide 30
1:Bébarová et al. (Naunyn Schmied Arch Pharmacol 2009; 380:125-133); 2: http://tmedweb.tulane.edu/tmedwiki/doku.php/intro_to_the_heart_cardiac_electrophysiology
1
2
INa
Ito
          Example: Effect of antipsychotic drug perphenazine on INa and Ito

## Slide 31
          Example: Effect of antidepressant nefazodone on IKr
Measurement was performed on
  Induced pluripotent stem cell-derived
  cardiac cells
Inhibition of IKr
  by nefazodone
Work about nefazodonueis from Lee et al., Toxicol Appl Pharmacol 2016; 296: 42-53; 1: Jouni et al., J Am Heart Assoc 2015; 4: e002159
1
Notes: Odkaz na TZKM
Možnost modelovat dědičné arytmie
Inhibice Ikr antidepresivem druhé generace nefazodonem (množící se zprávy o jeho proarytmogenní aktivitě)

## Slide 32
          Example: Brugada syndrome
Adopted from Bébarová et al. , Am J Physiol Heart Circ Physiol 2008; 295:H48-H58
clinical symptoms: syncope
ECG: ST elevation
P wave = 80 ms (120 ms)
QRS complex = 135 ms (100 ms)
QTc interval = 382 ms (440 ms)
AH = 109 ms (160 ms)
HV interval = 56 ms (50 ms)
COOH
NH2
Missence mutation in C-terminus INa channel
F2004L

## Slide 33
Measurement was performed on cell line transiently expressing human
  wild-type and mutated (F2004L) INa channel
Inhibition of INa in mutated channel
F2004L
Adopted from Bébarová et al. , Am J Physiol Heart Circ Physiol 2008; 295:H48-H58
          Example: Brugada syndrome

## Slide 34
Kinetic scheme of INa channel
d
Development of slow
inactivation
Development of closed state inactivation
Adopted from Bébarová et al. , Am J Physiol Heart Circ Physiol 2008; 295:H48-H58
          Example: Brugada syndrome

## Slide 35
Schematic model
Adopted from Bébarová et al. , Am J Physiol Heart Circ Physiol 2008; 295:H48-H58
          Example: Brugada syndrome

## Slide 36
Adopted from Bébarová et al. , Am J Physiol Heart Circ Physiol 2008; 295:H48-H58
          Example: Brugada syndrome
Schematic model

## Slide 37
The presentation was created with the support of the FRMU project „Modernization of teaching of cardiac cellular electrophysiology“, MUNI/FR/1490/2018.