## Slide 1: ECG – Electrocardiography
Practical Exercises in Physiology (Spring semester: 4th - 6th weeks)

## Slide 2: Electrocardiography
Definition: recording the cardiac electrical activity from the surface of the body (el. heart activity can also be obtained from the esophageal leads or the heart surface itself, but these methods are used by other names)

## Slide 3: Cardiac conduction system
Purkynje fibers
Sinoatrial node (SA)
Atrial preferential ways
Atrioventricular node (AV)
His bundle
Tawara (bundle) branches
SA node
Atrial myocyte
AV node
His bundle
Tawara branches
Purkynje fibers
Ventricular myocyte

## Slide 4: Cardiac conduction system
Function: AP formation and preferential conduction
The atriums are separated from the chambers by a non-conductive fibrous septum - the only way is through the AV
  Sinoatrial node (SA) - natural frequency 100 bpm (mostly under parasympathetic damping effect), conduction velocity 0.05 m/s
  Preferred internodal atrial ways - conduction velocity 0.8 - 1 m / s
  Atrioventricular node - single conductive connection between atria and ventricles, natural frequency 40 - 55 bpm, conduction velocity only 0.05 m / s (nodal delay)
  His bundle – conduction velocity 1–1,5 m/s
  Tawara (bundle) branches – conduction velocity 1–1,5 m/s
  Purkynje fibers – conduction velocity 3–3,5 m/s
Sinus rhythm - AP starts at the SA node
Junction rhythm - AP is formed in the AV node or His bundle
Tertiary (ventricular) rhythm - AP is formed in bundle branches or Purkynje fiber
Ventricular myocardial activation - from inside to outside, markedly synchronized, determined by the onset of excitement
Repolarization of ventricular myocardium - in the opposite direction, less sharp, repolarization isles
Note: natural frequency is the frequency of AP formation unaffected by neural and hormonal control
natural frequencies of 20 - 40 bpm, they have slow spontaneous depolarization

## Slide 5: Electric dipole
Electrode: records electrical potential (Φ)
Electrical lead: connection of two electrodes
  It records the voltage between the electrodes
  Voltage: difference of el. potentials (V= Φ1- Φ2)
electrode
lead
Φ1
Φ2

## Slide 6: Einthoven triangle (standard, limb, bipolar leads)
Bipolar leads: both electrodes are active (variable electrical potential)
Electrode colors: R: red, L: yellow, F: green
I
II
III
R
L
F

## Slide 7: Goldberger leads (augmented, limb, unipolar leads)
Unipolar leads: one electrode is active (variable electric potential) and the other is inactive (constant electric potential, usually 0 mV)
The active electrode is always positive
aVF
aVL
avR
R
L
F

## Slide 8: Wilsonova central terminal (W)
It is formed by the connection of limb electrodes through resistors
electrically represents the center of the heart (it is actually led out or it is calculated)
Inactive electrode (constant potential)
Central terminal
-
+
+
+
-
Real central terminal

## Slide 9: Chest leads
Chest lead: connection of chest electrode and central terminal
Unipolar leads: chest electrode is active (positive) and central terminal is inactive (0 mV potential)
1
2
3
4
5
6
hrudní elektroda

## Slide 10: Leads according to Cabrera
I
aVF
II
III
aVR
aVL
–
+
–
+
+
+
+
+
–
–
–
–
120°
90°
60°
30°
0°
-30°
+
-
+
R
L
F
aVR
-
+
-
+
aVL
aVF
–
–
+
+
–
I
III
II

## Slide 11: Analysis of ECG
Heart action
Heart rhythm
Heart rate
Waves, segments and intervals
  P wave
  PQ interval
  QRS complex
  ST segment
  T wave
  QT interval
Electrical heart axis
P
Q
R
S
T
Atrial depolarization
Ventricular depolarization - QRS
Ventricular repolarization
Svod II

## Slide 12: Analysis of ECG
A millimeter grid of paper will help in fast analysis
See the paper speed (here 25 mm / s)v
  How many ms is one mm?
  It is good to know how much mV is one mm

## Slide 13: 1) Heart action
Regularity of distances between QRS complexes - RR intervals
Calculate difference: RR – mean RR (you only need to choose the shortest and longest RR in the record)
Regular action: difference < 0,16 s
Irregular action: difference > 0,16 s
  Usually pathological
  Beware of significant sinus respiratory arrhythmia - it is very physiological. If you are unsure, ask the patient to hold their breath during recording
Note: if one extrasystole is present, but otherwise the action is regular, it is called regular
RR

## Slide 14: 2) Heart rhythm
Heart rhythm is determined by the source of action potentials that lead to ventricular depolarization ventricular depolarization is crucial, because it determines cardiac output
Sinus rhythm
  AP begins in SA node
  On ECG: present P wave (atrial depolarization) before QRS
Junction rhythm
  AP begins in AV node or His bundle, the frequency is usually 40-60 bpm
  P wave is not before QRS, QRS is normal (narrow)
  Heart rate is low (40-60 bpm)
  Atrial depolarization can be present in the ECG if the ventricular impulses are transferred to the atria - wave is after QRS and has opposite polarity because it runs in opposite direction
  Tertial (ventricular) rhythm
  AP begins in other parts of the conduction system, frequency 30-40 bpm
  QRS has a strange shape (wider), because it spreads in a non-standard direction in the ventricles

## Slide 15: 2) Srdeční rytmus
Sinusový rytmus – před každým QRS je přítomna vlna P – vzruch začíná v SA uzlu, ne na něj navázaná depolarizace komor
Junkční rytmus – nejsou přítomné normální vlny P před QRS – vzruch začíná v AV uzlu nebo Hisově svazku, nízká srdeční frekvence, ale normální QRS (v komoře se vzruch šíří normálně)
Terciální (komorový) rytmus – nejsou přítomné vlny normální P vázané na QRS, vzruch začíná někde v komorách – deformované QRS, hodně nízká srdeční frekvence, například AV blok III. stupně
AV blok III. stupně – komory si jedou terciální rytmus, síně si jednou svůj rychlejší rytmus určený SA uzlem, který se ale nepřevádí do komor
P – depolarizace síní
repolarizace síní
zpětná depolarizace síní
nebo

## Slide 16: 3) Heart rate (HR)
Frequency of ventricular contraction (because it determines cardiac output); on ECG - frequency of ventricular depolarizations
HR = 1 / RR bpm
Physiological: 60 - 90 bpm at rest
Tachycardia: > 90 bpm in rest
  Can be sinus (increase sympathetic aktivity, medication, …)
  Tachyarrhythmias: rhythm is not sinus
Bradycardia: < 60 bpm
  Can be sinus (increase sympathetic aktivity, sport heart - physiological)
  HR < 50 bpm, rhythm probably is not sinus

## Slide 17: 4) Waves, segments, intervals
Name | Norm
wave P | 80 ms
interval PQ (PR) | 120-200 ms
segment PQ (PR) | 50-120 ms
Q | -
complex QRS | 80-100ms
R | -
S | -
segment ST | 80-120 ms
interval QT | < 420ms
wave T | 160 ms
P
R
T
Q
S
P wave
PQ interval
PQ segment
QRS complex
ST segment
T wave
QT interval
Bazett´s formula:
QT depends on RR interval – correction of QT on RR

## Slide 18: 4) Waves, segments, intervals
name | Place and description | Physiological bacground | Norm
wave P | First round wave (negative or positive) | Atrial depolarization | 80 ms
Interval PQ (PR) | Interval from beginning of P to beginning of Q (or R, if Q is not present) | Time interval from SA node activation to the Purkynje fibers activation | 120-200 ms
segment PQ (PR) | From P wave end to beginning of Q (or R, if Q is not present) | Complete atrial depolarization, AP transfer from AV to ventricles | 50-120 ms
Q | First negative deflection | Depolarization of septum and papilar muscles | -
complex QRS | From beginning of R to end of S | Ventricular depolarization | 80-100ms
R | Positive deflection | Main ventricular depolarization | -
S | Negative deflection after positive deflection. |  | -
segment ST | Interval of isoelectric line between end of QRS and beginning of T wave | Complete depolarization of ventricles | 80-120 ms
Interval QT | From beginning of Q (or R) to the end of wave T | Electrical systole | < 420ms
wave T | Second round wave (negative or positive) | Ventricular repolarization | 160 ms

## Slide 19: 4) Waves
Wave P:
Is present?
Is positive/negative, one-peak/two-peak, high(>0,25mV)/normal/low?
QRS:
  Q: first negative deflection
  R: first positive deflection
  S: negative deflection after positive deflection
small deflection (pod 0,5 mV) – small letter
Strong deflection – capital letter
Second positive deflection (‘)
Wave T:
Is positive/negative/bipolar?
Does it have the same polarity as the strongest QRS deflection?
  Yes: concordant (ok), No: discordant (pathology)
Bipolar T:
  Preterminal negative (-/+)
  Terminal negative (+/-)
P
Q
R
S
T
Atrial depolarization
Ventricular depolarization - QRS
Ventricular repolarization
Lead II
RS
Examples:
qRs
rSr‘

## Slide 20: 5) Electrical heart axis
Electrical heart axis: average direction of the electric heart vector during ventricular depolarization (QRS complex) (can also be determined for atrial depolarization: P, or ventricular repolarization: T, but in practice we will analyse ventricular depolarization)
I
aVF
II
III
aVR
aVL
–
+
–
+
+
+
+
+
–
–
–
–
120°
90°
60°
30°
0°
-30°
Heart axis is physiologically directed down, left, back - refers to the real placement of the heart in the chest.
- Here we solve only the frontal plane (limb leads)
Physiological range:
Middle type 0° – 90°
Left type -30° - 0°
Right type 90° - 120°
Pathological range:
Right deviation: > 120 ° (P ventricular hypertrophy, dextrocardia)
Left deviation: < -30° (L ventricular hypertrophy, pregnancy, obesity)
El. heart axis
vectocardiogram
the axis is also changed when Tawara branches are blocked or after IM, missing el. activity of part of chambers

## Slide 21: Electrical heart axis - evaluation
Calculate the sum of QRS oscillations in leads I, II, III. When the oscillation is down, it is negative. When the oscillation is up, it is positive. Use a millimeter grid
  Lead I: QI=-1; RI=6; SI=0; QRSI=5
  Lead II: QII=-1; RII=17; SII=-1; QRSII=15
  Lead IIII: QIII=0; RIII=10; SIII=-1; QRSIII=9
Because the el. axis is related to ventricular depolarization in the frontal plane, use QRS in limb leads: I, II, III.

## Slide 22: Electrical heart axis - evaluation
Draw the Einthoven Triangle with Goldberger augmented Leads
Mark the angles around the triangle (in the circle)
Lead I:
  0 at lead I is in the center of lead
  QRSI = 5, so from 0, measure 5mm towards the positive electrode, make a mark (or any other units, ratio is important)
  If the sum of QRS is negative, you will go towards the negative electrode
  Run a line from the mark perpendicular to the I lead (parallel to the aVF lead)
0°
30°
60°
90°
-30°
120°
I
II
III
–
+
–
–
+
+
0
0
0
15
9
5

## Slide 23: Electrical heart axis - evaluation
Lead II:
  0 at lead II is again in the center of lead
  QRS II = 15, so from 0, measure 15 mm towards the positive electrode, make a mark (again, if the sum of QRS is negative, you will go towards the negative electrode)
  Run a line from the mark perpendicular to the II lead (parallel to the aVL lead)
0°
30°
60°
90°
-30°
120°
I
II
III
–
+
–
–
+
+
0
0
0
15
9
5

## Slide 24: Electrical heart axis - evaluation
Lead III:
  The same way draw line for QRS III = 9
  Draw an arrow that starts at the center of the triangle and passes the cross of the drawn lines
This arrow shows the direction of the cardiac electrical axis in the frontal plane
Note. logically, only lines from two leads are sufficient
0°
30°
60°
90°
-30°
120°
I
II
III
–
+
–
–
+
+
0
0
0
15
9
5
The cardiac electrical axis for ventricular depolarization in the frontal plane is 70 °

## Slide 25: Diagnostické využití EKG
Arytmie: porucha srdečního rytmu
síňová fibrilace
(chybí P, „zubatá“ izolinie, RR nepravidelné, frekvence 80 – 180 bpm)
komorová fibrilace
(srdce nefunguje jako pumpa, poškození mozku po 3 – 5 minutách fibrilace)
https://upload.wikimedia.org/wikipedia/commons/thumb/6/64/Afib_ecg.jpg/400px-Afib_ecg.jpg http://www.qureshiuniversity.com/Ventricular%20Fibrillation.gif
https://ekg.academy/ekgtracings/313.gif
Fibrilace: nesynchronizovaná aktivita kardiomyocytů
fibrilace
normal
AV blok I. stupně (prodloužení převodu vzruchu ze síně na komory, prodloužený PQ int.)
Atrioventrikulární blokáda: porucha převodu vzruchu ze síní na komory
(některé vzruchy se nepřevedou: výskyt P, po kterých nenásleduje QRS)
AV blok II. stupně
AV blok III. stupně
Kompletní blokáda převodu vzruchů ze síní na komory, P a QRS se objevují nesynchronizovaně
P
P
P
P
P
P

## Slide 26: Diagnostické využití EKG
ischemie srdce, infarkt myokardu
A
B (elevace ST)
elektrolytová nerovnováha - hyperkalémie

## Slide 27: Diagnostické využití EKG
24-hodinové monitorování EKG (Holter)

## Slide 28: Dodatek k EKG

## Slide 29: Svod II a aVR
Všimněte si vzhledu EKG ve svodu II a aVR. Oba svody se dívají na elektrickou srdeční aktivitu z podobného úhlu (odchylka jen 30°), ale aVR má opačnou polaritu (dívá se na srdce vzhůru nohama v porovnání s II).
Proto jsou svody II a aVR podobné, jen vůči sobě zrcadlově obrácené.
aVR má obvykle negativní T a P
Díky jinému vzhledu má QRS v aVR a II svodu různý zápis.
qRs
rSr‘
I
aVF
II
III
aVR
aVL
–
+
–
+
+
+
+
+
–
–
–
–
120°
90°
60°
30°
0°
-30°

## Slide 30: QRS ve svodech a el. osa
Q = -1
R = 6
S = 0
QRS = 5
Q = -1
R = 17
S = -1
QRS = 15
Q = 0
R = 10
S = -1
QRS = 9
Q = 1
R = -11
S = 0
QRS = -10
Q = 0
R = -3
S = 0
QRS = -3
Q = -1
R = 13
S = -1
QRS = 11
qR
qRs
qRs
rSr‘
qr‘
qRs
Zápis QRS
součet výchylek QRS
výchylky QRS
Pro zjednodušení výpočtu výchylek je Q první kmit, R druhý kmit a S třetí kmit

## Slide 31
Q = -1
R = 6
S = 0
QRS = 5
Q = -1
R = 17
S = -1
QRS = 15
Q = 0
R = 10
S = -1
QRS = 9
Q = 1
R = -11
S = 0
QRS = -10
Q = 0
R = -3
S = 0
QRS = -3
Q = -1
R = 13
S = -1
QRS = 11
součet QRS
výchylky QRS
Elektrická osa jinak
Najděte svod s největším a nejmenším součtem výchylek (jen tak od oka) – tyto svody budou na sebe kolmé. Úhel svodu s největším součtem QRS bude určovat přibližně el. osu srdeční. Nebude to dokonale přesné, ale to v praxi ani není potřeba.
I
aVR
II
aVF
aVL
III
0°
30°
60°
-30°
120°
90°
–
–
–
–
–
+
+
+
+
+
+
–
El. osa srdeční o něco víc než 60° (protože QRS aVL je lehce záporné)

## Slide 32
Určení elektrické osy srdeční – jak to dopadlo podle počítače?
72°
el. osa pro depolarizaci síní
el. osa pro repolarizaci komor
el. osa pro depolarizaci komor

## Slide 33: Flutter síní
Pravidelné pilovité zuby mezi QRS. Pravidelné RR, tachykardie.
Podkladem je krouživý vzruch (re-entry) v síních.
Pravidelnost je dána počtem „otoček“ vzruchu na převedení na komory (na obrázku: 3 otočky na 1 převedení na komory).
Pokud flutter nevymizí, mění se ve fibrilaci síní.

## Slide 34: Fibrilace
Síňová– chybí P, slabě nepravidelně „zubatá“ izolinie, RR nepravidelné, frekvence 80 – 180 bpm, není život ohrožující, ale vyčerpává srdce
Komorová – srdce nefunguje jako pumpa, nulový srdeční výdej, poškození mozku po 3 – 5 minutách fibrilace, bez včasné defibrilace se kardiomyocyty vyčerpají a přechází v asystolii
fibrilace
normal
Fibrilace: nesynchronizovaná aktivita kardiomyocytů
Asystolie – není přítomná elektrická aktivita, nedá se řešit defibrilací

## Slide 35: Extrasystoly
Supraventrikulární – ektopický vzruch vzniká v síni nebo v převodním systému AV
  QRS komplex extrasystoly má normální tvar (vzruch se komorou šíří normálně),
  vlna P nemá normální tvar (může být záporná či zakrytá QRS),
  může být s postextrasystolickou pauzou (pokus se vzruch šíří zpětně síněmi a vybije SA)
Ventrikulární – ektopický vzruch vzniká v komoře
  QRS komplex nemá normální tvar („obluda“)
  při pomalé srdeční frekvenci je bez kompenzační pauzy (extrasystola je vmezeřená mezi normální QRS) o sinusovém rytmu,
  nebo obsahuje kompenzační pauzu, pokud další vzruch pocházející z SA uzlu přijde v čase, kdy je komora ještě refrakterní

## Slide 36: Ischemie srdce
A
B
C
D
E
Deprese ST
elevace ST (Pardeho vlna)
Patologické Q
Transmurální infarkt
Negativní T (obrácený směr repolarizace)
Elevace ST – některé části tkáně se depolarizují se zpožděním
Patologické Q