## Slide 1: Vagus nerve stimulation - - intractable epilepsy therapy
Doc. MUDr. Eva Brichtová, Ph.D.
Dpt. of Neurosurgery
St. Anne University Hospital Brno and Masaryk University Brno
Epilepsy Center Brno

## Slide 2: Nervus vagus stimulation
Long-term vagus nerve stimulation (VNS) is a palliative treatment method for inoperable refractory epilepsy
First implantation in humans in 1988
The first implantation in Czech Republic in 1997
Nowadays about 60,000 patients
Czech Republic about 500 patients

## Slide 3: Indication
The VNS Therapy System is considered as supportive therapy
to reduce the frequency of seizures
in epileptic patients non-responding to antiepileptic drugs
with partial seizures (with or without secondary generalization) or generalized seizures

## Slide 4
The method utilizes the ability of afferent vagus nerve fibres to transmit nerve impulses into the brain stem nuclei (especially the solitary tract nucleus) and in this way further into the the limbic system and thalamo-cortical circuits.
Mechanism of VNS effect

## Slide 5: VNS implantation
The principle - electrical stimulation of the left vagus nerve through the bipolar electrode, which is connected to implantable pulse generator in the subclavian area.

## Slide 6
VNS implantation

## Slide 7
VNS implantation

## Slide 8
VNS implantation procedure

## Slide 9
Neurochirurgie patru; https://www.youtube.com/watch?v=T_W5WNgyR6M
VNS implantation procedure

## Slide 10
VNS implantation procedure

## Slide 11: Setting VNS therapy parameters
Typical stimulation parameters:
Current output: 1.0 to 2.0 mA Frequency: 20 Hz or 30 Hz
Pulse width: 250 or 500 us
Time ON stimulation: 30s Stimulation OFF time: 3 or 5min
using programming computer and
programming wand

## Slide 12
63% responders after 1 year, 55% after 2 years
Kuba R. 2002 Neurologie pro praxi
The effect of VNS therapy Reduction in number and intensity of seizures
Patients with at least to 50%
seizure reduction
(adult pts)

## Slide 13
ČESKÁ REPUBLIKA |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Brno |  | Brno dětská |  | NNH |  | FNM dětská |  | FNM dosp. |  | NNF |  | FTN dětská |  | FTN dosp. |  | ∑ | ∑ | ∑
 | primo | re | primo | re | primo | re | primo | re | primo | re | primo | re | primo | re | primo | re | primo | re | 
1997 |  |  |  |  |  |  |  |  |  |  | 1 |  | 1 |  |  |  | 2 | 0 | 2
1998 |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  | 1 | 0 | 1
1999 | 17 |  |  |  | 8 |  | 1 |  |  |  | 6 |  | 2 |  |  |  | 34 | 0 | 34
2000 | 12 |  |  |  | 8 |  | 2 |  |  |  | 2 |  | 2 | 1 |  |  | 26 | 1 | 27
2001 | 9 |  |  |  | 4 |  | 6 | 2 | 1 |  | 1 |  | 4 |  |  |  | 25 | 2 | 27
2002 | 11 |  |  |  |  |  | 2 |  |  |  |  |  | 2 |  | 3 |  | 18 | 0 | 18
2003 | 9 | 5 |  |  | 6 | 1 | 5 |  | 8 |  | 4 | 3 | 3 |  | 1 |  | 36 | 9 | 45
2004 | 10 | 4 |  |  | 13 | 1 | 1 |  | 1 |  | 3 | 3 | 5 |  | 1 |  | 34 | 8 | 42
2005 | 11 | 3 |  |  | 3 | 2 | 1 |  | 1 |  | 1 |  | 1 |  | 1 |  | 19 | 5 | 24
2006 | 17 | 3 |  |  | 9 | 9 | 5 |  |  |  | 1 |  | 2 |  |  |  | 34 | 12 | 46
2007 | 13 | 2 |  |  | 3 | 4 | 1 |  | 4 | 1 | 1 |  |  |  |  | 1 | 22 | 8 | 30
2008 | 10 | 1 | 2 | 0 | 3 |  | 1 |  | 3 |  | 4 |  |  |  | 3 |  | 26 | 1 | 27
2009 | 17 | 3 | 2 | 0 | 7 |  | 4 |  | 7 | 1 | 3 |  | 2 | 2 | 2 |  | 44 | 6 | 50
2010 | 12 | 10 | 4 | 0 | 4 | 3 | 3 |  | 3 | 1 | 4 | 1 | 3 | 1 |  | 2 | 33 | 18 | 51
2011 | 18 | 8 | 2 | 0 | 6 | 5 | 4 | 0 | 3 | 1 | 1 | 0 | 0 | 0 | 1 | 4 | 35 | 18 | 53
2012 | 11 | 12 | 1 | 0 | 6 | 5 | 3 | 0 | 2 | 4 | 4 | 1 | 0 | 0 | 0 | 1 | 27 | 23 | 50
2013 | 13 | 5 | 3 | 1 | 4 | 4 | 1 | 1 | 4 | 4 | 5 | 4 | 0 | 0 | 0 | 2 | 30 | 21 | 51
2014 | 10 | 7 | 2 | 2 | 6 | 6 | 4 | 0 | 3 | 2 | 4 | 2 | 0 | 0 | 1 | 6 | 30 | 25 | 55
2015 | 8 | 17 | 3 | 2 | 5 | 7 | 2 | 1 | 3 | 2 | 2 | 1 |  |  | 1 | 4 | 24 | 34 | 58
2016 | 1 | 2 | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  | 2 | 2 | 4
∑ | 209 | 82 | 20 | 5 | 95 | 47 | 47 | 4 | 43 | 16 | 47 | 15 | 27 | 4 | 14 | 20 | 476 | 157 | 633
VNS therapy in Czech republic

## Slide 14
Quality of life and VNS Therapy
Lethargy
Drowsiness
Difficulty
thinking
Depresion
Memory loss
Patients with refractory epilepsy
(n=503)
Quality of life and VNS Therapy
(n=2 229)
% of pts reporting
% of pts with improvement or
significant improvement
3 Months
12 Months
Activity
Postictal state
Seizure cluster
Verbal skill
Mood
Study results
Memory

## Slide 15
Kontakt:
eva.brichtova@fnusa.cz
Fakultní nemocnice u sv. Anny v Brně
Pekařská 53, Brno 656 91
Česká republika
Tel: + 420 543 181 111
www.fnusa.cz