## Slide 1: ELECTRODIAGNOSTICS IN PHYSICAL THERAPY
Electrogymnastic and Electrostimulation

## Slide 2: Electrodiognostics in Physical Therapy
Electrodiagnostics = determination of optimal parameters of impulses for stimulation of denervated muscles (electrostimulation) and continuous evaluation of the degree of reinnervation using the accommodation quotient.
performed using the Hoorveg-Weiss I / t curve - classical or in an abbreviated version.
https://www.google.com/url?sa=i&url=http%3A%2F%2Fwww.medwow.com%2Fmed%2Fultrasound_and_electrical_stimulation_unit%2Fgymna_uniphy%2Fguidance_c%2F6453.model-spec&psig=AOvVaw2uYUHQ7iOIdtyAE0_zjktV&ust=1606168390672000&source=images&cd=vfe&ved=0CAIQjRxqFwoTCIi-o9-Rl-0CFQAAAAAdAAAAABAD

## Slide 3: Electrodiognostics in Physical Therapy
I / t curve - used to measure the minimum intensity of rectangular and oblique pulses, causing visible or palpable contraction of the irritated muscle
Chronaxia:
  irritant pulse threshold time with two times higher than rheobase intensity (shortest time required to contract at double reobase)
Reobase:
  threshold intensity of the irritating pulse (the lowest intensity that can cause irritation with a sufficiently long pulse duration); low rheobase means high irritability and vice versa

## Slide 4: Electrodiognostics in Physical Therapy
Accommodation quotient (AQ):
  the ratio of the minimum intensity by an oblique and a rectangular pulse causing the contraction at a pulse length (time) of 1000 ms.
  AQ = oblique pulse ∕ rectangular pulse
  for healthy muscle it is 2 to 6
  partially denervated 1 to 2
  completely denervated around 1
  if the AQ is above 6 - a symptom of vegetative dystonia

## Slide 5: Hoorveg-Weiss I/t curve in Physical Therapy
I / t curve - used to measure the minimum intensity of rectangular and oblique pulses, causing visible or palpable contraction of the irritated muscle
Classical Hoorveg-Weiss I / t curve
  a complex form of irritability assessment
  the minimum intensity of rectangular and oblique pulses of standard length (time) is measured, causing a visible or palpable contraction of the irritated muscle
  pulse length (time) is 0.01; 0.05; 0.1; 0.5; 1; 5; 10; 50; 100; 500; 1000 ms
  44 measurements (very long timeduration method and unpleasant for the patient)

## Slide 6: Hoorveg-Weiss I/t curve in Physical Therapy
Abbreviated I / t curve
  measuring the minimum intensity causing contraction at a pulse length of 1000 ms for oblique and rectangular pulses
  comparing the results
  determination the AQ to make sure that we irritate a healthy or denervated muscle
  measurements for oblique pulses with a length of 100 and 500 ms (values ​​for 1000 ms are already measured), both for denervated and healthy muscle
  total 6 measurements
  semialgorithmic graph

## Slide 7: Hoorveg-Weiss I/t curve in Physical Therapy
According the target (stimulated) structure, the I / t curve can be divided into:
neurogenic (0.03 to 1.0 ms)
transient (1.0 to 10.0 ms)
myogenic (10.0 to 1000 ms) – for denerved muscle of our diagnostic by I/t curve most important

## Slide 8: Hoorveg-Weiss I/t curve
https://www.google.com/url?sa=i&url=https%3A%2F%2Fwww.wikilectures.eu%2Fw%2FELECTRO_THERAPY&psig=AOvVaw10sjwmN5aJbfPa7Bk4drId&ust=1605996330372000&source=images&cd=vfe&ved=2ahUKEwi12MPXkJLtAhUL-RQKHUS4DqMQjRx6BAgAEAc
OBLIQUE=

## Slide 9: Hoorveg-Weiss I/t curve
I/t curve of the health muscle ► solid line - rectangular pulses; dotted line - oblique pulses; AQ = 30/6= 5
I/t curve, determination of parameters for electrostimulation
► zp - curve for healthy muscle - rectangular impulses
► zš - curve for healthy muscle - oblique impulses
► dp - curve for denervated muscle - rectangular pulses
► dš - curve for denervated muscle - oblique pulses, AQ = 1
► ES - range of pulse parameters suitable for electrostimulation (for example 600 ms, 20 mA)

## Slide 10: Electrodiognostics in Physical Therapy
ELECTROTHERAPY is a type of physical therapy in which the healing effect of various forms of electrical energy is used. Electric currents or impulses are applied to the body for the purposes of therapy or diagnostics.
Division of electrotherapy used in electrostimulation a electrogymnastics:
GALVANOTHERAPY (direct current)
  resting galvanization, limb galvanic bath, electrotherapy bath, iontophoresis
LOW-FREQUENCY THERAPY (nf) f = 0 –1 kHz
  diadynamics, TENS, special currents
MED-FREQUENCY THERAPY (sf) f = 1 - 100 kHz
  bipolar application
  tetrapolar application: classical interference
  isoplanar vector field
  dipole vector field

## Slide 11: Electrogymnastic and Electrostimulation
Electrostimulation/electrogymnastics = impulse therapy
Electrostimulation = stimulation of denervated muscles, we use oblique pulses with a slow onset of intensity and a longer pulse length (time). Muscle test degree 0-1
Electrogymnastics = strengthening of weakened, not denervated muscles by means of rectangular impulses. Muscle test equal or higher then degree 2

## Slide 12: Practical application
Contraction-relaxation time:
phasic muscles - contraction 3-6 s, pause 2-3 times longer, (in case of extreme weakening we start with contraction 1s and increase with step 1s)
tonic muscles - contraction 10-40s, relaxation at least same long, optimally two times longer

## Slide 13: Electrostimulation – practical implementation
Stimulation - monopolary, with a ball (pen) electrode (cathode) in the place of the motor point of the muscle and anode with a significantly larger area is placed proximally or distally on the muscle
Bipolar stimulation with two equally large electrodes (anode proximal, cathode distal) – when a motor point cannot be found or for prolonged stimulation
CV mode
  The motor point of a muscle is the anatomically defined site from which contraction can be induced by percutaneous stimulation with the least intensity of irritating current. It is usually located in the proximal third of the muscle and is the site of nerve entry and the largest accumulation of neuromuscular discs. In denervated muscle, the motor point is located more distally
For practice, it is important to follow the principle of the same electrode

## Slide 14: Electrostimulation
Length of the procedure
  strictly individual.
  prevent energetic exhaustion of the muscle, which is manifested by a change in the quality of contraction and/or the need to increase the intensity
  better to perform electrostimulation for a shorter time:
    1 to 3 minutes or 5 to 15 contractions per motor point
    several times a day or to alternate individual muscles after 1 to 3 minutes during one session.

## Slide 15: Electrostimulation
Frequency of procedures
  started immidiately after diagnosis
  daily for a period proportional to the length of the regenerating axon (max. 3 mm per day)
  At intervals of 2 to 3 weeks
  control examination of the I/t curve of denervated muscle for rectangular pulses – if restored by rectangular pulses of 1 to 10 ms – change therapy on electrogymnastics

## Slide 16: Electrostimulation
Intensity
  always above the motor threshold (visible twitch of the muscle)
Contraction time - relaxation
  Phasic muscles - 3-6 s, in extreme weakness we start with 1s, we increase the length with a positive step of 1s, depending on how the muscle strength increases.
    The pause is 2-3 times longer than the contractions
    The duration of the procedure is 1-3 min. for each muscle, sports strengthening gradually, max 15 min.
  Tonic muscles - contraction - 10-40s, pause - min. equally long, optimally 2x longer, procedure time - 5-15min. not longer than 30 min.

## Slide 17: Electrostimulation - Low frequency currents
unpleasant perception by patients
DD-RS
  sinusoidal MF mounted on the galvanic component, 1s MF, 1s pause, frequency 50 Hz, pulse -10ms, pause 10ms
  poorly tolerated, painful contractions
Trabert
  Pulse, rectangular, monophasic, pulse 2ms, pause 5ms frequency 142.9 Hz is not frequency modulated - pleasant
  intensity at the margin of tolerance (subthreshold algic)
TENS surge (subjectively most pleasant, induced contraction is most similar to free contraction)
  Pulse length 100 - 500 microseconds (0.1-0.5 ms), (increasing pulse length, increases discomfort, therefore pulse length should be as short as possible, but must induce the required subjective intensity) optimal frequency is 50 Hz

## Slide 18: Electrostimulation - Mid-frequency currents
better subjectively tolerated
Carrier frequency from 2500 Hz, up to 12000 Hz
frequency modulation 50Hz constant or better 30-60 Hz (prevention of muscle fiber adaptation)
Kotz currents - Russian stimulation

## Slide 19: Electrostimulation - indications
strengthening of weakened muscles without reflex changes, which the patient is not able to consciously contract
Activation of the denervation muscles

## Slide 20: Electrostimulation - contraindications
febrile conditions of any etiology
general cachexia of any etiology
patients with an implanted pacemaker
haemorrhagic diathesis
metal objects under the application site or in a jet path
trophic skin changes at the application site
scars or fresh damage to the skin
pregnancy (exept TENS)
laryngeal and thyroid area
primary tuberculosis deposits, primary tumors without signs of metastasis below the site of application or in the current pathway
area of ​​large sympathetic plexuses
manifest cardiac or respiratory insufficiency
Sensitivity disorders at the application site

## Slide 21: Electrogymnastics
Exercise for weakened muscles
For muscles´ strength higher than level 2
mostly rectangular currents

## Slide 22: Electrogymnastics
Intensity
  always above the motor threshold (visible twitch of the muscle)
Contraction time - relaxation
  Phasic muscles - 3-6 s, in extreme weakness we start with 1s, we increase the length with a positive step of 1s, depending on how the muscle strength increases.
    The pause is 2-3 times longer than the contractions
    The duration of the procedure is 1-3 min. for each muscle, sports strengthening gradually, max 15 min.
  Tonic muscles - contraction - 10-40s, pause - min. equally long, optimally 2x longer, procedure time - 5-15min. not longer than 30 min.

## Slide 23: Electrogymnastics
Methods of application:
  bipolar EG: with two equally large electrodes placed over a given muscle - can only be accepted for long-term stimulation

## Slide 24: Electrogymnastics – most used currents
TENS surge (wave) - pulse length 100 - 500 μs, frequency 50 Hz, most pleasant for the patient
Middle frequencies currents - carrier frequency 2.5 kHz (Kotz currents= Russian stimulation ) -12 kHz, frequency modulation 30-60 Hz (modulation to avoid adaptation)
Low frequencies currents - Träbert currents, DD currents of the RS type - unpleasant, not used much

## Slide 25: Electrogymnastics - indications
strengthening of weakened muscles without reflex changes
muscle strength according muscle test: grade 2 and higher
creating the right gradual involvement of certain muscles (timing) in the optimal stereotypes of a certain movement in sport

## Slide 26: Electrogymnastics - contraindications
Contraindication:
febrile conditions of any etiology
general cachexia of any etiology
patients with an implanted pacemaker
haemorrhagic diathesis
metal objects under the application site or in a jet path
trophic skin changes at the application site
scars or fresh damage to the skin
pregnancy (exept TENS)
laryngeal and thyroid area
primary tuberculosis deposits, primary tumors without signs of metastasis below the site of application or in the current pathway
area of ​​large sympathetic plexuses
manifest cardiac or respiratory insufficiency
Sensitivity disorders at the application site

## Slide 27: Examples of specific use - neurology
Electrostimulation
  It is important to start as soon as possible
  according to the I / t curve, within 2-3 weeks a control examination is performed using rectangular impulse currents
  light paresis - lower intensity, shorter and steeper pulses
  heavy paresis - relatively high intensity, impulse rise slower, longer lasting
  Cerebral palsy
  Spastic paresis – stimulation of the agonistic muscle group
  Sclerosis multiplex
  Parkinson disease

## Slide 28: NEXT LECTURE – ONLINE TEST
Short online test – next Monday (30th November), 7 p.m.
check University Information system (Interactive syllabi)
Information in following days (Wednesday)

## Slide 29: Thank you for your attention
https://www.google.com/url?sa=i&url=https%3A%2F%2Fwww.mall.cz%2Ffilmove-predmety%2Fcurepink-plakat-star-wars-hvezdne-valky-yoda-may-the-force-be-with-you-61-x-91-5-cm-100028703944&psig=AOvVaw3giqGGvOnLeRuYvl_ryufw&ust=1606172542794000&source=images&cd=vfe&ved=0CAIQjRxqFwoTCPDu3aWhl-0CFQAAAAAdAAAAABAK