## Slide 1: Lectures on Medical Biophysics
Devices for substitution and assist of body organs

## Slide 2: Support and replacement of heart
Two pumps with an external pneumatic drive
Man who lived half a year with pair of rotation pumps Heartmate 2 without heart and pulse.

## Slide 3
During major heart or lungs surgery is often necessary to substitute function of these organs by an extracorporeal device. The lungs are substituted by oxygenator, which delivers oxygen to the body and removes carbon dioxide from it.
Two types of oxygenators: with direct contact of the gas with blood or based on diffusion of gases through a membrane between blood and gas.
In the bubble oxygenators, the oxygen bubbles ascend in a cylindrical vessel filled by blood. Blood uptakes oxygen and carbon dioxide is removed. Arising foam must be settled, then the blood passes through a filter and the „bubble trap“.
Membrane oxygenators are equipped by semipermeable membranes. Problem: certain denaturation of blood proteins and damage to the blood cells on the membranes limit their use to several hours. The membranes are layered or form capillaries. These oxygenators represent good approximation of lungs but it is necessary to disturb the blood layer on membranes by turbulences.
Cardiopulmonary bypass

## Slide 4: Cardiopulmonary bypass
Main parts of cardiopulmonary bypass: peristaltic pump, oxygenator, heat exchanger for heating or cooling blood and hence the patient’s body.
Membrane
oxygenator

## Slide 5: Cardiopulmonary bypass
Bubble oxygenator with heat exchanger.
The common problem of all cardiopulmonary bypasses is the need of certain increase of circulating blood volume – it can be done by dilution.

## Slide 6: Pacemaker
programmer
Pacemakers are used in patients with severe arrhythmias and some other heart diseases. This active implantable device consists of electrodes and a central unit driven by durable batteries. They can be programmed from outside the body according the patient’s conditions. They replace the natural pacemaker – the sinoatrial node.

## Slide 7: Defibrillators
Defibrillators are used in emergency medicine to renew spontaneous heart activity (in case of chamber fibrillation).
Implantable defibrillator/cardioverter

## Slide 8: „Iron lungs“ (in the past)
www.blinn.edu/natscience/phillips/ironlung.html
Poliomyelitis (polio) treatment in 50´.
Later was the problem solved by the Salk vaccine.

## Slide 9: Mechanical ventilation of lungs
Ventilation is performed with air pressure or volume limit
http://www.mtsinai.org/pulmonary/books/physiology/chap10a.htm

## Slide 10: Artificial kidney - haemodialysis
Superfluous volume of blood can be removed by underpressure in the dialysis solution
Arterial end
(arm)
Diluent added to blood
Dialyser - artificial kidney
Waste outlet
Venous end (arm)
“bubble trap”
Dialysis solution
According to: www.renalpatients.co.uk/ haemodialysis.htm. www.rheomed.de/Bilder/ produkte/dialyser.jpg

## Slide 11: Peritoneal dialysis
www.devicelink.com/ expo/awards02/98winQ.html. www.healthyeatingliving.com/ Kidney_failure.htm.
Peritoneal dialysis can be done by the patient at home. A catheter is permanently inserted into the peritoneal cavity serves for application as well as removal of dialysis solution. The procedure can be automated and performed during sleep.

## Slide 12: Haemofiltration
According to: info-dialyse.de/.../ haemo_haemofiltration.php.
Haemofiltration is an alternative of dialysis. It is very useful in some poisonings. Haemofiltrate with toxic substances is replaced by substitution solution added to blood in necessary amount.
High-flow-rate membrane
pump
Balancing of fluids
Substitution solution
haemo-filtrate

## Slide 13: Artificial pancreas – insulin pump
http://www.diabetesaustralia.com.au/conquest/0204-insulin-pump-therapy.htm www.pnl.gov/ energyscience/06-01/ws.htm.

## Slide 14: Retinal implant
www.nmi.de/deutsch/ showprj.php3?id=3&typ=1
MPDA – micro-photo-diode-array
Such devices are in clinical testing. They should enable basic spatial orientation.

## Slide 15: Cochlear implant
The electronic cochlear implants can partly replace the Corti's organ, mainly in children which have intact auditory nerve. It is an electrode system implanted into cochlea, which can stimulate the nerve by impulses generated in the so-called speech-processor.
http://www.accessexcellence.org/AB/BA/biochip3.html

## Slide 16: Hip joint substitution
http://www.orthogastonia.com/patient_ed/html_pages/hip/hip_hemiarthrooplasty.html
Hip or other joint substitutions are made of combinations of plastics and ceramics or titanium and its alloys. Titanium surface is porous, which enables the bone to grow inside the implant surface - lowering need of bone cement.

## Slide 17: Acetabular cup (hip joint socket) placement
Robots in orthopaedic surgery. The endoprosthesis must be positioned (oriented) with great angular precision.

## Slide 18: Knee joint substitution

## Slide 19: Ankle joint
http://www.orthogastonia.com/patient_ed/html_pages/ankle/ankle_arthroplasty.html

## Slide 20: Elbow and shoulder joint substitution
http://www.orthogastonia.com/patient-ed.html

## Slide 21: Joints of thumb and fingers
http://www.orthogastonia.com/patient_ed.html
CMC = carpometacarpal

## Slide 22: Bioprosthesis of hand – emerging reality
Electrode on efferent nerve;
Electrode on afferent nerve;
Implanted part for recording of nervous activity and nerve stimulation;
Efferent telemetric connection;
Afferent telemetric connection;
Bionic hand;
sensors;
Decoder of patient’s intentions and control of prosthesis;
Unit mediating the signals of sensors to the brain.
Subsystems 8-9 will be outside body but easy to carry.
http://www-arts.sssup.it/research/projects/CyberHand/default.htm

## Slide 23: Dental prostheses
Removable upper prosthesis
Partial prosthesis
Preparation of the bed for total fixed dentition substitution

## Slide 24: Penile endoprosthesis

## Slide 25
Author: Vojtěch Mornstein
Content collaboration and language revision: Carmel J. Caruana
Last revision November 2021, soundtrack addition: December 2020