## Slide 1: Spirometry

## Slide 2: Types of spirometers
pressure differences between the inner and outer spirometer membranes
air flow velocity according to the speed of the turbine rotation

## Slide 3: Static parameters
Tidal volume (TV) – the volume of air that enters the lungs during each inspiration (or the volume that is exhaled during every expiration).
Inspiratory reserve volume (IRV) – the maximal amount of additional air that can be drawn into the lungs by determined effort after a normal inspiration at rest.
Expiratory reserve volume (ERV) – the additional amount of air that can be exhaled from the lungs by determined effort after a normal expiration.
Residual volume (RV) – the volume of air still remaining in the lungs after the most forcible expiration possible.
V [l]
Vt (0,5 l)
IRV (2,5 l)
ERV (1,5 l)
RV (1,5 l)

## Slide 4: Static parameters
Lung capacity:
VC = VT + IRV + ERV
TLC = VC + RV
FRC = ERV + RV
IC = IRV + VT
EC = ERV + VT
Vt (0,5 l)
IRV (2,5 l)
ERV (1,5 l)
RV (1,5 l)
V [l]
Dynamic lung volumes:
VE
MMV

## Slide 5: Dynamic parameters
V [l]
Dynamic lung volumes:
Minute ventilation
Apneic pauses (inspirium/expirium)
Frequency of breathing
Apneic pause
Frequency
time

## Slide 6: Dynamic parameters
Dynamic lung volumes
V [l]
Time [s]
FVC
RV
1 s
FEV1
FVC – the maximum volume of air that can be exhaled after maximum inhale
FEV1 – the volume of air exhaled with the greatest effort in 1 second after maximum inhale
FEV1/FVC (%) – Tiffeneau index – around 0,8 (80 %)

## Slide 7: Obstructive/restrictive lung disease
1 s
V [l]
Time [s]
1 s
V [l]
Time [s]
FEV1
FEV1
FVC > FVC
Obstructive lung disease
(FVC=N; FEV1=↓)
tracheal stenosis
astma bronchiale
CHOPN
tumor
Restrictive lung disease
(FVC=↓; FEV1=N)
Pulmonary etiology
pulmonary fibrosis
lung resection
pulmonary edema
pneumonia
Extrapulmonary etiology
ascites
kyphoscoliosis
burns
high diaphragm condition

## Slide 8: Flow - volume curve
PIF – peek inspirátory flow; the highest speed of air flow at peak of inhale
PEF – peek expiratory flow; the highest speed of air flow at peak of exhale
FEF – maximum expiratory flow rates at different FVC levels (75 %, 50 % and 25 % of FVC)