## Slide 1: Contrast agents
Tereza Kopřivová

## Slide 2: Learning objective
Student will learn most comon contrast agents used in radiology and their adverse effects

## Slide 3: Classification of contrast agents
By modality
  US
  MRI
  Methods using X-rays
By way of application
  i.v., i.a., p.o., intrathecally, intravesically, into fistulas…
By type of contrast
  Positive
  Negative

## Slide 4: Contrast agent for US
Mikrobubbles of sulphur hexafluorid (SF6) stabilized by phospholipids (SonoVue)
Contrast created by differences of impedance on interface gas/liquid
Administered i.v., is strictly intravascular – shows microcirculation
Eliminated through lung capillaries (in cca 15 minutes)
Can be administered to patients with renal failure, adverse reactions are extremely rare
Contraindications: significant right-left shunts, severe lung hypertension, recent heart attack…

## Slide 5: C.a. for methods using X-rays
I.v. and any other way of administration
  Iodine c.a. (viz dále)
P.o. podání (event. per rectum, sondami do GIT)
  Positive
    Baryum k.l. (BaSO4) – in CT, fluoroscopy. Can not be used in suspected GIT perforation
  Negative
    Water – in CT for distension of upper GIT (water is absorbed aborally)
    Mannitol – in CT for distension of lower GIT (it is hyperosmolar)
    Gas – CO2 - in CT colonoscopy (administered p.r.), efervescent powder in fluoroscopy of oesophagus and stomach – for distension

## Slide 6: Iodine c.a. 1
Positive – iodine absorbs X rays (high nucleon number)
Administered anywere: i.a., i.v., p.o., intravesically, into tubes, drains, fistulas…
Moves to interstitium, does not move through normal hematoencephalic barrier
Mostly eliminated by kidneys (normally in cca 2h), elimination depends on glomerular filtration, critical for adverse reaction to kidney function is the first pass through kidneys, they can removed by dialysis
Now only non-ionic c.a. used
Main characteristics of iodine c.a. – concentration, osmolality, viscosity

## Slide 7: Iodine c.a. 2
Adverse effects
  Acute adverse reaction – different types (allergic, alergoid, chemotoxic…)
    Different severity: nauzea, vomiting, erythema, urticaria, seizures, arrythmias, anaphylaxis…
  Post contrast acute kidney injury
    = increase of serum creatinin by more than 26,5 umol/l 48-72h after administration of c.a., many different factors
Contraidications are relative – considering risk/benefit
  Alergic reaction to iodine c.a. in personal history
  Renal failure
  Metformin – when renal function decreases, metformin excretion is impeded and can cause lactic acidosis

## Slide 8: Contrast agents for MRI
I.v.
  Gadolinium c.a.
P.o.
  Blueberry/pineapple juice
    Negative contrast - Negative contrast in MRCP to cancel artifacts from stomach contents
  Mannitol
    In MR enterography – mainly for distension of bowels

## Slide 9: Gadolinium c.a. 1
Gd is paramagnetic, we do not see c.a. itself but how it influences magnetic field around it, it mainly shortens T1 time (= increase of signal on T1 weighted images = positive contrast)
Chelated Gd (Gd by itself is heavy toxic metal)
Moves into interstitium, does not move through normal hematoencephalic barrier, can be removed by dialysis
Excreted by kidneys, elimination halftime in normal renal functions is cca 90 min
There is a tissue specific Gd c.a. that is excreted half by kidneys, half by bile ducts, used for liver lesions and bile ducts imaging

## Slide 10: Gadolinium c.a. 2
Adverse effects
  Acute adverse reaction – analogically to iodine c.a., compared to them are less frequent (Gd c.a. are less hyperosmolar, chelated, there are smaller volumes administered…)
  Postcontrast acute kidney injury – minimal risk compared to iodine c.a.
  Nefrogenic systemic fibrosis (NSF)
    Rare systemic disease – thickening and induration of skin, pruritus, contractures, multiple organs affected, proved link to Gd c.a
    At risk patients – on dialysis, GF less than 15ml/min (Gd is released from chelates and causes damage) – carefully consider the indication

## Slide 11: Take home message
Referring physician should know adverse effects of commonly used contrast agents and provide relevant info = history of allergic reactions, current values of creatinin, use of metformin, can patient have p.o. c.a.?, is there GIT perforation suspected…