## Slide 1: Advanced microscopy techniques
Zuzana Tomášiková Cellular and Molecular Immunology, ICRC

## Slide 2: Microscopes allowed us to see the invisible...
Thanks to Golgi staining technique he was able to illustrate multiple structures of the nervous system, with particular attention to the multitude of neurons found in our brain
Marcello Malpighi (1628-1694)
The first to observe capillaries in animals;
Described the complex pulmonary structure;
Santiago Ramon y Cajal (1852-1934) Nobel prize 1906 “in recognition of his work on the structure of the nervous system”

## Slide 3: Evolution of microscopes helped us to improve our knowledge on both microorganisms and our own anatomy
1625
First use of term
“microscope”
1873
Abbe’s law and Electron Microscopy
1957
Confocal microscopy principles
1978
Confocal LSM
1986
Physics Nobel Prize for EM and STM
1990
Multiphoton microscopy
1993
Super-
resolution
1994
SIM and STED
techniques
2006
PALM and STORM
2014
Chemistry Nobel Prize for Super- resolution
Microscopy is one of the most powerful tool in many research fields;
It gave us the possibility to unravel what is beyond the capacity to be seen by
our eyes;
Since the beginning of microscopy history breakthrough discoveries have been made (e.g., electron microscopy);
Over the past two decades methods that can overcome the diffraction limit
and allow the imaging of complex structures have emerged;

## Slide 4: Techniques for different scales
Fluorescence microscopy
Electron microscopy
Super-resolution microscopy
1mm
100 µm
10 µm
1 µm
100 nm
10 nm
1 nm
1Å
Small organisms
Plant cell
animal cell
Mitochondria/ bacteria
Animal viruses
proteins
Small molecules
Scanning probe microscopy

## Slide 5: Many microscopy techniques are available for different case-study
fluorescence
confocal
multiphoton
Super-resolution
Optical
Transmission (TEM)
Electron
Scanning (SEM)
Scanning probe
Atomic force (AFM)
Scanning tunneling (STM)
Microscopy techniques

## Slide 6: Super-resolution microscopy
Multiple color labeling
Sample preparation straightforward (as in a simple
immunocytochemistry approach)
Temporal resolution may be a bit slower than a confocal (going from speed acquisition of msec to sec)
Important improvement in spatial resolution >> 20-150 nm
Define small structures (e.g., cytoskeletal components and organization; protein-protein interactions)
Live imaging for better acquisition of single molecule movement;
3D imaging for better understanding spatial organization of proteins (e.g., dsDNA interactions with surrounding proteins);
Nobel Prize in Chemistry, 2014
Eric Betzig
Stefan Hell
William Moerner
Abbe’s law
Structured Illuminated Microscopy (SIM)
Stimulated Emission Depletion (STED)
Single Molecule Localization Microscopy (SMLM)

## Slide 7: Structured Illuminated microscopy (SIM)
A sample with an unknown frequency pattern is illuminated with
light of a KNOWN high-frequency pattern (moiré pattern);
Angle changes to determine different patterns to apply for acquisition (15-25);
Different frequencies
Different patterns
Processed image (overlap of many
pattern/frequencies images)
Komis et al., 2015
GFP-labelled Arabidopsis thaliana microtubules

## Slide 8: What can we do with SIM?
Visualization of proteins at high resolution levels
Actin Actin
Clathrin-coated pits
Li et al., 2015
Cortical actin and internal filaments in COS7 cells
3D-SIM of DNA-damage repairing proteins
Ochs et al., 2019
DNA-proteins visualized in Retinal epithelial human cells
SIM-Live imaging of dendritic spines
Turcotte et al., 2019
Cytosolic GFP expressed in mouse brain neurons

## Slide 9: Can we go a little bit further ? Organization of cytoskeletal proteins in an in vitro model of Trauma Brain Injury
Unravel spatial organization of proteins and how it can change in specific conditions
Pozo Devoto et al., 2022
Figuring out details about proteins organization can help analyzing parameters such as orientation, periodicity of the protein in the cell, changes in conformation due to a pathological event

## Slide 10: What are the main limitations of SIM?
RESOLUTION
It can only be doubled compared to the classical diffraction limit of point scanning microscopy
SPEED
The acquisition rate is limited by the movements of the illumination patterns (depends on the grating rotation options of the machine);
SAMPLE QUALITY
Poor quality sample could lead to a wrong or no modulation of the grating pattern, requiring higher exposure, which can damage the sample;

## Slide 11: Stimulated Emission Depletion Microscopy (STED)
Confocal microscope;
The system needs an additional laser beam that quenches
”unnecessary” light;
Spatial resolution unlimited-bypass diffraction-limit;
Doesn’t require computational processing;
Vicidomini et al., 2011

## Slide 12: STED applications and achievements
Structural analysis;
Protein-protein interactions;
in vivo-imaging;
Actin rings periodicity at the dendrites
D’Este et al., 2015
Berning et al., 2012
In vivo imaging in a mouse brain of its synapses
Wegner et al., 2020
Dual-color STED imaging for post-synaptic protein dynamic studies

## Slide 13: STED is a powerful but challenging super-resolution technique
Multicolor imaging can be done, but it can be difficult since for each excitation wavelength an associated depletion beam is needed;
Solovei and Cremer,2010
Sample preparation needs to be very accurate,
both in the choice of fluorophores and the
“density” of their staining;
High resolutions require massive laser intensities, which can conduct to photobleaching and phototoxicity;
photobleached
Expensive technique, since requires a multilaser system;

## Slide 14: Where is the center?
Are we confident about the exact center of
this molecule?
Some microscopy techniques can push beyond the boundaries of resolution limit to visualize for single molecule imaging
A single Alexa Fluor 647 dye
Gaussian fit to find the center
x
Point Spread Function (PSF) Light waves converge and interfere at the focal point to produce a diffraction pattern of concentric rings

## Slide 15: Single Molecule Localization Microscopy (SMLM)
Employs conventional wide-field excitation and achieves super-resolution by localizing individual molecules;
  Can achieve spatial resolution of ca. 20-50 nm and sometimes even better (10x
more than conventional microscopy!);
    SMLM methods are relatively easy to implement, but require a careful choice of fluorophores;
Principle(1):
Spatial coordinates of fluorescently labelled molecules can be determined with high precision if their PSFs do not overlap;
Principle(2):
Photoswitching of fluorescent molecules is applied via multiple acquisition over time of different molecules;

## Slide 16: Many ways to acquire single molecules in our samples
PALM
Photoactivatable Localization Microscopy
Sequential imaging of fluorophores subsets and consequent reconstruction of their positions via multiple frame acquisition (the “blinking” image);
STORM
Stochastic Optical Reconstruction Microscopy
PAINT
Points Accumulation for Imaging in Nanoscale Topography
The fluorophores used for all these techniques switch from a
“bright” state to a “dark” one

## Slide 17: Stochastic Optical Reconstruction Microscopy (STORM)
Conventional microscopy
Lelek et al., 2021
STORM
Individual molecule activation
Individual molecule detection (gating)
Localization of single molecules (coordinates)

## Slide 18: Many fluorophores are available for different approaches
Fluorophores used in SMLM techniques fall into one of five different classes based on how they exchange their ON<>OFF status
Fluorescent dyes rather than fluorescent proteins have higher photon count therefore allowing shorter imaging times and higher localization precision
Fluorescent proteins are more suited for live-imaging applications (PALM), but premature bleaching or poor levels of expression in the specimen may limit the structural resolution
Lelek et al., 2021

## Slide 19: STORM applications and milestones
Since its discovery in 2006 this microscopy technique has evolved continuously guaranteeing a revolutionary approach to study proteins and nucleic acids at nanoscale resolution

## Slide 20: Unraveling nano-structures in cell nucleus
Ricci et al., Cell 2015
STORM images of H2B in human fibroblasts
Tens to hundreds of nucleosomes along the chromatin fiber
Thevathasan et al., Nat. Methods 2019
STORM imaging of single molecules for different nuclear pore proteins present at the nuclear level of Nup96 cells
RNApol II and Histone protein 2B interaction

## Slide 21: Cytoskeletal proteins ultrastructure and synaptic receptor organization
Siddig et al., Science 2020
Nanoscale organization of metabotropic glutamate receptors at presynaptic active zone
Xu et al., Science 2012
For the first time spatial organization of the cytoskeletal proteins of the axon was reconstructed thanks to STORM

## Slide 22: A fancy technique with different limitations…
1. Susceptibility to artefacts upon image reconstruction;
2. Difficulties in imaging thick samples: not suitable for tissue samples;
1. Low-throughput due by the small field of view required for single molecule localization and imaging;
Minimize with good software algorithms

## Slide 23: Electron microscopy
First application 1931 when Ernst Ruska built the first electron microscope, for which he was awarded with the Nobel Prize in Physics in 1986;
“for his fundamental work in electron optics, and for the design of the first electron
microscope”

## Slide 24: Basic concepts of Electron microscopy
The source allowing the images to be built is not a beam of light but of electrons, captured under vacuum condition usually on a phosphorescent screen;
Resolution and magnification capacities go beyond the classic diffraction limit, down to nm scale;
The main concept is based on the theory of Louis De Broglie (1924) that matter behaves like a wave exactly as light does;
the wavelengths of a beam of electrons is small such to don’t
have a remarkable impact on daily activities;
The smaller the wavelength the higher the resolution.

## Slide 25: General “workflow” of an electron microscope
Electron gun generates the beam
2 sets of condenser lenses direct the electron
beam toward the specimen;
To move electrons down the column an accelerating voltage is applied (100-1000 kV)
The electron beam passes through the sample, which based on its density will differently scatter the electrons
The beam then passes through the objective lens, forming the intermediate magnified image
Finally, another set of lenses produces the further
magnified image

## Slide 26: How are the images generated in electron microscopy?
EMs work using signals arising from the interaction of
an electron beam with the specimen
2 main EM techniques Transmission and Scanning Electron Microscopy (TEM and SEM respectively)
TEM (inner structures) SEM (outer structures)

## Slide 27: TEM was the first non-optical technique to give a remarkable resolution improvement
Analogous to a compound microscope where a system of multiple lenses are placed one after the other
Powerful for visualizing many kind of small molecules:
Arrangement of proteins,
Lipids
Nucleic acids (DNA, RNA, ribosomes)
Contrast for visualization of different structures is achieved often by using
metal compounds
  Osmium tetroxide (fixative, good lipid-binding)
  Uranyl acetate (good for nucleic acid contrast)
  Lead
Samples are dehydrated upon fixation and then stained;
Ultra-thin sections of 20 – 100 nm are then cut before imaging;
After the cut the thin layers are placed/embedded on a copper grid that
goes than to the microscope;
In the final image, the denser regions will reflect less and so they will be darker, while the less density will allow less absorption of electrons, thus generating a “brighter” image

## Slide 28: TEM was the first non-optical technique to give a remarkable resolution improvement
Contrast for visualization of different structures is achieved often by using
metal compounds
Osmium tetroxide (fixative, good lipid-binding)
Uranyl acetate (good for nucleic acid contrast)
Lead
Samples are dehydrated upon fixation and then stained;
Ultra-thin sections of 20 – 100 nm are then cut before imaging;
After the cut the thin layers are placed/embedded on a copper grid that
goes than to the microscope;
In the final image, the denser regions will reflect less and so they will be darker, while the less density will allow less absorption of electrons, thus generating a “brighter” image
Nucleus
microtubules
mitochondria
centriole
Nucleolus
Golgi
Lysosome

## Slide 29: Scanning Electron Microscopy (SEM)
a focused beam of high-energy electrons generates a variety of signals at the surface of solid specimens;
signals deriving from electron-sample interactions reveal
- external morphology
- chemical composition
- crystalline structure and orientation of materials;
magnification range >> 20-60000X
spatial resolution >> 50-100 nm
accelerated electrons carry significant amount of kinetic
energy, then dissipated as a variety of signals:
  secondary electrons (produce SEM images)
  backscattered electrons
  diffracted backscattered electrons (used to determine crystal structures and orientations of minerals)
samples
dehydrated
solid
Coated with Ag, Au, Pt, others

## Slide 30
An example of SEM application
Workflow to establish swelling formation in human neurons, a mechanism occurring after a traumatic impact in the brain.
In this experiments the number of events (swellings) forming after injury were quantified by immediately fixing the cells and then scan images in an electron microscope
Trauma brain injury model in vitro
Pozo Devoto et al., 2022
SEM images of ctrl and Injured axons
SEM image of full MF system
Quantification of swellings in SEM images before and post-injury

## Slide 31: TEM and SEM: advantages and limitations
High magnification and
resolution
Material rarely distorted during specimen preparation, which is
not complicated
Allows the investigation of deep structures but also surface
interactions
Live samples cannot be
imaged
TEM samples must be cut in
ultra-thin slices
Samples need to be properly dried to favor the internal vacuum
conditions
Expensive to maintain (very sensitive to vibration and external
magnetic fields)
PRO >>
<< CONS

## Slide 32: …. And more.. Scanning Probe Microscopy (1980s)
Nanoscale surfaces and structures, including atoms;
Resolution sometimes <1nm;
A physical probe is used to scan back and
forth over the sample surface;
Probe tip mounted at the end of a cantilever;
The tip can be as sharp as an atom;
The user doesn’t see the surface directly, is
the tool that “feels” it;
A computer collects the data to generate an image;
SPMs can measure deflections caused by many forces
  mechanical contact
  electrostatic
  magnetic
  Van der Waals
Images are colorless since they are measuring properties rather than reflection of light
AFM
Electrostatic forces between the cantilever tip and the sample;
Mechanical properties of
cells/tissues
STM
The electrical current flowing between the cantilever tip and the sample

## Slide 33: Conclusions
Microscopy helped us to unravel the invisible;
Nowadays advanced microscopy techniques have a variety of applications in many fields, being extremely important for
biology and understanding of structure and interactions between proteins;
Super-resolution microscopy allows multiple color imaging by breaking the boundaries of the diffraction limit;
single molecule imaging allowed the visualization of cellular nanostructures never resolved before with light
microscopy;
Electron microscopy was the earliest technique able to reach resolutions that light microscopy had never reached;
TEM and SEM are still of large use for describing composition of structures and microorganisms;
SPM techniques achieved the ability to image a structure just based on the atomic composition and the forces involved in the interaction between a surface and a scanning probe;
The use of fluorophores for staining cell cultures and tissues both for basic research purposes or diagnostic ones
(histopathology) is in continuous evolution and the offer on the market improves very quickly;

## Slide 34
Thank you for the attention!