## Slide 1
G7481
Magnetometry in geology and archaeology
Lecturer: Vojtěch Šešulka
spring 2010

## Slide 2
Geophysical methods
magnetometry
gravimetry
seismic
geoelectric
georadar
geothermic

## Slide 3
principal: measuring the Earth‘s magnetic field and its anomalies
observed units:
- total magnetic field T [nT]
- magnetic field gradient DT [nT/m]
- magnetic susceptibility k [n×10e-4]
Magnetic method
of geophysical survey

## Slide 4
Cesium magnetometer
SM-5 Navmag (Scintrex, Kanada)

## Slide 5
gradiometer
(magnetic field gradientΔT [nT/m])
variometer
(total magnetic fieldT [nT] )
Proton magnetometer PMG-1 fa
in gradient mode,
Geofyzika Brno
Modes of measurements

## Slide 6
Gradiometer
two vertically placed sensors
prevents the magnetic field variations error
better for shallow objects and structures

## Slide 7
Variometer
data collected with only one sensor
Earth‘s magnetic field variations error → neccesity of correction

## Slide 8
Application
of magnetic method
geological structures mapping
mapping buried ferrous metal objects and other burned structures

## Slide 9
Magnetometry
in archaeology
suitable:
-countersunk objects
-fireplaces, ovens, furnaces, …
-line objects (ramparts, trenches, palisades, …)
-identification of metal objects
-detection of landfills and terrain formations
less suitable:
-communications
-stone-made object (if is used the stone from the bedrock of the site)

## Slide 10
Measurements types
testing measurements
(suitability of the method)
areal measurements
(several days long measurements)
detail measurements
(the most interesting objects)

## Slide 11
physical contrast between the object and surroundings
good state of objects insitu
size, shape, orientation and count of objects
relief and vegetation
absence of structures, which are not in our interest
climatic conditions during the measurement
suitable combination of several geophysical methods
Presumption
of successful project

## Slide 12
the measurement runs in squares (often 50×50 m)
suitable profiles orientation to the measured structure (best in N-S direction)
density of recorded data up to 0,5×0,15 m (depend on our interest)
Magnetic method
of the geophysical survey

## Slide 13
Magnetic method
field work

## Slide 14
Magnetic method
interpretation

## Slide 15
Site: Němčice nad Hanou
Apparature: SM-5 Navmag (Scintrex, Canada)
Author: V. Šešulka
19/09/2006

## Slide 16
gradient T [nT/m] on the profile10 before (left) and after (right) the median correction

## Slide 17
nT/m
Site: Němčice nad Hanou
Apparature: SM-5 Navmag (Scintrex, Canada)
Author: V. Šešulka
19/09/2006

## Slide 18
Site: Pohansko near Břeclavi
Apparature: Smartmag – 4g
(Scintrex, Canada)
Author: R. Křivánek
19/09/2006
Magnetic method
interpretation

## Slide 19
Milo & Šešulka – Pohansko near Břeclavi 28. 3. 2007
Comparison between the measured data and the cross-section across the rampart
Magnetic method
interpretation

## Slide 20
Milo & Šešulka
Těšetice-Kyjovice 7. 3. 2007
(R – roundel; O – object; K –metal; C –path; Z – earth-house)

## Slide 21
Milo & Šešulka – Pohansko near Břeclav 29. 3. 2007
(O - object; K – metal)
Magnetic method
interpretation

## Slide 22
Site: Pohansko near Břeclav
Apparature: Smartmag-4g (Scintrex, Canada)
Author: R. Křivánek
21/08/2001
Tz gradient map (Fous et al. 2000)
Magnetic method
interpretation

## Slide 23
Site Přední Arnoštov, author V. Šešulka
Magnetic method
interpretation

## Slide 24
Site Budkovice, author V. Šešulka
Magnetic method
interpretation

## Slide 25
Site Pičín, author V. Šešulka
Magnetic method
interpretation

## Slide 26
Magnetic method
interpretation
Site Těšetice-Kyjovice, author V. Šešulka

## Slide 27
Fous A., Hašek V. & Záhora R. (2000): Zpráva o archeogeofyzikální prospekci na akci Břeclav-Pohansko. – MS, závěrečná zpráva. Ústav archeologie a muzeologie FF MU v Brně.
Hašek V. & Měřínský Z. (1991): Geofyzikální metody v archeologii na Moravě. – MSV. Brno.
Křivánek R. (2002): Závěrečná zpráva o geofyzikálním průzkumu prováděném na základě HS č. 792/02 na lokalitě Pohansko, okr. Břeclav. – Archiv ArÚ. Praha. č.j. 7486/02.
Křivánek R. (2004): Geofyzikální metody. – In: Kuna M. (ed.): Nedestruktivní archeologie. – Academia. Praha.
Kuna et al. (2004): Nedestruktivní archeologie. – Academia. Praha.
Literature
used and recommended