## Slide 1
NMR-based Structural Biology for Studying Biomolecular Interactions
Karel Kubíček

## Slide 4
NMR

## Slide 5
NMR
sample
spectrum
Structure
Relaxation properties
Interaction at atomic level resolution
Analysis
Image
200-500 ml of
100-1000 mM compound
Method of choice
Data to be analyzed
Results

## Slide 6
NMR hardware
Magnet
Spectrometer
Control units

## Slide 7
NMR spectrometer
Earth’s Magnetic Field
~ 50mT

## Slide 8
Ampere’s law & solenoid
Magnet
superconducting solenoids immersed into He bath
He-bath ~4 K further improved to ~2.1 K with J-T pump
field strength 25-28 Tesla
(Nb, Ta)3Sn superconductor of 0.81 mm with ~271 filaments
buried in OFHC copper matrix

## Slide 10
Bore cca 55 mm
He-refill
N2-refill

## Slide 11
Improvement of sensitivity, resolution and signal-to-noise ratio
Of NMR magnets
J. Emsley &
R. Feeney,
Progr.. NMR
Spectroscopy 1995, 28, 1
‘10
1945
60
1961
220
‘65
1973
360
1979
500
1987
600
‘92
750
1000
‘97
2000
‘68
decoupling
decoupling
TROSY
FT and nD
DNP in high
fields
Spectrometer Frequency [Hz]
Time [year]

## Slide 12
Quench
an abnormal termination of magnet operation
Occurs when part of the superconducting coil enters the normal (resistive) state.
This can occur
because the field inside the magnet is too large
the rate of change of field is too large (causing eddy currents and resultant heating in the copper support matrix)
or a combination of the two.
a defect in the magnet can cause a quench.
MOVIE: https://www.youtube.com/watch?v=d-G3Kg-7n_M

## Slide 13
NMR Probe(head)

## Slide 14
Spectrometer
CBU
Control board unit
FGU
Frequency gen. u.
Shimms
Temperature Unit
AcquisitionControler
Transmitter

## Slide 15
NMR Spectrometer - Overview
Signal - sl(t)= sl(t)
l

## Slide 16
NMR radiofrequency pulse
Pulzy:
tvrdé – 7-30 ms@-3~+3dB
selektivní – ms~s@>30db
adiabatické

## Slide 17
magnetic field = 0
magnetic field > 0
For NMR, nuclear spin is needed!!!
Spin analogy to a compass needle

## Slide 18
Electron
Proton
Neutron
Atom
=
In the planetary model of the atom, an electron orbits a nucleus, forming a closed-current loop and producing a magnetic field with a north pole and a south pole.
Molecule is hence a group of small magnetic fields and each atom within the molecule experiences different local magnetic field.

## Slide 19
NMR - Refresh
nuclear spin  0 (1H, 13C, 15N, 31P) - number of neutrons and the number of protons both even  NO nuclear spin - number of neutrons plus the number of protons odd  half-integer spin (i.e. ½, 3/2, 5/2) - number of neutrons and the number of protons both odd  integer spin (i.e. 1, 2, 3)
=*B (1) - when placed in a magnetic field of strength B, a nuclei with a net spin can absorb a photon, of frequency . The frequency  depends on the gyromagnetic ratio,  of the nuclei
from quantum mechanics we know that nucleus with spin I can have 2I +1 orientations  nuclei with a spin ½ can have two orientations in an external magnetic field– low / high energy
N
S
N
S
N
S
E=h  (2)

## Slide 20
Nuclear Magnetic Resonance
Refresh
From (1) and (2): E=h  B
N
S
N
S
Energy
Magnetic Field

## Slide 21
N
S
N
S
Energy
Magnetic Field
Abs. E.
Magnetic Field
change field
change frequency

## Slide 22
CW vs. Fourier transform NMR
Problem of NMR
the magnitude of the energy changes in NMR spectroscopy small  sensitivity is a major limitation
Solution I.
increase sensitivity by recording many spectra, and then add them together; because noise is random, it adds as the square root of the number of spectra recorded.
For example, if 100 spectra of a compound were recorded and summed, then the noise would increase by a factor of 10,
but the signal would increase in magnitude by a factor of 100
 large increase in sensitivity.
However, if this is done using a CW-NMR, the time needed to collect the spectra is very large (one scan takes 2 - 8 minutes).

## Slide 23
CW vs. Fourier transform NMR
Solution II.
FT-NMR  all frequencies in a spectrum are irradiated
simultaneously with a radio frequency pulse.
Following the pulse, the nuclei return to thermal equilibrium.
A time domain emission signal is recorded by the instrument as
the nuclei relax.
A frequency domain spectrum is obtained by Fourier transformation.
FT
time domain (FID – free induction decay)
frequency domain
RF pulse 90

## Slide 24
EtOH
protein
Each proton = 1 NMR signal

## Slide 25
Each (non-exchangeable) proton = 1 NMR signal
We
-NH
-NH/-NH2/arom
Ha
Hb
-CH3
H2O

## Slide 26
Each (non-exchangeable) proton = 1 NMR signal

## Slide 27
Size Relaxation FID NMR line(width) after FT
slow (i.e. long t2 time)
medium
fast
Time
Induced voltage
Time
Induced voltage
Hz
Hz
Hz

## Slide 28
Size Relaxation FID NMR line(width) after FT
slow (i.e. long t2 time)
medium
fast
Time
Induced voltage
Time
Induced voltage
Hz
Hz
Hz
e.g. Cholesterol
Biomolecules 5-30 kDa
Large molecules 50+ kDa

## Slide 29
NMR data processing

## Slide 30
NMR data processing
Window functions:
1) improvements od S/N ratio
2) increasing resolution

## Slide 31
Exp
Lor.-Gauss
Kaiser w. function
NMR data processing – window functions – apodization

## Slide 33
NMR data processing – Zero Filling, Linear prediction
Linear prediction
Zero filling
240 points
64 pts
LP to 128 pts
LP to 240 pts

## Slide 34
|nmrPipe -fn POLY -time \
|nmrPipe -fn SP -off 0.33 -end 0.98 -pow 2 -c 1.0 \
|nmrPipe -fn ZF -size 2048 \
|nmrPipe -fn FT -auto \
|nmrPipe -fn PS -p0 -76.0 -p1 0.0 -di \
|nmrPipe -fn EXT -x1 11.0ppm -xn 6.0ppm -sw \
|nmrPipe -fn POLY -ord 3 -auto \
|nmrPipe -fn TP \
Solvent suppression
Window function
Zero-filling
FT
Transpose (in case of multidimensional spectra)
F2
NMR data processing - summary

## Slide 36
NMR as a tool for study structure, dynamics and interactions of biomolecules
Structure determination of NAs and proteins
Protein – metal interaction
Protein – ligand interaction
For most of the modern applications, enrichment by 13C, 15N and often 2H needed!
Isotope | Ground state spin | Natural abundance [%] |  | Rel. Sensitivity
1H | ½ | ~100__ |  | 1.00x10+0
13C | ½ | 1.10 |  | 1.59x10-2
15N | ½ | 0.37 |  | 1.04x10-3
19F | ½ | 100__ |  | 8.30x10-1
31P | ½ | ~100__ |  | 6.63x10-2
12C | 0 | 98.90 |  | -
16O | 0 | ~100__ |  | -

## Slide 37
r1,2
r1,2; r1,3; r2,3≤ 6 Å
1Å=1.10-10m
NOE:
NMR as a tool for study structure, dynamics and interactions of biomolecules
0) AA/NA sequence, resonance assignment, standard chemical shifts
Structure determination of proteins/NAs
NMR can provide detailed information about the structure at the atomic level resolution relying on the spatial proximity of two interacting protons – nuclear Overhauser enhancement (NOE)
Additional structural information can be obtained (residual dipolar couplings – RDCs, J-couplings, backbone chemical shifts - CSI)

## Slide 38
http://www.fbreagents.com/basics_nmr/9proteins.htm
Structure calculation
Iterative procedure of structure determination by NMR
N
C
Nrd1 CID
PDB ID: 2LO6
Uncertainty of the final structure represented as a family of 10-20 structures with deviation among individual members indicated by RMSD (typically <1.5 Å2)
Final structure

## Slide 39
15N / ppm
1H / ppm
Studying interactions by NMR titration
Slow exch. regime (on the NMR timescale) – individual peaks for each of the studied states (e.g. free / complexed forms of a protein), peak intensity representing population of a given state
Intermediate exchange regime
Fast exchange regime – single peak whose chemical shift position is given by the molar ratio of the states present in solution
Slow (KD<1 mM)
Free Bound
100% 0%
50% 50%
0% 100%
Intermediate (KD ~1-10 mM)
Free Bound
100% 0%
50% 50%
0% 100%
Fast exchange regime (KD>10 mM)
Free Bound
100% 0%
50% 50%
0% 100%

## Slide 40
1H-15N HSQC, cca 155 aa, well folded, 600MHz, 293K
15N-1H HSQC – Heteronuclear Single Quantum Coherence
1 peak ≅ 1 amino acid
good estimate of the protein folding status
no information about sequential assignment (which peak is which amino acid)
for sequential assignment third dimension needed (13C)
once assignment of the peaks known – HSQC is optimal tool for monitoring interactions by NMR through titrations (i.e. stepwise addition of small amounts of ligand to the nearly constant volume solution with the isotopically enriched molecule)

## Slide 41
1H-15N HSQC, cca 155 aa, well folded, 600MHz, 293K
1H 1D, Cavanagh et al., 2007
water

## Slide 42: Interaction of Nrd1-CID with C-terminal domain (CTD) NMR Titration - 15N enriched CID + unlabeled CTD-Ser5P in n-steps, n=6 in our case - peaks corresponding to the interacting residues of CID change their chemical shift (position in the spectrum) => interaction surface, binding constant, stoichiometry
Notes: We studied the interaction between CTD and CID by monitoring the chemical shift changes of the CID residues – one peak represents one amino acid in this spectra - upon addition of the CTD. In this way, we indentified the interacting surface of the Nrd1-CID

## Slide 43: Nrd1 CID interaction surface – CID residues experiencing the largest chemical shift variations upon the interaction with 5-phospho-Ser CTD shown in blue with side-chains in stick representation
Notes: … that are located on three helices of the CID.

## Slide 44
CTD-CID interaction with mutants studied by fluorescence anisotropy
Notes: Additionally, still analyzing the chemical shift perturbations, we have selected the residues crucial for the interaction and have mutated them to observe a dramatic drop in the affinity as measured by fluorescence anisotropy.

## Slide 45
Interligand NOEs between CID and CTD – 900MHz, 150ms, 293K
CID resonances
CTD resonances
Notes: Next, we determined the NMR structure of the complex between Nrd1-CID and Ser5P-CTD by measuring intermolecular contacts that are defined by these NOEs, where in one frequency domain, we acquired the resonances of the protein and in the second dimension the resonances of the ligand.

## Slide 46: Transferred-NOE
NOE = pbound.NOEbound + pfree.NOEfree
tc,bound >> tc,free (and pL,free >> pL,bound)
NOEbound > NOEfree
Notes: The correlation time is roughly defined as the time taken for a molecule to rotate one radian or move a distance of the order of its own dimension. Usually it is assumed that the correlation time depend on temperature according to an Arrhenius type of function;
Correlation time - The characteristic time between significant fluctuations in the local magnetic field experienced by a spin due to molecular motions.

## Slide 47
Transferred NOE Experiments
tr-NOESY~600M Discodermolide without and with ~12M tubulin
800MHz,
mixing time=80ms
disco w/o tub
disco:tub 50:1
8 7 6 ppm
8 7 6 ppm

## Slide 48
protein
ligand2
ligand1
Magnetization to be transferred
Transferred magnetization
Note the weak “signal”
They “compete” for same place but never “meet”

## Slide 49
interligand NOE Experiments .

## Slide 50
interligand NOE Experiments .
(50)Tbs + (1)Tub
(50)EpoA + (1)Tub

## Slide 51
interligand NOE Experiments .
(50)Tbs + (1)Tub
(50)Tbs+(50)EpoA+(1)Tub
(50)EpoA + (1)Tub
interligand x-peaks, 100-450ms, 900MHz

## Slide 52
interligand NOE Experiments .
(50)Tbs + (1)Tub
(50)Tbs+(50)EpoA+(1)Tub
(50)EpoA + (1)Tub
interligand x-peaks, 100-450ms, 900MHz