## Slide 1: C8953 NMR structural analysis - seminar
1D 13C-NMR
Michal Knor
437395@mail.muni.cz
March 17, 2021

## Slide 2
1H vs 13C NMR
1H
13C
Spin number
1
2
1 2
H: s= × H: s=1
13
2
1 12
C: s= × C: s=0
Abundance [%] | 99.98 | 1.1
Gyromagnetic ratio [107 rad.T−1.s−1] | 26.8 | 6.7
Chemical shift range [ppm] | 0 - 15 | 0 - 200
Nuclear shielding | σdia | σdia + σpara
Integration of signals | C | ×
T1 relaxation [s] | 1-20 | 1-40
Homonuclear J-interaction | C | ×
H↔C J-interaction (∼ 100-250 Hz) | carbon satellites | (n + 1) splitting × decoupling

## Slide 3: 1H vs 13C NMR
1H
13C
Spin number
1
2
1 2
H: s= × H: s=1
13
2
1 12
C: s= × C: s=0
Abundance [%] | 99.98 | 1.1
Gyromagnetic ratio [107 rad.T−1.s−1] | 26.8 | 6.7
Chemical shift range [ppm] | 0 - 15 | 0 - 200
Nuclear shielding | σdia | σdia + σpara
Integration of signals | C | ×
T1 relaxation [s] | 1-20 | 1-40
Homonuclear J-interaction | C | ×
H↔C J-interaction (∼ 100-250 Hz) | carbon satellites | (n + 1) splitting × decoupling
1H-13Cα
1H-13Cβ
1H-12C
ωC-0.51JHC
ωC+0.51JHC
1JHC
1JHC
1D 1H NMR
1D 13C NMR
1Hα-13C 1Hβ-13C
1H decoupled

## Slide 4: Important regions of 13C chemical shifts
Aldehydes RCH=O
Ketones R1R2C=O
Carboxylic acids R-CO2H
Esters R-CO2R'
Amines R-CONR2'
C-NO2
C-F
C-Cl
C-Br
C-I
C-H Saturated Hydrocarbons
C-NH2
C-OH
C-SR
C-OR
C-Ar
C-SO2 R
C-CO R
C-C=C
C CR
RC N
Heteroaromatics
Aromatics
R2C=CH2
RHC=CHR
R2C=CH2
200
150
50
0.0
100
ppm(δ)
Alkenes
Alkynes

## Slide 5: 1JCH depends on the bond order ( hybridization ⇔
  haracter )
    -C-H 1JCH ≈ 125 Hz
► =C-H 1JCH ≈ 160 Hz
    ≡C-H 1JCH ≈ 250 Hz
    X-C-H
) X = N, O, S, F, Cl, . . . 1JCH ⇑
) X = Li, Mg, . . . 1JCH ⇓
2JCH < 0 or close to zero (<3 Hz)
    often not observable
in 1D 13C H-C interaction suppressed by DECOUPLING
⇒ simplification of spectra (splitting removed, sensitivity)
    saturation of 1H energy levels during decoupling enhances relatively intensity of 13C signals because of heteronuclear nOe ⇒ quaternary carbons usually less intensive.

## Slide 6: Values of chemical shift of important solvents
Abbr. Formula 1H |  |  | 13C
ACN | CH3CN | 1.9 | 118
Benzene | C6H6 | 7.2 | 128
 | CHCl3 | 7.2 | 77
DCM | CH2Cl2 | 5.3 | 54
DMF | (CH3)2NCHO | 2.9, 8.0 | 32, 163
DMSO | (CH3)2SO | 2.5 | 40
MeOH | CH3OH | 3.3, 4.8 | 49
Water | H2O | 4.8 | -
EXPLAIN effect of solvent on the position of residual 1H water signal:
CHCl3 - 1.6, ACN - 2.1, DMSO - 3.3, MeOH - 4.9

## Slide 7: How many 13C signal would you expect in the NMR spectrum?
Ru
N
N
N
N
Cl
S
3
Cl CH
CH3
Cl
O
N
N+ H

## Slide 8: How many 13C signal would you expect in the NMR spectrum? 7
Ru
N
N
N
N
Cl
S
3
Cl CH
CH3
Cl
O
N
N+ H

## Slide 9
1D 13C-NMR 1, bottom without CPD

## Slide 10: 1D 13C-NMR 1, bottom without CPD
Notes:
numbers at top of peaks refers to values JHC constants
C1+C7 connected to electronegative groups (C1 quaternary)
C2 ipso aromatic, C4+C6
shielded by M+ of OH
C5+C4 NOE-enhanced in bit larger extend by close H
C9→C12: decaying effect of N8

## Slide 11: 1D 13C-NMR 2
ZOOM of coupled region of most deshielded signals
coupled spectrum
spectrum with decoupling

## Slide 12: 1D 13C-NMR 2
Notes:
C7 carbonyl, C1 attached to N
C3/5 deshielded by M- CO, C2/6 shielded by M+ of NH2
C4 last quaternary aromatic signal (most isolated from H nuclei)
C9 effect of esteric group,
? C10 affected by NH exchange
C12/C14 + C13/C15
decaying effect of N+

## Slide 13
1D 13C-NMR 3, b - zoom of right region, a - full decoupled spectrum

## Slide 14: 1D 13C-NMR 3, b - zoom of right region, a - full decoupled spectrum
Notes:
C3/C4 quaternary aromatic deshielded by O, Cβ quaternary coupled by CH3 and CαH
Cα deshielded by NO2
C1 last quaternary aromatic signal
C2/C6 coupled mutually and with Cα, C5 isolated (contraintuitive)
quartets OMe, Cγ

## Slide 15
1D 13C-NMR 4, consider equilibrium minor-major form
Which form dominates and why?

## Slide 16
1D 13C-NMR 4, consider equilibrium minor-major form
Which form dominates and why?

## Slide 17
Draw structural formula of compound with summary formula C9H11NO2 (use 1D 13C NMR spectrum to find the right structure)

## Slide 18
Draw structural formula of compound with summary formula C9H11NO2 (use 1D 13C NMR spectrum to find the right structure)
1
7
1
2
3
4
5
6
7
4
3
2
6
5
Notes:
C1 quaternary carbonyl, C7 attached to N
C5 aromatic,deshielded by NH2, shielded by carbonyl group, C6 opposite effects
C2/C3 decreasing effect of O
C4 last quarternaty carbon

## Slide 19
Draw structural formula of compound with summary formula C7H9NO (use 1D 13C NMR spectrum to find the right structure)

## Slide 20
Draw structural formula of compound with summary formula C7H9NO (use 1D 13C NMR spectrum to find the right structure)
Notes:
C1 quaternary deshilded by O, 5 quarternary deshilded by N
C3 aromatic,deshielded by OCH3 and NH2
C2/C4 shielded by OCH3 and NH2 ,OCH3 shielding effect stronger
C6 shielded by both OCH3 and NH2
C7 isolated CH3 carbon
1
2
3
4
5
6
7
7
1
5
6
2
4
3

## Slide 21
Next topic
Vector Model + 13C APT experiment