## Slide 1: Plasma Physics 2
Lesson 05: High frequency discharges
Notes: Vylepsit …

## Slide 2
1
Lecture series contents
Townsend breakdown theory, Paschen‘s law
Glow discharge
Electric arc at low and high pressures
Magnetized low-pressure plasmas and their role in material deposition methods.
Brief introduction to high-frequency discharges
Streamer breakdown theory, corona discharge, spark discharge
Barrier discharges
Leader discharge mechanism, ionization and discharges in planetary atmospherres
Discharges in liquids, complex and quantum plasmas
Thermonuclear fusion, Lawson criterion, magnetic confinement systems, plasma heating and intertial confinement fusion.
Notes: Pozor je to pro verejnost … jednoduseji, schemata nazorna, ne moc analyz, jen par rovnic

## Slide 3
2
High frequency discharges
enable plasma discharge even for non-conductive electrodes
electron plasma frequency
numerically
varieties: - MHz = RF plasma, ohřev plazmy posuvným proudem - capacitively coupled plasma – collisionall and collisionless heating, can run at very low pressures - inductively coupled plasma – heating on the plasma surface or in plasma volume - GHz = microwave discharges, surface wave heating or volume heating
electrons do have enough time to react to the external electric field!
Notes: Pozor je to pro verejnost … jednoduseji, schemata nazorna, ne moc analyz, jen par rovnic

## Slide 4
2a
High frequency discharges
enable plasma discharge even for non-conductive electrodes
electron plasma frequency
numerically
Notes: Pozor je to pro verejnost … jednoduseji, schemata nazorna, ne moc analyz, jen par rovnic

## Slide 5: High frequency breakdown

## Slide 6
At about 100 kHz, the time that the electron needs to transfer between the electrodes starts to be comparable with the period of the external electric field. The electron avalanche does not reach the electrode and it reverses direction!
electron heating in the external field is given as:
The optimum power is reached when:
3
High frequency breakdown
Mean electron energy
External electric field
Low frequencies
Notes: Pozor je to pro verejnost … jednoduseji, schemata nazorna, ne moc analyz, jen par rovnic

## Slide 7
3a
High frequency breakdown
At about 100 kHz, the time that the electron needs to transfer between the electrodes starts to be comparable with the period of the external electric field. The electron avalanche does not reach the electrode and it reverses direction!
electron heating in the external field is given as:
The optimum power
Mean electron energy
External electric field
Mean electron energy (prior to multiplication)
External E field
nízké frekvence
High frequency
Notes: Pozor je to pro verejnost … jednoduseji, schemata nazorna, ne moc analyz, jen par rovnic

## Slide 8
5
High Frequency breakdown
The Paschen curve for RF breakdown has two minima: 1) Classical DC-like: Electron attains some „ideal“ energy when traversing between electrodes 2) Resonance capture of electrons: electrons bounce off a plasma sheath that is approaching them.
Drift-diffusion branch – secondary emission affects the breakdown voltage
multi-pactor branch – electrons interact more
with walls than with themselves
Emission-free branch, breakdown voltage does not depend on the electrode distance
Notes: Pozor je to pro verejnost … jednoduseji, schemata nazorna, ne moc analyz, jen par rovnic

## Slide 9
3a
CCP vs ICP vs MW plasma
Notes: Pozor je to pro verejnost … jednoduseji, schemata nazorna, ne moc analyz, jen par rovnic

## Slide 10: capacitively coupled plasma anatomy

## Slide 11
3a
CCP plasma anatomy
Near-electrode electron heating (stochastic)
Bulk plasma heating (ohmic)
Typical frequencies: 10 MHz – 100 MHz (13.56 MHz ”standard”)
Typical pressure: 1 Pa – 1000 Pa
Notes: Pozor je to pro verejnost … jednoduseji, schemata nazorna, ne moc analyz, jen par rovnic

## Slide 12
6
CCP plasma anatomy
Simples case are two planar electrodes, covered with dielectric. Potential and density evolution during phase as follows:
Notes: Pozor je to pro verejnost … jednoduseji, schemata nazorna, ne moc analyz, jen par rovnic

## Slide 13
8
CCP plasma – self bias voltage
In CCP plasmas, we see emergence of the so-called self-bias DC voltage.
empirically, we see: where A1, A2 are electrode surface areas
An approximate derivation can be made as follows – we assume that the ion current on both electrodes has to be the same:
And if we further assume that the ion densities in front of both electrodes are the same we obtain
And ultimately
The smaller electrode has to have higher negative voltage to draw the same ion current => it acts as a cathode and it can be used e.g. for sputtering of material
This derivation is still extremely simplistic, will be done more properly in Plasma Physics 3
Notes: Pozor je to pro verejnost … jednoduseji, schemata nazorna, ne moc analyz, jen par rovnic

## Slide 14: Inductively coupled plasma anatomy

## Slide 15
3a
ICP plasma anatomy
Localized power deposition
Typical frequencies: 10 MHz – 100 MHz (13.56 MHz ”standard”)
Typical pressure: 1 Pa – 1000 Pa
Notes: Pozor je to pro verejnost … jednoduseji, schemata nazorna, ne moc analyz, jen par rovnic

## Slide 16
9
ICP plasma anatomy
Plasma is generated by electromagnetic induction – The RF coil creates H field, which creates poloidal E field in the volume
This wireless transfer of energy makes it possible to run the system at very high temperatures, because the walls can be made of ceramics with high thermal resistivity.
Notes: Pozor je to pro verejnost … jednoduseji, schemata nazorna, ne moc analyz, jen par rovnic

## Slide 17: Microwave plasma anatomy

## Slide 18
3a
MW plasma anatomy
Typical frequencies:
100 MHz – 10 GHz MHz (2.45 GHz ”standard”)
Gas pressure:
100 Pa – 1 atm
Notes: Pozor je to pro verejnost … jednoduseji, schemata nazorna, ne moc analyz, jen par rovnic

## Slide 19
10
MW plasma anatomy
There are various setups for MW plasma generation – surfatron, surfaguide, coaxial line, ….
Notes: Pozor je to pro verejnost … jednoduseji, schemata nazorna, ne moc analyz, jen par rovnic

## Slide 20: Applications of CCP, ICP, MW

## Slide 21
10
CCP and ICP applications – semiconductor etching
Notes: Pozor je to pro verejnost … jednoduseji, schemata nazorna, ne moc analyz, jen par rovnic

## Slide 22
10
CCP application – gridded ion thruster
Notes: Pozor je to pro verejnost … jednoduseji, schemata nazorna, ne moc analyz, jen par rovnic

## Slide 23
10
ICP application – DC torch analogue
At atm. pressure and high power levels, so-called ICP torches can generate fully ionized plasmas. Support similar power ranges (5 kW – 1 MW)
Advantage over DC torches: no contact with metal
Notes: Pozor je to pro verejnost … jednoduseji, schemata nazorna, ne moc analyz, jen par rovnic

## Slide 24
10
MW application – DC torch analogue
MW plasma is also being used as an analogue to DC torches
As opposed to DC or ICP torches, MW plasma typically operates at lower powers (tens of kW)
Microwave plasma can also be non-LTE (plasma does not have to be so conductive to enable MW absorption) => lower plasma densities achievable
Notes: Pozor je to pro verejnost … jednoduseji, schemata nazorna, ne moc analyz, jen par rovnic

## Slide 25
10
MW application – Plasmaline for solar cells
At atm. pressure and high power levels, so-called ICP torches can generate fully ionized plasmas.
Advantage over DC torches: no contact with metal
Notes: Pozor je to pro verejnost … jednoduseji, schemata nazorna, ne moc analyz, jen par rovnic

## Slide 26: Takeaways
High frequency breakdown
Different layouts for wave-driven discharges
CCP, ICP, MW – different power absorption mechanisms
Applications