## Slide 1: Lasers basics principles
Vítězslav Otruba, Karel Novotný

## Slide 2
Simplest configuration?

## Slide 3
High energetic lasers - PALS Prague Asterix Laser System
The vacuum chambers at the PALS laboratory in Prague, where a 1 kJ pulse creates plasma for X-ray generation

## Slide 4: Lasers – Light Amplification by Stimulated Emission of Radiation
Spectral range 1 mm – 50 nm, (experimentally) X ray range up to 1 nm, extreme experiments up to 0,01 nm –radiation generators especially (XASER)
For sub millimeter wave range MASERS (Microwave Amplification by Stimulated Emission of Radiation) - mainly as low noise radio signal amplifiers

## Slide 5
Commercially available – VUV – VIS – MID IR

## Slide 6: Properties of laser radiation
Emissions of elementary oscillators(atoms, molecules…) narrow beam– spatial energy concentration
Δλ can be very small– spectral concentration of energy
Synchronous operation of elementary oscillators– time concentration of energy
Coherence length up to tens (in vacuum up to thousands) kilometers

## Slide 7: Types of lasers by:
• emission wavelengths
• time mode of operation - continuous (cw) or pulse
• type of excitation – optical excited lasers, electric discharge, chemical, mechanical (particle collisions), injection of charge carriers, …
• type of active medium - solid, liquid (dye), gas, ion,
excimer, semiconductor (diode),…
• pulse duration (nanosecond, picosecond, femtosecond, ...) - the shorter pulse duration means higher the Peak power at the same Average Power

## Slide 8: Types of lasers
Properties of Active laser medium (gain medium, lasing medium)
Excitation of atoms up to
metastable state
By collisions between two kinds of atoms (He-Ne, CO2)
Optical excitation – pumping (ruby, neodymium glass)
Excitation in the chemical reaction (eximers)
By electric current (semiconductors,GaAs)
and other ways
Light output of lasers:
Continuous laser up to tens of mW
Pulse laser with an average power of 10 mW can have parameters:
  pulse duration = 1 ns,
  pulse energy = 1 mJ,
  pulse power = 1 MW
  repetition rate = 10 Hz

## Slide 9: Radiation Processes
E0
E1
hν = E1-E0
spontaneous
emission
absorption
stimulated
emission
A ~ ΔE2 ~ λ-2 (transition probability)
Radiation intensity : I(ν)=Nu·A·hν
Strong transitions :
E1 (electric dipole)
A~108 s-1 for neutrals
Weak transitions:
M1 (magnetic dipole),
E2 (electric quadrupole),
some E1
A ~1-100 s-1 for neutrals

## Slide 10: Radiative Processes cont’d
O I lines:
3P1-1D2
3P2-1D2
1D2-1S0
M1
E2
557,7 nm
630 nm
mean lifetime exc. state 0,7 s
mean lifetime exc. state 110 s

## Slide 11: spontaneous emissions
Probability of photon absorption :
w01=n0ρ(ν)B01
Probability of spontaneous emissions :
w10=n1A10
ρ(ν) – spectral density of radiation with frequency ν
B01 – Einstein coefficient of absorption
A10 – Einstein coefficient of spontaneous emission

## Slide 12: Stimulated emission
Probability of stimulated emission :
w10=n1ρ(ν)B10
B10 – – Einstein coefficient of stimulated emission
Process of interaction with radiation :
n0ρ(ν)B01=
n1ρ(ν)B10 +n1A10
1
0
1

## Slide 13: Interaction with radiation
Two-level model in thermodynamic equilibrium :
From the equation we express ρ(ν):
Boltzmann distribution in TD equilibrium (exponential decrease in level occupation with increasing energy):
[1]

## Slide 14: Relation between Einstein coefficients
Substituting the Boltzmann distribution [1] into the previous equation
for volume density of radiation we get:
For the spectral density of radiation we can use Planck relationship:
By combining the equations, it is possible to find the relationship between the Einstein coefficients:

## Slide 15: What is the relative number of acts of stimulated and spontaneous emission per unit of time?
R=
The number of stimulated emissions per second
The number of spontaneous emissions per second
wavelength
wavenumber
(cm-1)
frequency
(Hz)

## Slide 16: Inverse population
The Einstein coefficients for stimulated emission and absorption are equal: B01=B10=B
For absorption:
dΦA=hνn0Bρ(ν)dt
For stimulated emission:
dΦE=hνn1Bρ(ν)dt
Total radiant flux change:
dΦ/dt=hν(n1-n0)B
Condition for amplification of radiation:
n1- n0 >0, tj. inverse population

## Slide 17: Inverse population
The normal population distribution is shown in Figure a).
In order to create an active environment, it is necessary to intervene in the system in order to change the distribution of the energy level occupation in the way shown in Figure b).
The process is usually referred to as laser excitation or pumping. The basic method is optical excitation.

## Slide 18: Three-level system
Application: ruby laser
Level 2 is metastable
The disadvantage is low efficiency - for reach the inverse population at least 50% of the particles have to be brought to level 2
1
0
2
pumping
relaxation
stimulated emission

## Slide 19: Energy diagram of a ruby laser

## Slide 20: Three-level system
Modified three - level system with excitation to metastable level 1.
pumping
stimulated emission
relaxation
1
2
0

## Slide 21: Four-level system
Example - laser Nd: YAG
High efficiency
An inverse population must only be reached between levels 2 and 3
Laser Transition
Pump Transition
Fast decay
Fast decay
0
1
2
3
21

## Slide 22: Radiation amplification - quantum amplifier
Active environment amplifies the incoming radiation:
Φ=Φ0exp[-l(α+β)]
α - absorption coefficient (α‹0)
β - losses (β›0)
l - length of amplifying medium
α
Φ0
Φ

## Slide 23: Generation of radiation
By introducing positive feedback from the output to the input of the amplifier we get an oscillator whose frequency is given by the amplifier and the feedback circuit, usually realized by a Fabry-Perot resonator
F.-P.
+

## Slide 24: Laser radiation generation
Feedback is usually realized by a Fabry-Perot resonator.
For short pulse generation, the amplifier frequency bandwidth must be at least:
Δf ≅ 1/(2τ)
where τ is the pulse width
(polychromaticity of short pulses)

## Slide 25: Fourier decomposing functions
Anharmonic waves are sums of sinusoids.

## Slide 26: Conditions for radiation generation
The reflectance of the mirrors shall be chosen with regard to the amplification of the active environment so that the losses do not exceed the amplification of the active environment G:
R1R2exp[-2l(α+β)]≥1
pumping

## Slide 27: Optical resonator
The length of resonator L is M multiple of half-wave (M is an integer). The length L corresponds to given resonator frequencies νM (longitudinal laser modes). Inside the resonator is a standing wave of electric field E with frequency νM = c/λM

## Slide 28: Fabry-Perot etalon
Quality of resonator Q
(QFP~108-109)
Em- energy of the given mode
Pz- power dissipation
ω0- angular frequency of oscillator
ω0 = 2πν0 =2π/T0 [s-1]
Notes: Em energie daného módu v rezonátoru

## Slide 29: Spectral line width and laser modes
Δλ~1 pm – 10 nm
VIS, gas - semiconductor
The figure shows the individual resonances basic longitudinal mode.
Doppler line width
generation threshold

## Slide 30: Resonant modes and bandwidth gain of the active medium

## Slide 31: Optical resonators
Planparallel : r1 = r2 =
S1=S2
center of curvature
r2
r1
F1=F2
r
Concentric : r1 = r2 = L/2
Confocal : r1 = r2 = r = L/4
Hemispherical : r1 = L, r2 =
r1
S2
S1
F2
F1
focus
Volume of the optical (electric) field in resonator

## Slide 32: Coupled resonators
L – length of open resonator
l1,l2 – distance of interior mirrors
open resonator modes Z1-Z3
internal resonator modes Z2-Z3
resulting spectrum of frequencies

## Slide 33: Single mode laser
Combination of resonant modes and internal FP standard
or Lyot filter (narrowband polarization filter)
and the gain bandwidth generates only one longitudinal mode
generation threshold
internal etalon

## Slide 34: Open optical resonator
glass support
dielectric layer
Open resonator modes
Longitudinal modes: distribution of light radiation in the longitudinal direction
Transverse modes: distribution of light radiation in the transverse direction

## Slide 35: Transverse modes of the resonator Transverse Electromagnetic Mode - TEM
Transverse modes are characterized by a pair of numbers m and n. These numbers represent the number of nodes of the standing wave on the axes (x, y) perpendicular to the optical axis.
The number of nodes of the standing wave in the optical axis L is high and is not given.
The basic mode is TEM00, in which the radiation intensity profile has a Gaussian profile.

## Slide 36: Transverse modes of the resonator

## Slide 37: Gaussian beam (profile) mode TEM00
ws = distance from the resonator axis,
where the radiation intensity decrease to
1/e axis intensity

## Slide 38: Profile of the focused laser beam in its focus

## Slide 39: Coherence of radiation
coherence length lc- related to how long a continuous electromagnetic wave (sinusoidal wave) is emitted.
Heisenberg uncertainty principle : E t  h  2
hE  ht h  2  1  2 t
coherence time– 
where is the width of the spectral interval
In general, coherence can be understood as the ability of radiation to interfere with relative time shifts of the emitted radiation

## Slide 40: Brewster’s angle
Exit windows separating the low pressure area from the atmosphere
they are inclined at Brewster's angle to form a lossless optical feedthrough, which, as a by-product, causes the output radiation to be linearly polarized, a feature useful for a variety of applications.
For the size of the Brewster angle, it can be deduced from the Fresnel equations (indicating the intensity of the reflected and refracted light) that:
Where αB is the value of the Brewster angle and n relative refractive index between input and output medium.
discharge tube with active medium
polarization

## Slide 41: He – Ne and CO2 laser
Energy scheme of excitation
(so-called three-level system)
aB
If the exit windows are inclined at Brewster angle, the laser beam is linearly polarized
Glass discharge tube filled with He (pressure about 100 Pa) and Ne (pressure about 10 Pa).
For CO2 laser: nitrogen takes over the function of He and molecule of CO2 takes over the function of neon
E
He
Ne
1.
2.
3.
photon
He atom is excited to E1 by the discharge
By collisions He and Ne atoms - Ne atom is excited to a metastable state
In the presence of an electric field with a frequency nM the Ne emits stimulated photon, otherwise spontaneous
Ne
E1
E2
E3
hn = E2 – E3
Typical continuous lasers.
l(He-Ne) = 632.8 nm
l(CO2) = 10.6 mm

## Slide 42: Semiconductor laser
AlxGa1-xAs, p-typ
AlxGa1-xAs, n-typ
GaAs, p-typ
+
-
electron flow
hole flow
radiative recombination
emission of stimulated photons
Mirrored -
modified front surface
of crystal
The external voltage of this polarity causes a large number of electrons and holes (with a sufficiently long lifetime) to accumulate simultaneously in the optically active layer of GaAs, which can only recombine together by radiative transitions.
The mirrored crystal surface forms a plan-parallel optical resonator of about 1 mm in length. This ensures that stimulated photon emission occurs when electrons and holes recombining.Vlnová délka emitovaného světla je z intervalu 700 až 900 nm podle obsahu Al.
Luminescent photodiodes (LEDs) work on a similar principle. They do not have a resonator and the electrons and holes in the active environment recombine almost immediately.

## Slide 43: Summary
laser radiation has a much smaller line width than the emission line of the active medium
the laser emits radiation corresponding to the longitudinal (or transverse) modes, depending on the resonator configuration
the laser emits only in those modes whose gain is greater than the threshold
laser radiation has a high coherence
if the optical system includes an element supporting a particular polarization orientation, the output radiation is polarized.

## Slide 44
G.M. Hieftje, J.C. Travis, F. E. Lytle. Lasers in Chemical Analysis, The HUMANA Press. Inc. 1981
D. L. Andrews, Lasers in chemistry, Springer – Verlag, Third edition, 1997
N. Omenetto, Analytical Laser Spectroscopy, John Wiley & Sons, 18. 1. 1979
Literature