## Slide 1
Protein NMR Spectroscopy: Principal and Practice
Chapter 3.4 and 3.5:
Pulse Techniques and Spin Decoupling
Mar 19, 2009

## Slide 2
NMR Pulse Sequence

## Slide 3
z
x
Mxy
y
z
x
y
Mo
90oy
Maximizes signal in x,y-plane
where NMR signal detected
z
x
-Mo
y
z
x
y
Mo
180oy
90o pulse
180o pulse
Inverts the spin-population.
No NMR signal detected
NMR Pulse

## Slide 4
Off-Resonance Effects
Initial magnetization along z
y-pulse:
Ideal
On-resonance: Mz -> Mx
Off-resonance: phase 
z
x
Mxy
y
z
x
y
Mo
90o
Mxy

x
y

## Slide 5
Off-Resonance Effects - 90º Pulse
90º hard pulse works well for < 1
Phase shift is approximately linear
Effective flip angle  increases

## Slide 6
Off-Resonance Effects - 90º Pulse
Assume:
  Close to resonance
  First-order approximation
Phase angle is proportional to offset

## Slide 7
Off-Resonance Effects - 180º Pulse
180º pulse:
  Poor off-resonance performance
  Linear phase twist

## Slide 8
Composite Pulses
Trains of rectangular pulses instead of a single pulse
90x-180y-90x replaces 180x for inversion
The middle 180º compensates for off-resonance behavior of the outer 90º pulses

## Slide 9
Selective Pulses
Requirements:
  Uniform excitation or inversion profile
  Minimal perturbation outside the desired frequency range
  Uniform resulting phase for excitation
  Short pulse length to minimize relaxation effects
  Simple to implement experimentally

## Slide 10
Selective Pulses -- Soft Rectangular Pulses
174
CO
ppm
56
CA


## Slide 11
Selective Pulses -- Shaped Pulses
Approximated by a series of short rectangular pulses
Every point i:
  Amplitude i
  Phase i
Square pulse
Sinx/x
Gaussian
Not selective, residues distant from excitation frequency are excited

## Slide 12: Decouping--Definitions
    1. Simplifies the spectra
    2. Improves sensitivity by gathering all the intensity of a multiplet into a singlet
Coupled spin system
Decoupled spin system
Incomplete decoupling
Coupling: a physical interaction between two nuclear spins carried through
the bonding electrons in the molecule
Decoupling: the observed spin-spin splitting to be reduced such a small value
that they are no longer resolved
Notes: Decoupling is used principally as a method of simplification of spectra of heteronuclear species (for example 13C or 15N) by removing the splittings due to coupling to protons.

## Slide 13
Spin Decoupling Theory
A frequency sum rule:
this means that the splittings in the I and S doublets must always remain the same:

## Slide 14
Consequently, decoupling of the S-spin resonance may be
achieved by forcing the two I-spin transitions to process at the same frequency under the influence of the decoupling radiofrequency field.
 0

## Slide 15
The effective decoupling bandwidth, which should be uniformly efficient across the entire range of chemical shifts of the irradiated spins.
Figure of merit:
F: the effective decoupling bandwidth
2. The heating effect generated by the intense radiofrequency field (B2 ) required for broadband decoupling.
Thus always try to obtain satisfactory decoupling at the lowest possible radiofrequency power to cover the entire range of chemical shifts of the irradiated spins
Evaluation of decoupling methods
 = 2F/ B2

## Slide 16
Coherent continuous-wave decoupling
The earliest decoupling experiments achieved this result by irradiation of the I spins with a coherent radiofrequency field B2
The two I-spin transitions process at frequencies determined by B2 and the appropriate resonance offsets:
Provided that the decoupling field B2/2 is strong in comparison with |J/2| and B/2 , the residual splitting is given by
Decoupling methods
Notes: If only one chemical site
needs to be decoupled, the irradiation frequency can be set
at the centre of the I-spin doublet, where DB = 0, so that
f(I1 ) = f(I2 ), and we have perfect decoupling. However, in
the more general case of two or more chemical sites with
appreciably different chemical shifts, this condition cannot
be satisfied for all the sites.

## Slide 17
the residual splitting of the I-spin spectrum increases rapidly as a function of B/2
Coherent decoupling
is extremely sensitive to resonance offset, and is virtually useless when there is an appreciable range of chemical shifts to be covered.
 = 0.2 for 1H-1H
then the ‘effective decoupling bandwidth’ is 4 Hz

## Slide 18
The splitting of the S-spin resonance vanishes because the I spins make rapid (random) transitions between their and  states, thereby ‘washing out’ the spin–spin splitting.
Advantages:
1. It is very simple to set up and operate.
2. It is effective over a band roughly 1 kHz wide.
During a period of 15 years it was the method of choice, proving satisfactory in most practical situations.
It ran into difficulties:
when higher applied fields (B0 ) (and the correspondingly wider chemical shift ranges) became available,
where the sample had a high dielectric loss, aggravating the radiofrequency heating.
Noise decoupling
A dramatic improvement in the effective decoupling bandwidth was achieved by replacing the coherent continuous-wave irradiation with an incoherent source.
 = 0.3
Notes: In There is still no formal theoretical analysis of noise decoupling.
principle this would involve modulation by white noise, but
in practice it was implemented by imposing pseudo-random
phase inversions on the radiofrequency source B2

## Slide 19
  180 pulse
      1. The pulse exchanges I  and  spin states
      2. S is alternatively coupled to I  and  spin state
      3. Effectively averages to decoupling I and S nuclei




S
S
I
I




S
S
I
I
Composite pulse decoupling
180

## Slide 20
  Sequence of 1H 180 pulses
      Each spin precess in the X,Y plane at a rate equal to the sum of its chemical shift and ½ its coupling constants
      Each 180 pulse inverts the evolution of the two spins in the X,Y plane
      Result is the two spins for the coupled doublet process as the same rate of a decoupled singlet
Effectively removes the coupling constant contribution to its rate of processing in the X,Y plane

## Slide 21
These are far less sensitive to resonance offset than simple 180°pulses. Consequently, a given effective bandwidth can be achieved with a far lower pulse intensity.
However,
With such high repetition rates, very small deviations from ideal spin inversion cause appreciable cumulative errors.
A single 180 pulse is sensitive to off-resonance effect, so a composite 180 pulse can be used by one the following types:

## Slide 22
Magic cycles
Assemble the inversion ‘elements’ into a self-compensating ‘magic cycle’
The first such magic cycle was:
where R represents a composite spin inversion pulse and R is its phase-inverted counterpart.
R=(90o)x(270o)y(90o)x
Trajectory of I nuclei after two R MLEV-4 pulses results in an effective 360 pulse. Results is improved slightly by following with two R pulses with reverse phase.

## Slide 23
The remaining tiny imperfections of the MLEV sequence can be further reduced by creating ‘supercycles’, where the residual rotation of one basic cycle is partially compensated by the opposite rotation of the next basic cycle.
and magic supercycles

## Slide 24
WALTZ decoupling
    The basic composite pulse:
    Then
WALTZ-4
WALTZ-8
WALTZ-16

## Slide 25
Supercycles are better than cycles
      Decouples efficiently over 6 kHz
      Corrects imperfections in MLEV

## Slide 26
    Computer optimized using non-90o flip angles
GARP
    Effective decoupling bandwidth of ± 15 kHz

## Slide 27
    WURST:
    1. The effective bandwidth of an adiabatic decoupling sequence is proportional to the square of the applied rf field strength
    2. The performance of a WURST sequence depends on the choice of experimental parameters and can be played to match particular requirements
Adiabatic spin coupling
  500MHz 600MHz 750MHz
  rf power 1.0 1.4 2.3

## Slide 28
Figure of merit  = 2F/ B2 for various broadband decoupling scheme
Sequence 
Coherent continuous-wave 0.0075
Noise decoupling 0.3
MLEV-16 1.5
WALTZ-16 1.8
GARP-16 4.8
WURST 16.7